## Slide 1: An Alternate Methodology for Validating Hardware Write Block Devices
AAFS – 23 February 2012
Ben Livelsberger
NIST
Information Technology Laboratory
CFTT Project

## Slide 2: Disclaimer
Certain trade names and company products are mentioned in the text or identified. In no case does such identification imply recommendation or endorsement by the National Institute of Standards and Technology, nor does it imply that the products are necessarily the best available for the purpose.
Notes: This is our standard disclaimer

## Slide 3: Overview
Federated Testing
Validating Hardware Write Blockers - Usual Method
NIST HWB Test Tools
Interesting Discoveries
Conclusion
Sponsors

## Slide 4: Federated Testing at NIST
NIST is exporting its tool testing expertise and methods
Benefits
  A common test methodology
  Time savings & peer-reviewed test reports
CFTT Strength – Formal, well researched test methods
CFTT Weakness – Limited resources for testing
Notes: Beef up?

## Slide 5: Validating Hardware Write Blockers – Usual Method
Write block drive
Attempt write to drive
Attempt to format drive
Check if drive changed

## Slide 6: Problem - OSes Implement Multiple Write Commands
ATA drives:
  Most OSes default to using READ & WRITE DMA commands
  Some drives < 128 GB: implement WRITE DMA, but not WRITE DMA EXT
  Drives > 128 GB: need EXT command set (WRITE DMA EXT) to fully access drives
  Older drives: only implement PIO (WRITE SECTORS & WRITE SECTORS EXT)
Notes: There are a lot of commands that an OS could use to write to a drive and different drives force different commands to be used. If you’re using the format drive/file copy method, you don’t know which command you’re testing your blocker for when you need to be testing your blocker for all the commands the OS can & will use.

## Slide 7: Possible Write Commands
T10 Technical Committee, http://www.t10.org/ - 20 SCSI write commands
T13 Technical Committee, http://www.t13.org/ - 17 ATA write commands
Wanted a way to test write blockers using all 17 ATA and all 20 SCSI write commands
Notes: It turns out that there are 20 possible SCSI commands and 17 possible ATA commands, that’s a lot of commands

## Slide 8: NIST Approach – ataraw library
ataraw 0.2.1 http://afflib.org/downloads/ataraw-0.2.1.tar.gz
  Kyle Sanders – Masters student at Naval Post Graduate School
  uses the Linux SG_IO ioctl, to pass SCSI/ATA command packets to Linux SCSI Generic driver
Extended ataraw library to implement more ATA and SCSI commands (ATA specs 4-8, SCSI RBC-2)
4 SCSI reads, 4 SCSI writes
12 ATA reads, 15 ATA writes
Notes: We use the ataraw library developed by the Naval Post Graduate school that we extended

## Slide 9: Commands Implemented
Reads Commands (SCSI) | C4h READ MULTIPLE | Write Commands (SCSI) | 3Dh WRITE DMA FUA EXT
08h READ 6 | 22h READ LONG | A0h WRITE 6 | CCh WRITE DMA QUEUED
28h READ 10 | C9h READ DMA w/o retries | 2Ah WRITE 10 | 36h WRITE DMA QUEUED EXT
A8h READ 12 | 23h READ LONG w/o retries | AAh WRITE 12 | C5h WRITE MULTIPLE
88h READ 16 | 21h READ SECTOR(S) w/o retries | 8Ah WRITE 16 | 39h WRITE MULTIPLE EXT
7Fh READ 32 | 25h READ DMA EXT | 7Fh WRITE 32 | CEh WRITE MULTIPLE FUA EXT
 | 26h READ DMA QUEUED EXT |  | 3Ah WRITE STREAM DMA EXT
Reads Commands (ATA) | 29h READ MULTIPLE EXT | Write Commands (ATA) | 3Bh WRITE STREAM EXT
C8h READ DMA | 25h READ SECTOR(S) EXT | 30h WRITE SECTORS | CBh WRITE DMA W/O RETRIES
C7h READ DMA QUEUED | 2Ah READ STREAM EXT | 34h WRITE SECTORS EXT | 31h WRITE SECTORS W/O RETRIES
20h READ SECTOR(S) | 2Ah READ STREAM DMA EXT | CAh WRITE DMA | 3Ch WRITE VERIFY
 |  | 35h WRITE DMA EXT | 
Notes: Here’s the commands that were implemented

## Slide 10: Implementation – try_read, try_write, write_verify
try_write – send every ATA or SCSI write command to unique LBAs (based on the command’s opcode) on drive
try_read – send all the ATA or SCSI read commands to a drive
write_verify – read sectors from a hard drive to measure which, if any, write commands were able to write to the drive
Notes: We implemented 3 programs, one that read, one that write, and one that goes back to check that the writes happened

## Slide 11: Testing a Blocker with the NIST programs
For each hard drive interface supported by the write block (e.g., ATA,SAS,SATA), initialize a drive to known content
Calculate a “before” reference hash for each drive
For each permutation of host-to-blocker and blocker-to-drive interfaces execute the try_read and try_write programs
Calculate an “after” reference hash for each drive
Execute write_verify for each drive. Use the write_verify output along with the reference hashes to measure whether any sectors on the test drives have changed.
Notes: To test a blocker we initialize a drive, try to write to it, and then check to see if anything changed

## Slide 12: Advantages of the NIST Approach
Ability to validate your write block with multiple write commands
Know which commands you’ve validated your blocker for
Know which, if any, commands your blocker fails for
try_write and try_read have been validated for the eSATA, FireWire, and USB interfaces in Ubuntu 11.10
Notes: The main advantage of the NIST approach is we know which commands we’re sending and we know what happens with them.

## Slide 13: Notes of Interest – defense in depth
“/dev/sdd: Read-only file system”
First layer of defense: the firmware logic that blocks writes and passes reads
Second layer: advertising the protected drive as read-only
Modern OSes try to enforce “read-only”; older versions of Linux do not
Notes: Something interesting we found was that some blockers

## Slide 14: Test Results – how good is your write block?
Tested 3 write blockers from 3 leading manufactures using the NIST tools
For one blocker, one sector of our drives kept changing
For the USB interface, the blocker let me write content to the drive using the WRITE 16 command
Reason to fret?
  defense in depth
  All the OSes I’ve tested use the WRITE 10 command
  2008 firmware version; now it’s fixed

## Slide 15: Conclusion
Federated Testing – exporting test materials
The usual method for write blocker testing is incomplete
The NIST hardware write block test tools addresses those problems
Good product design with defense in depth
Important for you to validate your write block devices
Notes: Federated testing will help labs and practitioners share information about tools

## Slide 16: Project Sponsors
National Institute of Justice (Major funding)
Homeland Security (Major funding)
FBI (Additional funding)
Department of Defense, DCCI (Equipment and support)
Federal, State & Local agencies (Technical input)
NIST/OLES (Program management)

## Slide 17: Contacts
Ben Livelsberger www.cftt.nist.gov
livebe01@nist.gov cftt@nist.gov
Sue Ballou, Office of Law Enforcement Standards
susan.ballou@nist.gov
NIST tools, http://www.cftt.nist.gov/###.tar.gz

## Slide 18: Questions?