Appendix C

Proposed Revisions to NCWM Publication 14, Policy C, Product Families for Meters –

By Henry Oppermann and Mike Keilty Following October 2009 Sector Meeting

C.	Product Families for Meters

When submitting a meter for evaluation, the manufacturer must specify the product family and critical parameters for which the meter is being submitted.

The product family and the specific product subgroup covered by the Certificate are to be identified on Page 1 of the Certificate of Conformance.  More detailed information, including the typical product types found in the subgroup, is to be included in the application section of the Certificate.

| Mass Meter Product Category & Test Requirements | Magnetic Flow Meter Product Category & Test Requirements | Positive Displacement Flow Meter Product Category & Test Requirements | Turbine Flow Meter Product Category & Test Requirements |
| --- | --- | --- | --- |
| Test B: To cover a range of the following products, test with one product having a low specific gravity and test with a second product having a high specific gravity. The Certificate of Conformance will cover all products in all product categories listed in the table within the specific gravity range tested. | Test F – To cover a range of the following products, test with one product having a specified conductivity. The Certificate of Conformance will cover all products in both of the families with conductivity equal to or above the conductivity of the tested liquid. | Test C - To cover a range of products within each product category, test with one product having a low viscosity and test with a second product having a high viscosity within each category. The Certificate of Conformance will cover all products in the product category within the viscosity range tested. | Test E – To cover a range of products within each product category, test with one product having a low kinematic viscosity and test with a second product having a high kinematic viscosity within each category. The Certificate of Conformance will cover all products in the product category within the kinematic viscosity range tested. |
| Typical Products | Specific Gravity* (60 °F) | Product Category | Typical Products | Product Category | Product Category: Fuels, Lubricants, Industrial and Food Grade Liquid Oils (FL&O) | Product Category: Fuels, Lubricants, Industrial and Food Grade Liquid Oils (FL&O) |
| Asphalt |  | FL&O | Gasoline | FL&O | Typical Products | Reference Viscosity* (60 F) | Typical Products | Reference Viscosity* (60 °F) |
| Asphalt |  | Heated | JP4 | FL&O |  | Centipoise (cP) |  | Centipoise (cP) |
| Avgas |  | FL&O | Jet A-1 | FL&O | Gasoline | 0.28 | Gasoline | 0.28 |
| Jet A |  | FL&O | JP7 & JP8 | FL&O | JP4 | 1.02 | JP4 | 1.02 |
| Jet B |  | FL&O | Kerosene | FL&O | Jet A-1 | 1.36 | Jet A-1 | 1.36 |
| Spindle Oil |  | FL&O | JP5 | FL&O | JP7 & JP8 | 1.82 | JP7 & JP8 | 1.82 |
| Adjuvants | 0.7 to 1.2 | CC | Corn Oil | FL&O | Kerosene | 1.94 | Kerosene | 1.94 |
| Banvel | 0.7 to 1.2 | CC | Cooking Oils | FL&O | JP5 | 1.94 | JP5 | 1.94 |
| Fumigants | 0.7 to 1.2 | CC | Diesel Fuel | FL&O | Corn Oil | 4 | Corn Oil | 4 |
| Fungicides | 0.7 to 1.2 | CC | Biodiesel above B20 | FL&O | Cooking Oils | 9.93 | Cooking Oils | 9.93 |
| Herbicides | 0.7 to 1.2 | CC | Light Oil | FL&O | Diesel Fuel | 10 | Diesel Fuel | 10 |
| Insecticides | 0.7 to 1.2 | CC | Sunflower Oil | FL&O | Biodiesel above B20 | 10.12 | Biodiesel above B20 | 10.12 |
| Paraquat | 0.7 to 1.2 | CC | Soy Oil | FL&O | Light Oil | 13.47 | Light Oil | 13.47 |
| Prowl | 0.7 to 1.2 | CC | Olive Oil | FL&O | Sunflower Oil | 90.1 | Sunflower Oil | 90.1 |
| Round-up | 0.7 to 1.2 | CC | Vegetable Oil | FL&O | Soy Oil | 90.6 | Soy Oil | 90.6 |
| Touchdown | 0.7 to 1.2 | CC | Bunker Oil | FL&O | Olive Oil | 116.8 | Olive Oil | 116.8 |
| Treflan | 0.7 to 1.2 | CC | Avgas | FL&O | Vegetable Oil | 133 | Vegetable Oil | 133 |
| Ammonia Nitrate | 1.16 to 1.37 | Fert | Jet A | FL&O | Bunker Oil | 11,200 | Bunker Oil | 11,200 |
| Crude Oil | 0.79 to 0.97 | FL&O | Jet B | FL&O | Avgas | 1.5 to 6 | Avgas | 1.5 to 6 |
| Lubricating Oils | 0.80 to 0.90 | FL&O | Asphalt | FL&O | Jet A | 1.5 to 6 | Jet A | 1.5 to 6 |
| Peanut Oil | 0.9 to 1.0 | FL&O | Peanut Oil | FL&O | Jet B | 1.5 to 6 | Jet B | 1.5 to 6 |
| Hexane | 0.66 | Sol Gen | SAE Grades | FL&O | Asphalt | 100 to 5000 | Asphalt | 100 to 5000 |
| Diesel Fuel | 0.72 | FL&O | Lubricating Oils | FL&O | Peanut Oil | 11 to 110 | Peanut Oil | 11 to 110 |
| Gasoline | 0.72 | FL&O | Crude Oil | FL&O | SAE Grades | 192 to 3626 | SAE Grades | 192 to 3626 |
| Kerosene | 0.75 | FL&O | 6 Oil (#5, #6) | FL&O | Lubricating Oils | 20 to 1000 | Lubricating Oils | 20 to 1000 |
| Jet A-1 | 0.76 | FL&O | Fuel Oil (#1, #2, #3, #4) | FL&O | Crude Oil | 3 to 1783 | Crude Oil | 3 to 1783 |
| JP4 | 0.76 | FL&O | Spindle Oil | FL&O | 6 Oil (#5, #6) | 66 to 13,000 | 6 Oil (#5, #6) | 66 to 13,000 |
| JP5 | 0.76 | FL&O | Acetone | Sol Gen | Fuel Oil (#1, #2, #3, #4) | 8 to 88 | Fuel Oil (#1, #2, #3, #4) | 8 to 88 |
| JP7 JP8 | 0.76 | FL&O | Hexane | Sol Gen | Spindle Oil |  | Spindle Oil |  |
| Ethanol | 0.79 | Alc Gly | Acetates | Sol Gen | Product Category: Solvents General (Sol Gen) | Product Category: Solvents General (Sol Gen) |
| Isopropyl | 0.79 | Alc Gly | MEK | Sol Gen | Typical Products | Reference Viscosity* (60 °F) | Typical Products | Reference Viscosity* (60 °F) |
| Acetone | 0.8 | Sol Gen | Toluene | Sol Gen |  | Centipoise (cP) |  | Centipoise (cP) |
| Methanol | 0.80 | Alc Gly | Xylene | Sol Gen | Acetone | 0.34 | Acetone | 0.34 |
| Butanol | 0.81 | Alc Gly | Ethylacetate | Sol Gen | Hexane | 0.34 | Hexane | 0.34 |
| Isobutyl | 0.81 | Alc Gly | Methylene-Chloride | Sol Chl | Acetates | 0.44 | Acetates | 0.44 |
| MEK | 0.81 | Sol Gen | Trichloro-Ethylene | Sol Chl | MEK | 0.45 | MEK | 0.45 |
| Biodiesel above B20 | 0.86 | FL&O | Carbon Tetra-Chloride | Sol Chl | Toluene | 0.62 | Toluene | 0.62 |
| Light Oil | 0.86 | FL&O | Perchloro-Ethylene | Sol Chl | Xylene | 0.86 | Xylene | 0.86 |
| Toluene | 0.87 | Sol Gen | Methanol | Alc Gly | Ethylacetate | 1.36 | Ethylacetate | 1.36 |
| 20 % Aqua-Ammonia | 0.89 | Fert | Ethanol | Alc Gly | Product Category: Solvents Chlorinated (Sol Chl) | Product Category: Alcohols, Glycols & Water Mixes Thereof (Alc Gly) |
| Xylene | 0.89 | Sol Gen | Isopropyl | Alc Gly | Typical Products | Reference Viscosity* (60 F) | Typical Products | Reference Viscosity* (60 F) |
| 6 Oil (#5, #6) | 0.9 | FL&O | Butanol | Alc Gly |  | Centipoise (cP) |  | Centipoise (cP) |
| Fuel Oil (#1, #2, #3, #4) | 0.9 | FL&O | Isobutyl | Alc Gly | Methylene-Chloride | 0.46 | Methanol | 0.64 |
| SAE Grades | 0.9 | FL&O | Ethylene glycol | Alc Gly | Trichloro-Ethylene | 0.6 | Ethanol | 1.29 |
| Corn Oil | 0.91 | FL&O | Propylene glycol | Alc Gly | Carbon Tetra-Chloride | 0.99 | Isopropyl | 2.78 |
| Cooking Oils | 0.92 | FL&O | Demineralized | Water | Perchloro-Ethylene | 1 | Butanol | 3.34 |
| Olive Oil | 0.92 | FL&O | Deionized | Water | Product Category: Alcohols, Glycols & Water Mixes Thereof (Alc Gly) | Isobutyl | 4.54 |
| Vegetable Oil | 0.92 | FL&O | Asphalt | Heated | Typical Products | Reference Viscosity* (60 °F) | Ethylene glycol | 25.5 |
| Acetates | 0.93 | Sol Gen | Bunker C | Heated |  | Centipoise (cP) | Propylene glycol | 54 |
| Soy Oil | 0.93 | FL&O | Test D – To obtain coverage for a product category: Test with one product in the product category. The Certificate of Conformance will cover all products in the category. | Methanol | 0.64 | Compressed liquids: Fuels and Refrigerants, NH3 |
|  |  |  |  |  |  | Typical Products | Reference Viscosity* (60 °F) Centipoise (cP) |
| Sunflower Oil | 0.93 | FL&O |  | Ethanol | 1.29 | Propane | 0.098 |
|  |  |  |  |  |  | Anhydrous Ammonia | 0.188 |
| Ethylacetate | 0.96 | Sol Gen |  | Isopropyl | 2.78 | Butane | 0.19 |
| Bunker Oil | 0.99 | FL&O |  | Butanol | 3.34 | Freon 11 | 0.313 |
| Beverages | 1.0 | Water | Tap water | Water | Isobutyl | 4.54 | Freon 12 | 0.359 |
| Deionized | 1.0 | Water | Potable | Water | Ethylene glycol | 25.5 | Freon 22 | 1.99 |
| Demineralized | 1.0 | Water | Nonpotable | Water | Propylene glycol | 54 | Ethane |  |
| Juices | 1.0 | Water | Juices | Water | Product Category: Clear Liquid Fertilizers (Liq Fert) | Test A – The following products must be individually tested and noted on the Certificate of Conformance. |
| Milk | 1.0 | Water | Beverages | Water | Typical Products | Reference Viscosity* (60 °F) |  |
| Nonpotable | 1.0 | Water | Water mixes of alcohols & glycols | Alc Gly |  | Centipoise (cP) | Typical Products | Product Category |
| Potable | 1.0 | Water | Urea | Fert | Urea | 1 | Methylene-Chloride | Sol Chl |
| Tap Water | 1.0 | Water | Ammonia Nitrate | Fert | Ammonia Nitrate | 11.22 | Trichloro-Ethylene | Sol Chl |
| Propylene glycol | 1.04 | Alc Gly | 10-34-0 | Fert | 10-34-0 | 48 | Carbon Tetra-Chloride | Sol Chl |
| Hydrochloric Acid | 1.1 | Chem | 20 % Aqua-Ammonia | Fert | 20 % Aqua-Ammonia | 1.1 to 1.3 | Perchloro-Ethylene | Sol Chl |
| Ethylene glycol | 1.19 | Alc Gly | Chlear Liquid Fert | Fert | Chlear Liquid Fert | 31 to 110 | Urea | Liq Fert |
| Liquid Molasses | 1.25 | Liq Feed | Nitrogen Solution | Fert | Nitrogen Solution | 31 to 110 | Ammonia Nitrate | Liq Fert |
| 9-18-9 | 1.32 | Fert | 28 %, 30 % or 32 % | Fert | 28 %, 30 % or 32 % | 31 to 110 | 10-34-0 | Liq Fert |
| Methylene-Chloride | 1.34 | Sol Chl | N-P-K solutions | Fert | N-P-K solutions |  | 20% Aqua-Ammonia | Liq Fert |
| 10-34-0 | 1.39 | Fert | 9-18-0 | Fert | 9-18-0 |  | Chlear Liquid Fert | Liq Fert |
| Trichloro-Ethylene | 1.47 | Sol Chl | 4-4-27 | Sus Fert | Product Category: Suspension Fertilizers (Sus Fert) | Nitrogen Solution | Liq Fert |
| Carbon Tetra-Chloride | 1.6 | Sol Chl | 3-10-30 | Sus Fert | Typical Products | Reference Viscosity* (60 °F) | 28 %, 30 % or 32 % | Liq Fert |
| Perchloro-Ethylene | 1.6 | Sol Chl | Molasses plus Phos Acid and/or Urea (TreaChle) | Liq Feed |  | Centipoise (cP) | N-P-K solutions | Liq Fert |
| Sulfuric Acid | 1.83 | Chem | Liquid Molasses | Liq Feed | 4-4-27 | 20 to 215 | 9-18-0 | Liq Fert |
| Phosphoric Acid | 1.87 | Chem | Sulfuric Acid | Chem | 3-10-30 | 100 to 1000 | 4-4-27 | Sus Fert |
| Urea | 1.89 | Fert | Phosphoric Acid | Chem | Product Category: Liquid Feeds (Liq Feed) | 3-10-30 | Sus Fert |
| Bunker C | 1.99 | Heated | Hydrochloric Acid | Chem | Typical Products | Reference Viscosity* (60 °F) | Molasses plus Phos Acid and/or Urea (TreaChle) | Liq Feed |
| Fungicides | 1 to 1.2 | CC | Herbicides | CC-A |  | Centipoise (cP) | Liquid Molasses | Liq Feed |
| Micronutrients | 1 to 1.2 | CC | Round-up | CC-A | Molasses plus Phos Acid and/or Urea (TreaChle) | 2882 | Asphalt | Heated |
| Molasses plus Phos Acid and/or Urea (TreaChle) | 1.1 to 1.3 | Liq Feed | Touchdown | CC-A | Liquid Molasses | 8640 | Bunker C | Heated |
| 3-10-30 | 0.9 to 1.65 | Liq Fert | Banvel | CC-A | Product Category: Heated Products (Heated) | Sulfuric Acid | Chem |
| 4-4-27 | 0.9 to 1.65 | Liq Fert | Treflan | CC-A | Typical Products | Reference Viscosity* (60 °F) | Phosphoric Acid | Chem |
| Micronutrients | 0.9 to 1.65 | Liq Fert | Paraquat | CC-A |  | Centipoise (cP) | Hydrochloric Acid | Chem |
| 28%, 30% or 32% | 1.28 to 1.32 | Fert | Prowl | CC-A | Asphalt | 100 to 5000 | Herbicides | CC-A |
| N-P-K solutions | 1.2 – 1.4 | Fert | Herbicides | CC-A | Bunker C | 11,200 | Round-up | CC-A |
| Chlear Liquid Fert | 1.17 to 1.44 | Fert | Fungicides | CC-B | Product Category: Chemicals (Chem) | Touchdown | CC-A |
| Nitrogen Solution | 1.17 to 1.44 | Fert | Insecticides | CC-B | Typical Products | Reference Viscosity* (60 °F) | Treflan | CC-A |
| Test D – To obtain coverage for each of the following product categories, test with one product in each product category. The Certificate of Conformance will cover all of the products in the product category in which a product was tested. | Adjuvants | CC-B |  |  | Banvel | CC-A |
|  | Fumigants | CC-B | Sulfuric Acid | 1.49 | Paraquat | CC-A |
|  | Fungicides | CC-C | Phosphoric Acid | 161 | Prowl | CC-A |
| Product Category | Typical Products | Specific Gravity* (60 F) | Micronutrients | CC-D | Hydrochloric Acid | 0.80 to 1. 0 | Herbicides | CC-A |
| Comp gas | Compressed Natural Gas (CNG) | 0.6 to 0.8 (1=Air) |  |  | Product Category: Crop Chemicals (Type A) (CC-A) | Fungicides | CC-B |
|  |  |  |  |  | Typical Products | Reference Viscosity* (60 °F) | Insecticides | CC-B |
| Comp liq | Anhydrous Ammonia | 0.61 |  |  |  | Centipoise (cP) | Adjuvants | CC-B |
| Comp liq | Butane | 0.595 |  |  | Herbicides | 4 to 400 | Fumigants | CC-B |
| Comp liq | Ethane |  |  |  | Round-up | 4 to 400 | Fungicides | CC-C |
| Comp liq | Freon 11 | 1.49 |  |  | Touchdown | 4 to 400 | Micronutrients | CC-D |
| Comp liq | Freon 12 | 1.33 |  |  | Banvel | 4 to 400 | Dual | Flow |
| Comp liq | Freon 22 | 1.37 |  |  | Treflan | 4 to 400 | Bicep | Flow |
|  |  |  |  |  | Paraquat | 4 to 400 | Marksman | Flow |
| Comp liq | Propane | 0.504 |  |  | Prowl | 4 to 400 | Broadstrike | Flow |
|  |  |  |  |  | Product Category: Crop Chemicals (Type B) (CC-B) | Doubleplay | Flow |
| Cryo LNG | Liquefied Natural Gas |  |  |  | Typical Products | Reference Viscosity* (60 °F) | Topnotch | Flow |
| Cryo LNG | Liquefied Oxygen | 0.66 |  |  |  | Centipoise (cP) | Guardsman | Flow |
| Cryo LNG | Nitrogen | 0.31 |  |  | Fungicides | 0.7 to 100 | Harness | Flow |
|  |  |  |  |  | Insecticides | 0.7 to 100 | NH3 |  |
|  |  |  |  |  | Adjuvants | 0.7 to 100 | Test D – To obtain coverage for a product category: Test with one product in the product category. The Certificate of Conformance will cover all products in the category. |
|  |  |  |  |  | Fumigants | 0.7 to 100 |  |
|  |  |  |  |  | Product Category: Crop Chemicals (Type C) (CC-C) |  |
|  |  |  |  |  | Typical Products | Reference Viscosity* (60 °F) | Tap Water | Water |
|  |  |  |  |  |  | Centipoise (cP) | Deionized | Water |
|  |  |  |  |  | Fungicides | 20 to 900 | Demineralized | Water |
|  |  |  |  |  | Product Category: Crop Chemicals (Type D) (CC-D) | Potable | Water |
|  |  |  |  |  | Typical Products | Reference Viscosity* (60 °F) | Nonpotable | Water |
|  |  |  |  |  |  | Centipoise (cP) | Juices | Water |
|  |  |  |  |  | Micronutrients | 20 to 1000 | Beverages | Water |
|  |  |  |  |  | Product Category: Flowables (Flow) | Milk | Water |
|  |  |  |  |  | Typical Products | Reference Viscosity* (60 °F) | Liquefied Oxygen | Cryo LNG |
|  |  |  |  |  |  | Centipoise (cP) | Nitrogen | Cryo LNG |
|  |  |  |  |  | Dual | 20 to 900 | Liquefied Natural Gas | Cryo LNG |
|  |  |  |  |  | Bicep | 20 to 900 |  |  |
|  |  |  |  |  | Marksman | 20 to 900 |  |  |
|  |  |  |  |  | Broadstrike | 20 to 900 |  |  |
|  |  |  |  |  | Doubleplay | 20 to 900 |  |  |
|  |  |  |  |  | Topnotch | 20 to 900 |  |  |
|  |  |  |  |  | Guardsman | 20 to 900 |  |  |
|  |  |  |  |  | Harness | 20 to 900 |  |  |
|  |  |  |  |  | Product Category: Compressed Liquids: Fuels and Refrigerants (Comp liq) |  |  |
|  |  |  |  |  | Typical Products | Reference Viscosity* (60 °F) |  |  |
|  |  |  |  |  |  | Centipoise (cP) |  |  |
|  |  |  |  |  | Propane | 0.098 |  |  |
|  |  |  |  |  | Anhydrous Ammonia | 0.188 |  |  |
|  |  |  |  |  | Butane | 0.19 |  |  |
|  |  |  |  |  | Freon 11 | 0.313 |  |  |
|  |  |  |  |  | Freon 12 | 0.359 |  |  |
|  |  |  |  |  | Freon 22 | 1.99 |  |  |
|  |  |  |  |  | Ethane |  |  |  |
|  |  |  |  |  | Test D – To obtain coverage for a product category: Test with one product in the product category. The Certificate of Conformance will cover all products in the category. |  |  |
|  |  |  |  |  | Product Category: All Water (Water) |  |  |
|  |  |  |  |  | Typical Products | Reference Viscosity* (60 °F) |  |  |
|  |  |  |  |  |  | Centipoise (cP) |  |  |
|  |  |  |  |  | Tap Water | 1.0 |  |  |
|  |  |  |  |  | Deionized | 1.0 |  |  |
|  |  |  |  |  | Demineralized | 1.0 |  |  |
|  |  |  |  |  | Potable | 1.0 |  |  |
|  |  |  |  |  | Nonpotable | 1.0 |  |  |
|  |  |  |  |  | Juices | 1.0 |  |  |
|  |  |  |  |  | Beverages | 1.0 |  |  |
|  |  |  |  |  | Milk | 1.0 |  |  |
|  |  |  |  |  | Test A – The following products must be individually tested and noted on the Certificate of Conformance. |  |  |
|  |  |  |  |  | Product Category: Cryogenic Liquids and Liquefied Natural Gas (Cryo LNG) |  |  |
|  |  |  |  |  | Typical Products | Reference Viscosity* (60 °F) |  |  |
|  |  |  |  |  |  | Centipoise (cP) |  |  |
|  |  |  |  |  | Liquefied Oxygen | 0.038 |  |  |
|  |  |  |  |  | Nitrogen | 1.07 |  |  |
|  |  |  |  |  | Liquefied Natural Gas |  |  |  |

| Product Family Table – Category Abbreviations |
| --- |
| Abbreviation | Product Categories |
| FL&O | Fuels, Lubricants, Industrial and Food Grade Liquid Oils |
| Solv Gen | Solvents General |
| Solv Cl | Solvents Chlorinated |
| Alc Gly | Alcohols, Glycols & Water Mixes thereof |
| Water | Water |
| Fert | Fertilizers |
| CC-A | Crop Chemicals (Type A) |
| CC-B | Crop Chemicals (Type B) |
| CC-C | Crop Chemicals (Type C) |
| CC-D | Crop Chemicals (Type D) |
| Flow | Flowables |
| Sus Fert | Suspension Fertilizers |
| Liq Feed | Liquid Feeds |
| Chem | Chemicals |
| Heated | Heated Products |
| Comp liq | Compressed Liquids: Fuels and Refrigerants NH3 |
| Comp gas | Compressed Gases |
| Cryo LNG | Cryogenic Liquids and Liquefied Natural Gas |

1Note:  The Typical Products listed in this table are not limiting or all-inclusive; there may be other products and product trade names, which fall into a product family.  Water and a product such as stoddard solvent or mineral spirits may be used as test products in the fuels, lubricants, industrial, and food- grade liquid oils product family.

2 The specific gravity of a liquid is the ratio of its density to that of water at standard conditions, usually 4 °C (or 40 °F) and 1 atm.  The density of water at standard conditions is approximately 1000 kg/m3 (or 998 kg/m3)

3 Diesel fuel blends (biodiesel) with up to 20 % vegetable or animal fat/oil.

4 Gasoline includes oxygenated fuel blends with up to 15 % oxygenate.

Centipoise

Centistokes   =   ---------------------

Specific Gravity

5 Kinematic viscosity is measured in centistokes.

Source for some of the viscosity value information is in the Industry Canada - Measurement Canada “Liquid Products Group, Bulletin V-16-E (rev. 1), August 3, 1999.”

THIS PAGE INTENTIONALLY LEFT BLANK