# Section 4.46.  Berry Baskets and Boxes

## A.  Application

A.1. - This code applies to baskets and boxes for berries and small fruits in capacities of 1 dry quart and less.

A.2. - See also Sec. 1.10; General Code requirements.

## S.  Specifications

S.1.  Units. - The capacity of a berry basket or box shall be ½ dry pint, 1 dry pint, or 1 dry quart.

S.2.  Materials. - A berry basket or box shall be made of any suitable materials that will retain its shape during normal filling, storage, and handling.

S.3.  Capacity Point. - The capacity of a berry basket or box shall be determined by its top edges.

## N.  Notes

N.1.  Method of Test. - A berry basket or box may be tested either volumetrically, using rape seed as the testing medium, or geometrically through accurate inside dimension measurement and calculation.

## T.  Tolerances

T.1.  Tolerances on Individual Measures. - Maintenance and acceptance tolerances in excess and deficiency on an individual measure shall be as shown in Table 1.

T.2.  Tolerances on Average Capacity. - The average capacity on a random sample of 10 measures selected from a lot of 25 or more shall be equal to or greater than the nominal capacity.

(Amended 1979)

| Table 1. Maintenance and Acceptance Tolerances in Excess and in Deficiency |
| --- |
| Nominal Capacity | Tolerance |
|  | In Excess cubic inches | In Deficiency cubic inches |
| ½ pint | 1 | 0.5 |
| 1 pint | 2 | 1.0 |
| 1 quart | 3 | 1.5 |

THIS PAGE LEFT INTENTIONALLY BLANK.