## Slide 1: Measurement Assurance Concepts for Flow Cytometry
John T. Elliott Jr., Cell Systems Science Group Leader
National Institute of Standards and Technology (NIST), Department of Commerce, Gaithersburg, MD 20899
NIST-FDA Flow Cytometry Workshop, 2017

## Slide 2: What is Measurement Science?
A systematic approach that informs on the comparability and trust in a measurement result
  Data-based decision making
Components of a measurement:
  Value- it is on a scale; enables compared to other measurements
  Uncertainty- variability in the measurement; enables statistics
  Evidence- evaluation of the measurement system; confidence
1
2
Controls meet specification

## Slide 3: What is Measurement Science?
Treat the assay as a measurement process
Process controls provide evidence that the measurement process is proceeding as expected
Adapt the process quality tools to cell assays
  Cause and effect diagram
  “In-line” and “one-off” process controls
  Control charting
  Sensitivity analysis
  Experimental design
  Interlaboratory testing
  Acceptance specifications

## Slide 4
Generalized Flow Chart of the Measurement Process for a Cell Assay
Generated from NIST Measurement Assurance Workshop 2015
Collection/ storage/ transportation
Sample Preparation
Sampling
Measurement/Data collection
Reporting
Data Analysis
Process Controls
Upstream Considerations for Assay Development
Intended Use
Material Choice (Population Definition)
Choice of Instrument (IQ/OQ/PQ)
Instrument set-up/ validation
Control of Raw & Consumable
http://www.nist.gov/mml/bbd/biomaterials/measurement-assurance-for-cell-therapy-products.cfm
Metric and specification development

## Slide 5: Cause and Effect Diagram
Instrumentation
Treatment
Staining
Cell Maintenance
Harvesting
Variability in extracted values
Variability in fluorescence measurement
Cell ID
cell count/
passage
Incubator
Reagent
quality
trypsinization
Phenotype drift
dissolution
vehicle
Counting/
seeding
Pipetting/
resuspension
Pipetting/
resuspension
Treatment
time
trypsinization
agglomeration
Cell
debris
pipetting
Reagent
quality
Stain
concentration
Stain
time
mixing
dissolution
PMT voltage
Laser power
Linear range
Flow rate
filters
Sensitivity/
saturation
Non-laminar
Sheath
debris
Classifiers/gates
Fluorescence measurement
Data Analysis
Volume
Counting beads
Antibody quality

## Slide 6: Do we have the appropriate process controls?
Cell staining/sampling
Flow cytometer experiment
Generate test result
Treatment
Cell preparation/harvest
Cell Maintenance
Doubling time
Seeding density
Cell counting/viability
Cell morph/volume
Drug stock absorbance
Solvent control
replicates
Cell agglomeration fraction
Cell debris detection
Cell count
Stain stock character
Solvent control
Replicates
Cell debris detection
Linearity/sensitivity/saturation
Reference materials
Benchmark
Stain intensity
Scattering/debris
Control experiment for setting gates
Possible process controls to provide evidence of step completion

## Slide 7: Charting Process Control Data and Specifications
By charting process control results, begin to establish specifications for the process
Meeting a process control specifications indicates a measurement process worked
Process controls results in evidence for measurement assurance
linearity
Linearity: Expected Range
21.75-23.75

## Slide 8: What does confidence look like?
Evidence for confidence:
Benchmark reference materials
Assigned ERF beads
Instrument performance in spec
Cell count/mL< 20000
Aggregate/doublets <10%
Cell debris <10%
Scattering in spec
Antibody staining in specification
Compensation collected and in spec
Test result
Clumps/debris/count not affecting measurement
Fit for purpose
Fit for purpose
In-line measurements
One-off process control
FSC
SSC
FL3-DRAQ5
FL1-GFP
Calibrations/Instrument
All channels benchmarked/calibrated
Fluorescent events in linear range
Instrument OK

## Slide 9: Focus of this workshop
Discussion 1 (11:20 am-12:00 pm)- Reference materials and standardizing fluorescence measurements: What and how do you do it.
Discussion 2 (3:00 pm-4:30 pm)- Best practices and other ways to provide measurement assurance: controls, samples, reagents, gating, new methods, moving forward

## Slide 10: Developing a Flow Cytometry Standard
Measurement assurance strategies provides a framework for developing a documentary “how-to” standard for flow cytometry
Standard would be independent of instrument, software and reagent vendor, but would enable development of test method that is fit-for-purpose
Consensus and leveraging existing best practices will be critical for standard development