## Slide 1: Procedural Model Generators for RSoXS Simulation Suite
By Aaron Tian
Mentored by Dr. Peter Beaucage

## Slide 2: Resonant Soft X Ray Scattering
Small angle scattering technique
  Similar to SAXS and SANS
Capable of determining orientation at nanoscale
  Establish processing structure performance correlation
Cy-RSoXS Scattering Simulator
  Voxel based forward scattering simulator
  Analyze simulated scattering patterns

## Slide 3: Simulation Suite and Programmatic Model Generation
Cy-RSoXS Scattering simulator
  Many parameters means much data
Lack of abstraction
  Must hard code each individual step in generating morphology
  Voxel Placement
  Voxel Alignment
  Shape tiling
  File serialization

## Slide 4: Goals
Build software library to abstract morphology creation process
  Individual morphology shape generation
  Choosing points within space
  Placing morphologies at those points
  Serializing morphology to disk for simulation
Easy to use and maintain
  Add extra point generation algorithms
  Add extra preset morphologies to tile
  Still provide option to create your own morphology

## Slide 5: Morphology Structure
Shape Object
Euler
  Volume Fraction (Vfrac)
  Alignment Magnitude (S)
  Theta
  Psi
Euler object for each material in the shape

## Slide 6: Individual Morphology Generation
Create Volume Array
Create Alignment Array
Calculate Angles
  Theta: Inverse tangent y / x
  Psi: Inverse tangent r / z
Apply rotation
  Non-isotropic only

## Slide 7: Default Shapes
Sphere
Core-Shell
  Same or different material
Ellipsoid
Random generation
  Create n shapes with randomized parameters

## Slide 8: Point Generation
Poisson Disk Sampling
  Random points but at least X distance away from all others
Uniform Grid
  Point placed every X distance
Random Offset Grid
  Uniform but with random offsets

## Slide 9: Morphology Tiling
Copy individual morphologies at points
On Collide
  Overwrite
  Skip

## Slide 10: Collision Checking
Point generation and shapes know nothing about each other
Accelerated Spatial Partition
Bucket / Chunking System
  Create arbitrarily sized buckets
  Check which buckets bounding box is in
  Perform axis aligned cube overlap with other shapes in the buckets

## Slide 11: HDF5 Serialization
Provide file name, shape object, physical size
  Everything is automatically created
  Other optional parameters

## Slide 12: Example Use Case
CyRoXS 1.1 Tutorial
  Core Shell Morphology
  Random points
80% less code
  Original: Over 40 lines
  Library: 7 lines

## Slide 13: Simulation Scattering Patterns (1 NM)

## Slide 14: Vertical Projection Data

## Slide 15: Anisotropy

## Slide 16: Horizontal and Vertical

## Slide 17: Possible Future Steps
More preset shapes
  More non-isotropic morphologies
More point algorithms
  Random sequential
  Volume in space
More robust collision detection system
  Octree

## Slide 18: Acknowledgements
Dr. Peter Beaucage
Dr. Peter Dudenas
Dr. Dean DeLongchamp
CHRNS / NCNR
Internship directors Julie Borchers and Joe Dura

## Slide 19: Questions?