## Slide 1: AISC CIS/2 Workshop #I
Item 2.3
“Description of Conformance Classes”
Irvine, CA: February 1999 (1.4)

## Slide 2: Objective
To explain the concept of Conformance Classes as used in CIS/2

## Slide 3: Context: Item 2.3
Study
Implement
Map Data
Scope

## Slide 4: Basic Concepts

## Slide 5: Conformance Class
Term borrowed from ISO10303 (STEP)
A logical subset of the LPM
  for specifying translator scope
  for testing translator compliance
Hard boundaries
  all entities within must be supported in full!

## Slide 6: Conformance Class
Pre-defined in the CIS/2 documentation
  scope of each CC is derived logically from the EXPRESS schema
Large number of defined CCs
  and they can be used in combination!
  which CCs to use?

## Slide 7: Base Conformance Class
545 BASE-CCs defined in documentation
  each “based” on a different entity
  other “included” entities are listed
As defined, each BASE-CCs is either Complete or Incomplete
  must be “completed” prior to use!

## Slide 8: Completing CCs
BASE-CC
Complete
Incomplete
Completed_by

## Slide 9: Completing CCs
BASE-CC
Complete
Incomplete
Completed_by

## Slide 10: CC Combinations
Combination
Comprise
Entities
BASE-CC
Comprise
Completed
Comprise
CC123
CC123 + CC127
CC53 + CC123 + CC127
name

## Slide 11: CC Combinations
Assemble as needed from completed BASE-CCs
Define by a list of BASE-CC numbers
  same entity can be repeatedly included at multiple levels (Venn diagram nesting)
Huge number of possible combinations!

## Slide 12: Why so complex?

## Slide 13: Valid Subsets
A completed CC simply defines a subset of the LPM that is logically valid to instantiate
  subset need not be useful
  subset need not be (that) meaningful
LPM/5 is large and complex
  many valid subsets are possible!

## Slide 14: Hard Boundaries
The overall scope of a particular translator corresponds to a particular CC combination
  correctly translate all data within that valid subset
    every entity, and
    every attribute (see Part 13)
  may translator provide user control for exporting or importing lesser valid scopes
Care when scoping a translator!

## Slide 15: Export Translator
Full information scope of the application
Full CC scope of export translator
Lesser valid subsets

## Slide 16: Export Scope: Full Data
Application fully populated with data
Export full CC scope of the translator
  CIS data will also satisfy any subset CCs
Where the translator provides for it, export a lesser valid subset
  CIS data will also satisfy any subset CCs

## Slide 17: Export Translator
Full information scope of the application
Full CC scope of export translator
Part populated information scope
Lesser valid subsets

## Slide 18: Export Scope: Partial Data
Application only partly populated with data
Export full CC scope of the translator
  will the mapping logic still work correctly?
  subset CCs may be fully populated with CIS data
Where the translator provides for it, export a lesser but fully populated valid subset

## Slide 19: Import Translator
Full information scope of the application
Full CC scope of import translator

## Slide 20: Import Translator
Full information scope of the application
Full CC scope of import translator
Greater valid subsets

## Slide 21: Import Scope: Full Data
(Importing application not populated with data)
CIS data full populates CC scope of import translator
  CIS data may exceed CC scope of translator!
1/2

## Slide 22: Import Translator
Full information scope of the application
Full CC scope of import translator
Populated valid subset

## Slide 23: Import Scope: Partial Data
(Importing application not populated with data)
Import full CC scope of translator
  will the mapping logic work correctly?
  Ideally mapping logic able to import, in isolation, each “within-scope” completed BASE-CC!
Where the translator provides for it, import a lesser (but fully populated) valid subset

## Slide 24: Export and Import
Export
  Full CC scope of translator
  Lesser valid subset (requested and/or partial data)
Import
  Full CC scope of translator
    Excess data CIS data ignored
  Lesser valid subset (requested and/or partial data)
    application must be able to store and manipulate any such subset!

## Slide 25: Import Translator
Full information scope of application
Full CC scope of import translator
Lesser valid subsets
Populated valid subset

## Slide 26: CIS/2 (AISC Beta) Documenation

## Slide 27: Part 12a Conformance Classes
Introduction
Explains Base Conformance Classes
  How to use Definition Table in Part 12b
  Combination Rules
Appendix A
  background use of CCs in CIS/2

## Slide 28: Part 12b Base Conformance Classes
Normative
Base Conformance Class definition table
  short form

## Slide 29: Part 12c Base Conformance Classes
Informative
Base Conformance Class definition table
  long form

## Slide 30: BASE-CCs Explained

## Slide 31: BASE-CC
One for each non-abstract entity in LPM/5
  abstract entities are not instanced
The BASE-CC for each base entity built from the EXPRESS definition of LPM/5
  pull-in: entities it references directly
  pull-in: entities that must point at it (via explicit inverse relationships - with no zero cardinality)

## Slide 32: BASE-CC
Inheritance requires relationships to any super-types to be considered
  BASE-CCs where generated automatically from the EXPRESS
    WHERE rules where not considered!
A “valid subset” results from recursively applying this pull-in until entity list is stable
  a base entity may have many valid subsets!

## Slide 33: Entity Pull-in Rules
INV

## Slide 34: Incomplete BASE-CC
Includes a reference to an entity that is external to that BASE-CC
Arise due to “dangling” multiple-choice references via
  ABSTRACT super-type
  SELECT type

## Slide 35: Via ABSTRACT supertype
ABS
OR

## Slide 36: Via ABSTRACT supertype
ABS
OR

## Slide 37: Via SELECT type
OR
SELECT

## Slide 38: Via SELECT type
OR
SELECT

## Slide 39: Incomplete BASE-CC
Must be “completed” to create a valid set
  choices for completing them!
CIS/2 defines rules for satisfy dangling relationships by adding in selected BASE-CCs
  rules derived (by hand) from the EXPRESS for each type of dangling reference

## Slide 40: WHERE Rules
The as-defined, BASE-CCs do not allow for the existence of any WHERE rules that require the co-existence of entities from different BASE-CCs.
  such rules may require some BASE-CCs to be used in combination, effective reducing the number of
    BASE-CCs
    incomplete BASE-CCs

## Slide 41: End: Item 2.3