## Slide 1: AISC CIS/2 Technical Workshop II, 22-25 June 1999, California
Dr A.J. Crowley
CIM steel
Session 0.2
ISO 10303-11: 1994 An Introduction to the EXPRESS Data Definition Language

## Slide 2
CIM steel
CIS/2
STEP
Part 4x:
Generic
Resources
Part 21:
Physical File
Format
Part 11:
EXPRESS
Part 22:
SDAI

## Slide 3
Part 11:
EXPRESS
Origin in STEP
Its Role
Its use in LPM/5
Mains features
EXPRESS-G

## Slide 4: EXPRESS: Its origin in STEP
STEP needed a modelling language that was:
  independent of a storage or programming paradigm,
  exchangeable in ASCII between different computers using different operating systems,
  sufficiently rigorous to define all the constraints required to model product data, and
  compilable into a schema for at least one of the following:
    1) an exchange file (Level 1 Implementation form),
    2) a shared memory (Level 2 Implementation form),
    3) a shared logical database (Level 3 Implementation form),
    4) a share knowledge base (Level 4 Implementation form).

## Slide 5: ISO 10303-11: 1994
A standard language for data specification
  forms a neutral computer processable conceptual schema
  can be parsed into a variety of formats
    (e.g. SQL, C++, FORTRAN).
It allows a data model of a product to be defined in terms of:
  a schema,
  containing entities
  with attributes,
  and constraints.

## Slide 6: The Role of EXPRESS
EXPRESS has been created specifically to define the information throughout a product’s life-cycle.
  EXPRESS itself does not provide for the definition of database formats, file formats, or transfer syntax.
    Other parts of ISO 10303 provide for mappings from EXPRESS schemata to implementation forms;
    (e.g. ISO 10303-21 which defines the exchange file format).
  EXPRESS data models are used to generate the data structures held within the STEP physical file using the mappings defined in the standard.
    However, the STEP physical file format is totally independent of EXPRESS.

## Slide 7: Use of EXPRESS in LPM/5
LPM/5 is the key component of CIS/2
Graphically presented in EXPRESS-G
Formally specified in EXPRESS
  Short form (containing definitions of specialized constructs)
  Long form (implementation schema)

## Slide 8: LPM/5: EXPRESS Short Form
LPM/5 EXPRESS Schema 'short form'
  provides illustrated descriptions of LPM/5 entities
    with their attributes & formal propositions (rules & constraints),
    together with references to STEP resources.
    It does not repeat the definitions of those STEP entities that have been used from the Generic Resources.
  Contains
    Schema Declaration
    Schema Interface Declarations
    Type Declarations - for Types specific to LPM/5
    Entity Declarations - for Entities specific to LPM/5
    Rule Declarations
    Function Declarations

## Slide 9: LPM/5 EXPRESS Long Form
LPM/5 EXPRESS Schema 'long form’
  one single schema
  with all the inter-schema references resolved.
  contains no definitions or explanations,
  merely an EXPRESS long form listing of the CIS/2 implementation schema.
  Contains
    Schema Declaration - STRUCTURAL_FRAME_SCHEMA
    Type Declarations - for all (Generic & Specific) Types
    Entity Declarations - for all (Generic & Specific) Entities
    Rule Declarations - for all (imported) Rules
    Function Declarations - for all (imported) Functions

## Slide 10: The Main Features of EXPRESS
The containing structure - SCHEMA
The definition of objects - ENTITIES
The attributes of the objects - TYPES
Constraints on the objects
    WHERE
    INVERSE
    DERIVE
    UNIQUE
    FUNCTIONs,
    Global RULEs,

## Slide 11: EXPRESS Data Types
In EXPRESS every value (attribute, local variable or formal parameter) has an associated data type.
Types can be classified as either:
  1) SIMPLE,
  2) NAMED,
    a) ENTITY TYPE, or
    b) DEFINED TYPE
  3) AGGREGATION,
  4) CONSTRUCTED
    a) ENUMERATION, or
    b) SELECT
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: 1. Simple Data Types
Simple data types are the basic types provided by the EXPRESS language.
  NUMBER
  REAL
  INTEGER
  STRING
  BOOLEAN
  LOGICAL
  BINARY
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: 2a. ENTITY Data Types
An ENTITY data type used to establish a relationship.
    ENTITY group_relationship;
    name : label;
    description : text;
    relating_group : group;
    related_group : group;
    END_ENTITY;
    ENTITY group;
    group_name : label;
    group_description : text;
    END_ENTITY;
The group_relationship entity has two attributes named having the data type group.
This effectively relates the group_relationship with two groups,
and hence relates two groups to each other.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: 2b. DEFINED Data Types
Example of a DEFINED data type declared by a TYPE assigned by the modeller.
    TYPE identifier = STRING;
    END_TYPE;
    TYPE label = STRING;
    END_TYPE;
    TYPE text = STRING;
    END_TYPE;
  The attributes named id, name, and description are all STRINGs. However, the use of the defined data types help to clarify the meaning and context of the STRINGs.
    ENTITY organization ;
    id : OPTIONAL identifier;
    name : label;
    description : text;
    UNIQUE
    UR1 : id;
    END_ENTITY;
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: 3. Aggregation Data Types
Aggregation types are used to represent ordered or unordered collections of elements of some basic type.
    ENTITY assembly_design_structural_connection_internal
    SUBTYPE OF (assembly_design_structural_connection);
    connected_members : SET [2:?] OF
    assembly_design_structural_member;
    END_ENTITY;
  - AGGREGATION data types may be either: ARRAY, BAG, LIST, or SET.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: 4a. Enumeration Data Type
An enumeration data type is an ordered set of values represented by names.
  The values of the enumeration type are designated by enumeration_ids and are referred to as enumeration items.
  Each enumeration item belongs only to the data type which defines it and must be unique within that type definition.
    TYPE action_source_accidential
    = ENUMERATION OF (fire, impulse, impact, undefined);
    END_TYPE;
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: 4b. Select Data Type
A select data type defines a named collection of other types.
  This collection is called the select list.
  An instance of a select data type is an instance of one of the types specified in the type list.
    This allows an attribute or variable to be one of several types.
  If the type of an attribute is a select type, then it is defined to be one of the types in the select list.
    TYPE assembly_component_select
    = SELECT (assembly_manufacturing_child, located_part, located_feature, located_joint_system);
    END_TYPE;
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18: Domain Rules
Domain rules specify constraints that restrict a defined data type.
  Domain rules follow the WHERE keyword.
    Each domain rule evaluates to a logical (TRUE, FALSE, UNKNOWN) value.
    TYPE length_measure = REAL;
    END_TYPE; -- STEP Part 41
    TYPE positive_length_measure
    = length_measure;
    WHERE
    WR41T1 : SELF > 0;
    END_TYPE; -- STEP Part 41
  Any attribute, local variable or formal parameter declared to be of type positive_length_measure is constrained to have only positive values.
Notes: <number>
<footer>
<header>
<date/time>
A domain rule is asserted when the expression evaluates to TRUE; and is violated when the expression evaluates to FALSE.

## Slide 19: Supertypes & Subtypes
The subtype/supertype structure is the mechanism for specifying classification (or categorization) of object types
      ENTITY assembly ABSTRACT SUPERTYPE OF
      (ONEOF (assembly_design, assembly_manufacturing)
      ANDOR assembly_with_shape) SUBTYPE OF (structural_frame_product); assembly_sequence_number : OPTIONAL INTEGER; complexity : OPTIONAL complexity_level; END_ENTITY;
A subtype inherits all the attributes of its supertype(s)
  … and the attributes of the supertypes’ supertypes, etc...
Notes: <number>
<footer>
<header>
<date/time>
Since the subtype is a more specific kind of its supertype, every instance of a subtype is an instance of its supertype(s). An entity is a subtype if, and only if, it contains a subtype clause. A subtype entity inherits the attributes of the more general entities occurring above it in the subtype/supertype hierarchy.

## Slide 20: INVERSE attributes
Every attribute which as an entity as its data type, establishes an entity relationship.
  In both directions!!!
  By default the inverse cardinality is [0:?]
Inverse attributes are declared following the INVERSE keyword.
The INVERSE clause constrains the relationship in the inverse direction
  An inverse attribute captures the relationship between the entity being referred to, and the named attribute of the referencing entity.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: INVERSE attributes (Example)
ENTITY analysis_model
...
INVERSE
component_elements : SET [1:?] OF element FOR parent_model;
component_nodes : SET [2:?] OF node FOR parent_model;
END_ENTITY;
ENTITY node; node_name : label;
...
parent_model : analysis_model;
UNIQUE
UR1 : node_name, parent_model;
END_ENTITY;
ENTITYelement
element_name : label;
..
parent_model : analysis_model;
UNIQUE
UR1 : element_name, parent_model;
END_ENTITY;
mutual dependency!!!

## Slide 24: EXPRESS-G
A Graphical form of EXRESS
  Used to illustrated EXPRESS data models
  Presents a limited subset of EXPRESS language
label
STRING
si_unit
name
si_unit_name
si_prefix
prefix
measure_with_unit
unit
derived_unit
named_unit
unit_component
context_dependent_unit
name

## Slide 25: Simple & Defined Data types
item_number
label
structural_frame_item
Entity
Data Types
text
item_name
item_description
Attributes
Simple
Defined
INTEGER
STRING
Defined
Simple
ENTITY structural_frame_item;
item_number : INTEGER;
item_name : label;
item_description : OPTIONAL text;
END_ENTITY;
Optional attribute

## Slide 26: Entity Data Types
dimensions
dimensional_exponents
named_unit
ENTITY named_unit;
dimensions : dimensional_exponents;
END_ENTITY;
ENTITY dimensional_exponents;
length_exponent : REAL;
mass_exponent : REAL;
time_exponent : REAL;
END_ENTITY;
length_exponent
Entity
Attributes
Entity Data Type
mass_exponent
time_exponent
REAL
REAL
REAL

## Slide 27: Supertypes & Subtypes
structural_frame_item
structural_frame_product
Supertype
structural_frame_product
_with_material
ANDOR
Subtype
part
coating
fastener
1
(ABS)
assembly
Subtypes
Subtype
ENTITY structural_frame_product
SUPERTYPE OF
(ONEOF (assembly,coating, part, fastener)
ANDOR structural_frame_product_with_material)
SUBTYPE OF (structural_frame_item);
life_cycle_stage : OPTIONAL label;
END_ENTITY;

## Slide 28: Enumeration Data Types
si_unit
name
si_unit_name
si_prefix
prefix
named_unit
1
Enumeration
Data Types
ENTITY si_unit
SUBTYPE OF (named_unit);
prefix : OPTIONAL si_prefix;
name : si_unit_name;
END_ENTITY;
TYPE si_unit_name = ENUMERATION OF (METRE, GRAM, SECOND, AMPERE,
KELVIN, MOLE, CANDELA, RADIAN, STERADIAN, HERTZ, NEWTON, PASCAL, JOULE, WATT, COULOMB, VOLT, FARAD, OHM, SIEMENS, WEBER, TESLA, HENRY, DEGREE_CELSIUS, LUMEN, LUX, BECQUEREL, GRAY, SIEVERT);
END_TYPE;

## Slide 29: Select Data Types (1)
measure_with_unit
measure_value
value_component
REAL
length_measure
mass_measure
Select Type
ENTITY measure_with_unit;
value_component : measure_value;
unit_component : unit;
END_ENTITY;
TYPE measure_value = SELECT
(length_measure, mass_measure);
END_TYPE;
TYPE length_measure = REAL;
END_TYPE;
TYPE mass_measure = REAL;
END_TYPE;

## Slide 30: Select Data Types (2)
measure_with_unit
unit
derived_unit
named_unit
unit_component
measure_value
value_component
Select Type
ENTITY measure_with_unit;
value_component : measure_value;
unit_component : unit;
END_ENTITY;
TYPE unit = SELECT
(derived_unit, named_unit);
END_TYPE;
ENTITY named_unit;
END_ENTITY;
TYPE derived_unit;
END_ENTITY;

## Slide 31: Aggregation Data Types
moments_of_inertia A[1:3] A[1:3]
masses A[1:3]
element_point_stationary_mass
REAL
REAL
Two Dimensional ARRAY
One Dimensional ARRAY
ENTITY element_point_stationary_mass
masses : ARRAY [1:3] OF REAL;
moments_of_inertia : ARRAY [1:3] OF ARRAY [1:3] OF REAL;
END_ENTITY;

## Slide 32: Inverse Clauses
representation
name
representation_item
context_of_items
representation_context
context_type
context_identifier
items S[1:?]
name
(INV) representations_in_context S [1:?]
ENTITY representation;
name : label;
items : SET [1:?] OF representation_item;
context_of_items : representation_context;
END_ENTITY;
ENTITY representation_context;
context_identifier : identifier;
context_type : text;
INVERSE
representations_in_context : SET [1:?] OF representation FOR context_of_items;
END_ENTITY;

## Slide 33
CIM steel
CIS/2
STEP
Part 4x:
Generic
Resources
Part 21:
Physical File
Format
Part 11:
EXPRESS
Part 22:
SDAI

## Slide 34
Part 11:
EXPRESS
Questions?