## Slide 1: AISC CIS/2 Technical Workshop II, 22-25 June 1999, California
Dr A.J. Crowley
CIM steel
Session 0.3
ISO 10303-21: 1994 An Introduction to the STEP Physical File Format

## Slide 2
CIM steel
CIS/2
STEP
Part 4x:
Generic
Resources
Part 21:
Physical File
Format
Part 11:
EXPRESS
Part 22:
SDAI

## Slide 3
Part 21:
Physical File
Format
Requirements of CIS/2
The Exchange Structure
The Special Tokens
Header & Data Sections
Mapping from EXPRESS

## Slide 4: Requirements of CIS/2
For file exchange, CIS/2 specifies that:
  the physical file format shall be in accordance with ISO 10303-21: 1994
    November 1994 International Standard issue together with the 1996 'Technical Corrigendum'.
    Implementation Methods: ‘Clear text encoding of the exchange structure’

## Slide 5: The Exchange Structure
A sequential file using a clear text encoding.
Described by an unambiguous, context-free grammar to facilitate parsing by software.
  The grammar is expressed in Wirth Syntax Notation.
Consists of two sections:
  header section
    providing data relating to the exchange structure itself, and
  data section
    providing the data to be transferred.

## Slide 6: The Special Tokens
ISO-10303-21;
  used to open an exchange structure,
HEADER;
  used to open the header section.
DATA;
  used to open the data section.
ENDSEC;
  is used to close both sections.
END-ISO-10303-21;
  used to close an exchange structure.

## Slide 7: Header Schema
SCHEMA header_section_schema;
ENTITY file_description;
description: LIST [1:?] OF STRING (256);
implementation_level: STRING (256);
END_ENTITY;
ENTITY file_name;
name: STRING (256);
time_stamp: STRING (256);
author: LIST [1:?] OF STRING (256);
organization: LIST [1:?] OF STRING (256);
preprocessor_version: STRING (256);
originating_system: STRING (256);
authorization: STRING (256);
END_ENTITY;
ENTITY file_schema;
schema_identifiers:
LIST [1:1] OF schema_name;
END_ENTITY;
TYPE schema_name =
STRING (1024);
END_TYPE;

## Slide 8: Header Section
Example Populated Header Section
HEADER;
FILE_DESCRIPTION (('Test case 1'),'1');
FILE_NAME ('testcase1.stp', '1999-05-19T12:16:30', ('A.J.Crowley'), ('Steel Construction Institute'), '1.5.1 (compiled 17:44 11/24/1998)', 'NIST EXPRESSO', 'ajc');
FILE_SCHEMA (('STRUCTURAL_FRAME_SCHEMA'));
ENDSEC;

## Slide 9: The Data Section
Contains instances of entities that correspond to the EXPRESS schema governing the exchange structure in the header section.
Six simple data types are used:
  INTEGER,
  REAL,
  STRING,
  ENTITY instance name (i.e. the # number),
  ENUMERATION, and
  BINARY.

## Slide 10: Mapping to the Data Section
The form of the product data in the exchange structure is specified by using a mapping from the EXPRESS language.
Part 21:
Physical File
Format
Part 11:
EXPRESS
LPM/5
EXPRESS
Schema
Populated
CIS data
exchange file

## Slide 11: Mapping of EXPRESS constructs
STEP Part 21 defines mappings into the exchange structure for the following EXPRESS constructs:
  ENTITY
  SIMPLE Data types
  AGGREGATION Data types
  ENUMERATION Data types
  SELECT Data types
  SUPERTYPE-SUBTYPE

## Slide 12: Unmapped Constructions
The following EXPRESS constructs do not map into the exchange structure:
  WHERE Rules
  INVERSE Attributes
  SCHEMA Declaration
  CONSTANTs
  RULEs
  Remarks

## Slide 13: Mapping Entities & Entity Types
Each entity instance shall be represented at most once in the data section;
  distinct entity instances shall have distinct entity instance names (i.e. the #number).
The entity instances need not be ordered in the exchange structure.
  An entity instance may be referenced before its name occurs as an identifier in the exchange structure.
  An entity data type is mapped by placing the #number in the place of the attribute value
#123 = ENTITY_NAME (values of attributes);

## Slide 14: Mapping Entities: Example
Example entity definition in EXPRESS
ENTITY widget;
widget_material : material;
END_ENTITY;
ENTITY material;
name : STRING;
END_ENTITY;
Sample entity instance in data section
#1 = WIDGET (#3);
#3 = MATERIAL (‘steel’);

## Slide 15: Mapping Simple data types
Optional values
  Where an Optional attribute has not been given a value, it shall be encoded as a dollar sign "$".
Boolean
  The EXPRESS element of BOOLEAN shall be treated as a pre-defined enumerated data type with a value encoded as "T" (for TRUE) and "F" (for FALSE).
Logical
  The EXPRESS element of LOGICAL shall be treated as a pre-defined enumerated data type with a value encoded as "T" (for TRUE), "F" (for FALSE) and "U" (for UNKNOWN).

## Slide 16: Mapping Simple data types: Example
Example entity definition in EXPRESS
ENTITY widget;
A : OPTIONAL REAL;
B : BOOLEAN;
C : LOGICAL;
END_ENTITY;
Sample entity instance in data section
#1 = WIDGET ($, .T., .F.);
widget
C
B
A
BOOLEAN
REAL
LOGICAL

## Slide 17: Mapping Aggregation data types
Aggregation data types
  The EXPRESS elements of LIST, BAG, SET or an ARRAY shall be mapped to the exchange structure as a list data type.
  If an entire list is optional and does not exist, the list shall be encoded by a dollar sign “$”.
  If the list is empty, the list shall be encoded as a left parenthesis “(” followed by a right parenthesis “)”.

## Slide 18: Mapping Aggregation types: Example
Example entity definition in EXPRESS
ENTITY widget;
attribute1: LIST [0:6] OF INTEGER;
attribute2: SET [1:?] OF INTEGER;
attribute3: OPTIONAL ARRAY [1:3] OF INTEGER;
END_ENTITY;
Sample entity instance
in data section:
#4 = WIDGET((), (1,2,4), $);
widget
attribute3 A[1:3]
attribute2 S[1:?]
attribute1 L[0:6]
INTEGER
INTEGER
INTEGER

## Slide 19: Mapping Enumeration data types
Enumeration data types
  The actual value in an instance of the ENUMERATION shall be one of the enumerated values in the EXPRESS schema, in capital letters and delimited by full stops.

## Slide 20: Mapping Enumeration types: Example
Example entity definition in EXPRESS
TYPE primary_colour = ENUMERATION OF (red, green, blue);
END_TYPE;
ENTITY widget;
p_colour : primary_colour;
END_ENTITY;
Sample entity instance in data section
#2 = WIDGET(.RED.);
widget
p_colour
primary_colour

## Slide 21: Mapping SELECT data types
Defines a list of data types,
  called the 'select-list',
  whose values are valid instances of select data type,
  and include all of the subtype entities of supertypes
An instance of a select data type shall be a value of a least one of the data types in the select-list.
  If the data type in the select list is itself a select data type, then the encoding rules are applied recursively.
  Only instances of entity data types, simple data types and enumeration data types can actually be encoded.

## Slide 22: Mapping SELECT types: Example (1)
measure_with_unit
unit
derived_unit
named_unit
unit_component
measure_value
value_component
length_measure _with_unit
mass_measure _with_unit
time_measure _with_unit
1
REAL
length_unit
mass_unit
time_unit
1
length_measure
mass_measure
time_measure

## Slide 23: Mapping SELECT types: Example (2)
Entity definition in EXPRESS
ENTITY measure_with_unit;
value_component : measure_value;
unit_component : unit;
END_ENTITY;
TYPE measure_value = SELECT (length_measure, mass_measure);
END_TYPE;
TYPE unit = SELECT (derived_unit, named_unit);
END_TYPE;
Sample entity instance in data section
#202 = LENGTH_MEASURE_WITH_UNIT (LENGTH_MEASURE(498.0), #1021);
#1021 = LENGTH_UNIT( );

## Slide 24: Mapping of Supertype / subtypes
Supertype / subtype entities
  Population results in ‘complex entity instances’.
Two ‘Mapping Rules’ defined
  Internal mapping
  External mapping
    Selection depends on which (STEP Part 21) Conformance Class selected (and stated in HEADER section).
  If Conformance Class 1 selected
    Use Internal mapping for single inheritance graphs and
    External mapping for multiple inheritance graphs
  If Conformance Class 2 selected
    Use External mapping for all ‘complex entity instances’

## Slide 25: Internal & External Mapping
Internal mapping
  only the name of the lowest level subtype shown in physical file
  attributes appear in order of inheritance
    e.g. #100 = CC (aa, cc);
External mapping
  all entities in the inheritance graph named in physical file in alphabetical order of the entity name
  attributes appear with their parent entity
    e.g. #100 = (AA (aa) BB(bb) CC(cc));

## Slide 26: Supertype-subtypes: Example
Entity definition in EXPRESS
ENTITY named_unit
SUPERTYPE OF (ONE OF (length_unit, mass_unit, time_unit)
ANDOR (ONEOF (si_unit, conversion_based_unit)));
dimensions : dimensional_exponents;
END_ENTITY;
ENTITY si_unit ;
SUBTYPE OF (named_unit);
prefix : OPTIONAL si_prefix;
name : si_unit_name;
DERIVE
SELF\named_unit.dimensions : dimensional_exponents := dimensions_for_si_unit (SELF.name);
END_ENTITY;
ENTITY length_unit ;
SUBTYPE OF (named_unit);
END_ENTITY;

## Slide 27: Internal mapping: Example (1)
length_unit
mass_unit
time_unit
conversion_based_unit
name
dimensions
dimensional_exponents
si_unit
name
si_unit_name
si_prefix
prefix
named_unit
1
1
Sample entity instance in data section
/* Length Unit (mm) */
#1021 = LENGTH_UNIT(#1022);
#1022 = DIMENSIONAL_EXPONENTS (1.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0);

## Slide 28: External mapping: Example (1)
Sample entity instance
/* Length Unit (mm) */
#1020 = SI_UNIT (*, .MILLI., .METRE.));
#1021 = (LENGTH_UNIT() NAMED_UNIT(*) SI_UNIT(.MILLI., .METRE.));
length_unit
mass_unit
time_unit
conversion_based_unit
name
dimensions
dimensional_exponents
si_unit
name
si_unit_name
si_prefix
prefix
named_unit
1
1
Redefined attribute

## Slide 29: Redefined attributes
Supertype attributes redefined in a subtype
  If a subtype entity redefines an attribute of its supertype using the DERIVE clause, that attribute in the supertype shall be encoded with an asterisk “*”.
Sample entity instance
/* Length Unit (mm) */
#1020 = SI_UNIT (*, .MILLI., .METRE.));
#1021 = (LENGTH_UNIT() NAMED_UNIT(*) SI_UNIT(.MILLI., .METRE.));
Redefined attribute

## Slide 30
CIM steel
CIS/2
STEP
Part 4x:
Generic
Resources
Part 21:
Physical File
Format
Part 11:
EXPRESS
Part 22:
SDAI

## Slide 31: Questions?
Part 21:
Physical File
Format

## Slide 32: Related Web Sites
http://www.steel-sci.org/
The Steel Construction Institute
About SCI
News
Expertise
Membership
Courses &
Publications
Education
http://www.cis2.org/
CIM steel