## Slide 1: AISC CIS/2 Technical Workshop II, 22-25 June 1999, California
Session 0.4
An Introduction to LPM/5:
The Basic Principles
Dr A.J. Crowley
CIM steel

## Slide 2
CIM steel
CIS/2
CCs
STEP
Product
Modelling
LPM/5

## Slide 3
The LPM Concept
Requirements of LPM/5
Fundamental Principles
Key Aspects
LPM/5

## Slide 4: The LPM Concept
Logical
  It exists at the logical level, as opposed to the application or physical level.
Product
  the product we are concerned with is a building-type structural steel frame.
Model
  It is a limited representation of some aspect of the real world.

## Slide 5: The Logical Product Model
The LPM defines a logical structure for data in terms of:
  entities (or things),
  attributes (or characteristics),
  and relationships between entities.
part_prismatic_
simple_curved
axis_definition
curve

## Slide 6: LPM/5
A formal definition of how engineering information should be systematically structured for data exchange
  Intended to cover all types of engineering information associated with a steel frames
Graphically presented in EXPRESS-G
Formally specified in EXPRESS
  Short form (containing definitions of specialized constructs)
  Long form (implementation schema)
The key component of the CIS

## Slide 7: LPM/5: Short Form
LPM/5 EXPRESS Schema ‘short form’
  provides illustrated descriptions of LPM/5 entities
    with their attributes & formal propositions (rules & constraints),
    together with references to STEP resources.
    It does not repeat the definitions of those STEP entities that have been used from the Generic Resources.
  Contains
    Schema Declaration
    Schema Interface Declarations
    Type Declarations - for Types specific to LPM/5
    Entity Declarations - for Entities specific to LPM/5
    Rule Declarations
    Function Declarations

## Slide 8: LPM/5 Long Form
LPM/5 EXPRESS Schema ‘long form’
  one single schema
  with all the inter-schema references resolved.
  contains no definitions or explanations,
  merely an EXPRESS long form listing of the CIS/2 implementation schema.
  Contains
    Schema Declaration - STRUCTURAL_FRAME_SCHEMA
    Type Declarations - for all (Generic & Specific) Types
    Entity Declarations - for all (Generic & Specific) Entities
    Rule Declarations - for all (imported) Rules
    Function Declarations - for all (imported) Functions

## Slide 9: Requirements of LPM/5
part_prismatic_
simple_curved
axis_definition
curve

## Slide 10: Requirements of LPM/5
part_prismatic_
simple_castellated
profile
section_profile_i_type
part_castellation_type
castellation_type
= .CIRCULAR.

## Slide 11
profile
part_prismatic_
simple_curved
axis_definition
curve
part_prismatic_
simple_castellated
part_castellation_type
castellation_type
= .CIRCULAR.
part_prismatic_simple
section_profile_i_type
ANDOR

## Slide 12
part_prismatic_simple
profile
section_profile_
i_type_asymmetric
part_sheet_profiled
sheet_profile
curve

## Slide 13
joint_system_complex
systems (1)
systems (2)
joint_system_welded
weld_mechanism
weld_specification
composite_curve
weld_path
fastener_simple_ shear_connector
mechanism
joint_system_mechanical
fastener_mechanism
fasteners L[1:?]
points
layout_points
L[1:?]

## Slide 14: Fundamental Principles of LPM/5
CIS/2 presents LPM/5 as both:
  Short form EXPRESS schema and
  Long form EXPRESS schema
LPM/5 uses STEP ‘Generic Resources’ wherever possible
  ISO 10303-41: 1994 - date, person, measures and units
  ISO 10303-42: 1994 - explicit geometry and topology
  ISO 10303-43: 1994
  ISO 10303-44: 1994
LPM/5 contains 3 “Views” (models) of structure
  Analysis, Design, Manufacturing (Physical)

## Slide 15: LPM/5 Short Form: Details
Divided into 17 ‘subject areas’:
  1. Decomposition
  2. Project Definition
  3. Structural Modelling
  4. Loading
  5. Structural Response
  6. Parts
  7. Features
  8. Joint Systems
  9. Materials
  10. Location
  11. Grouping
  12. Geometry
  13. Units & Measures
  14. Items References
  15. Product Definition
  16. Process Definition
  17. Data Management

## Slide 16: LPM/5: The 3 ‘Views’
Analysis
Design
Manufacturing
LPM/5
Mapping

## Slide 17: Analysis - Design - Manufacturing
(ABS)
assembly
assembly_design
assembly_manufacturing
1
analysis_model
element
node
located_joint_system
located_part
design_part
design_joint_system

## Slide 18: Key Aspects of LPM/5
Data management constructs
  separating data from meta-data
Product item references
  standard, proprietary, library
Inclusion of implicit & explicit geometry
  simple & complex
Use of ANDOR SUPERTYPEs
Use of ‘associative entities’
  the ‘level discriminator’
Units and measures
  Global and individual

## Slide 19: Naming Convention
Entities listed in alphabetical order
    ENTITY action;
    ...
    ...
    ENTITY zone_of_structure
Entities given full names
  abbreviations avoided
  name reflects inheritance
    e.g. assembly_design_structural_member_linear

## Slide 20: Data Management in CIS/2
LPM/5 separates data from ‘meta-data’,
  This ‘meta-data’ includes some or all of the following:
  The unique identifier for the item.
  The person who created / modified / deleted the data.
  The date when it was created / modified / deleted.
  Whether the data was new or old data that had been modified.
  Whether the data has been approved or not.

## Slide 21: Data Management via CIS/2
In CIS/2, data management is considered to be the process of assigning meta-data to data.
  ‘Data Management Conformant’ (DMC) applications produce ‘managed data’
    Each item of data is given a unique id and placed in a data set
  ‘Non-DMC applications’ produce ‘unmanaged data’
Using a DMC application,
  ‘unmanaged data’ may be mapped onto meta data
  to become ‘managed data’
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Data Management: The Basics
select_data_item
*data_item
managed_data_item
structural_frame_item
generic_item
INTEGER
LOGICAL
original_data
*instance_id
deleted_item

## Slide 23: Data Management: The Basics
managed_application_usage
*history L[1:?]
INV processed_items S[1:?]
select_data_item
*data_item
managed_application _installation
managed_data_item
*installation_id,
*application_id
structural_frame_item
generic_item
INTEGER
LOGICAL
original_data
*instance_id
deleted_item
originating_application
application

## Slide 24: Data Management: The Meta-data
managed_application_usage
*history L[1:?]
INV processed_items S[1:?]
managed_application _installation
managed_data_item
originating_application
application
person_and_organization
date_and_time
BOOLEAN
new_ids_added
label
text
user
processing_date
usage_description
life_cycle_stage

## Slide 25: Product Identifiers in CIS/2
4 classes of product item are defined
  Standard Items.
  Proprietary Items
  Library Items
    information exchanged by being “passed-by-reference” rather than being “passed by attribute value”.
  Non-standard Items

## Slide 26: Assigning Item References
assigned_reference
structural_frame_item
item_reference_assigned
identifier
ref
item_reference _proprietary
item_reference _standard
(ABS)
item_ref_source
item_reference
1
1
item_ref_source _standard
item_ref_source _proprietary
source
source
assigned_to_item

## Slide 27
ISO-10303-21;
HEADER;
FILE_DESCRIPTION(('STEP US FLAVOUR'), '1');
FILE_NAME('Step US Flavour', '11-05-1998', (‘’), (‘’), ‘’,’’,’’);
FILE_SCHEMA(('STRUCTURAL_FRAME_SCHEMA'));
ENDSEC;
DATA;
#3000=GROUP(‘US Flavour list’, ‘List of item references in accordance with
ASTM standards’);
#3001=FLAVOUR(#3000, (#1, #3, ….. , #2354, #2355)):
#1 = ITEM_REFERENCE_STANDARD (‘W1100X424’, #2);
#2 = ITEM_REF_SOURCE_STANDARD (‘ASTM’, ‘ASTM_A6M’, 1994, $);
#3 = ITEM_REFERENCE_STANDARD (‘W1100X369’, #2);
#4 = ITEM_REFERENCE_STANDARD (‘W1100X333’, #2);
#5 = ITEM_REFERENCE_STANDARD (‘W1100X295’, #2);
#2354 = ITEM_REFERENCE_STANDARD (‘M30_TYPE1’, #2349);
#2355 = ITEM_REFERENCE_STANDARD (‘M36_TYPE1’, #2349);
ENDSEC;
END-ISO-10303-21;
Physical File (extract)

## Slide 28: Implicit and Explicit Geometry
CIS/1 contained no provision for explicit geometry
  all geometry defined implicitly using parameters
CIS/2 incorporates the whole of STEP Part 42
  all the EXPRESS constructs for geometry and topology included in LPM/5
  used as resources as required

## Slide 29: ‘Simple’ & ‘Complex’ Objects
In LPM/5 Objects are categorized (through subtyping) as either simple or complex
  depending on the definition of the shape of object
Simple Objects
  have their shape defined implicitly through parameters
Complex Objects
  have their shape defined explicitly using constructs from STEP Part 42

## Slide 30: ‘Simple’ & ‘Complex’ Objects
ENTITY object
SUPERTYPE OF (ONE OF(object_simple, object_complex));
END_ENTITY;
ENTITY object_simple
SUBTYPE OF (object);
length : length_measure_with_unit;
depth : length_measure_with_unit;
width : length_measure_with_unit;
END_ENTITY;
ENTITY object_complex
SUBTYPE OF (object);
shape : shape_representation;
END_ENTITY;

## Slide 31: ANDOR SUPERTYPEs
structural_frame_product
material_definition
part
coating
fastener
1
structural_frame_product
_with_material
ANDOR
material
(ABS)
assembly

## Slide 32: ‘Associative entities’
joined_parts S [0:?]
(INV) required_joints S [0:?]
locations S[0:?]
assembly_manufacturing
part
parent_assemblies S [0:?]
joint_system
parent_assemblies S [0:?]
coord_system
locations S[0:?]
parent_coord_system

## Slide 33: ‘The Level Discriminator’
located_part_joint
parent_assembly
located_joint_system
descriptive_joint_system
located_part
descriptive_part
(ABS)
located_item
location
1
coord_system
assembly_manufacturing
part
parent_assembly
joint_system
logically_joined_parts S[2:2]
required_joints S[1:?]
coord_system_child
parent_coord_system

## Slide 34: Representations
Two points p1 (0, 0, 0) and p2 (1, 1, 1)
  How far apart? (3?)

## Slide 35: Representation of shape
geometric_ representation_context
coordinate_space _dimension
representation
name
representation_item
context_of_items
representation_context
context_type
context_identifier
items
S[1:?]
shape_representation
name
geometric_ representation_item
Every representation item needs to be placed into its context

## Slide 36: Geometric representation items
curve
point
geometric_ representation_item
1
name
representation_item
cartesian_point
coordinates L[1:3]
line
pnt
vector
direction
orientation
length_measure
magnitude
dir
REAL
direction_ratios
L[1:3]

## Slide 37: Units & Measures
Constructs for units and measures have been taken from STEP Part 41
  Using the ‘interpreted route’
Units are specified either Globally or individually
  In general, constructs taken from STEP have their units assigned globally
  Constructs developed for LPM/5 have their units assigned individually

## Slide 38: Globally assigned units
geometric_ representation_context
coordinate_space _dimension
representation_context
context_type
context_identifier
global_unit_ assigned_context
ANDOR
unit
derived_unit
named_unit
units S[1:?]
unit
derived_unit_element
REAL
exponent
elements
S[1:?]
dimensions

## Slide 39: Named units
length_unit
mass_unit
time_unit
context_dependent_unit
name
conversion_based_unit
name
dimensions
dimensional_exponents
si_unit
name
si_unit_name
si_prefix
prefix
measure_with_unit
conversion_factor
named_unit
1
1
ANDOR

## Slide 40: Sample physical file
#1 = CARTESIAN_POINT ('node point 1', (0.0, 0.0, 0.0));
#2 = CARTESIAN_POINT ('node point 2', (0.0, 0.0, 5000.0));
...
#501 = REPRESENTATION ('nodal points', (#1, #2, #3, #4, #5, #6), #502);
#502 = (GEOMETRIC_REPRESENTATION_CONTEXT(3) GLOBAL_UNIT_ASSIGNED_CONTEXT((#1021)) REPRESENTATION_CONTEXT('context for nodal points', 'units for coordinates'));
...
/* Length Unit (mm) */
#1021 = (LENGTH_UNIT()NAMED_UNIT(*)SI_UNIT(.MILLI.,.METRE.));
/* Force Unit (KN) */
#1031 = (FORCE_UNIT()NAMED_UNIT(*)SI_UNIT(.KILO.,.NEWTON.));
/* Plane Angle Unit (radian) */
#1033 = (NAMED_UNIT(*)PLANE_ANGLE_UNIT()SI_UNIT($,.RADIAN.));

## Slide 41: Derived units
/* Inertia Unit (cm4) */
#1149 = (LENGTH_UNIT()NAMED_UNIT(*)SI_UNIT(.CENTI.,.METRE.));
#1150 = DERIVED_UNIT_ELEMENT (#1149, 4.0);
#1151 = INERTIA_UNIT ((#1150));
/* Modulus Unit (cm3) */
#1156 = DERIVED_UNIT_ELEMENT (#1149, 3.0);
#1157 = MODULUS_UNIT ((#1156));
/* Area Unit (cm2) */
#1161 = (AREA_UNIT()CONVERSION_BASED_UNIT('square centimetre', #1162)NAMED_UNIT (#1165));
#1162 = MEASURE_WITH_UNIT (1.0, #1163);
#1163 = DERIVED_UNIT ((#1164));
#1164 = DERIVED_UNIT_ELEMENT (#1149, 2.0);
#1165 = DIMENSIONAL_EXPONENTS (2.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0);

## Slide 42: Explicit units
measure_with_unit
unit
derived_unit
named_unit
unit_component
measure_value
value_component
length_measure _with_unit
mass_measure _with_unit
time_measure _with_unit
1
REAL
length_unit
mass_unit
time_unit
1
length_measure
mass_measure
time_measure
WHERE

## Slide 43: Explicit units in use
section_profile_circle
section_profile_circle_hollow
measure_with_unit
external_radius
positive_length_ measure_with_unit
wall_thickness
measure_value
value_component
length_measure
unit
named_unit
unit_component
length_unit
REAL
positive_length_measure

## Slide 44: Sample physical file
#201 = SECTION_PROFILE_CIRCLE_HOLLOW (’CHS273x10', 1, ’Circular Hollow Section beam to EN10210, 'Plastic', $, #202, #203);
#202 = POSITIVE_LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(136.5), #1021);
#203 = POSITIVE_ LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(10.0), #1021);
...
/* Length Unit (mm) */
#1021 = (LENGTH_UNIT()NAMED_UNIT(*)SI_UNIT(.MILLI.,.METRE.));

## Slide 45: Uncertainty
geometric_ representation_context
representation_context
context_type
context_identifier
global_unit_ assigned_context
ANDOR
unit
named_unit
units S[1:?]
REAL
length_unit
global_uncertainty_assigned_context
uncertainty_measure_with_unit
uncertainty S[1:?]
measure_with_unit
measure_value
value_component
length_measure
unit_component

## Slide 46: Related Web Sites
http://www.steel-sci.org/
The Steel Construction Institute
About SCI
News
Expertise
Membership
Courses &
Publications
Education
http://www.cis2.org/
CIM steel