## Slide 1: AISC CIS/2 Workshop #2
Item 1.7
Conformance Classes: Revision plus Changes since CIS/2 
Irvine, CA: June 1999 (rev 2)

## Slide 2: Objective
To briefly revise the topic of Conformance Classes (CCs)
To introduce some CC related changes since Workshop #1
  i.e. from CIS/2  release to CIS/2 Publish

## Slide 3: Context
Study
Implement
Map Data
Scope

## Slide 4: CC Revision
from Workshop #1
or from Day 0

## Slide 5: Basic Concepts

## Slide 6: Conformance Class
Term borrowed from ISO10303 (STEP)
A logical subset of the LPM
  for specifying translator scope
  for testing translator compliance
Hard boundaries
  all entities within must be supported in full!

## Slide 7: Conformance Class
Pre-defined in the CIS/2 documentation
  scope of each CC is derived logically from the EXPRESS schema
Large number of defined CCs
  and they can be used in combination!
  which CCs to use?

## Slide 8: Base Conformance Class
CIS/2  documentation defines 545 BASE-CCs
  each is “based-on” a different entity
  lists other “included entities”
As defined, each BASE-CCs is either Complete or Incomplete
  must be “completed” prior to use!

## Slide 9: Completing CCs
BASE-CC
Complete
Incomplete
Completed_by

## Slide 10: Completing CCs
BASE-CC
Complete
Incomplete
Completed_by

## Slide 11: CC Combinations
Assemble as needed from completed BASE-CCs
Define by a list of BASE-CC numbers
  same entity can be repeatedly included at multiple levels (Venn diagram nesting)
Huge number of possible combinations!

## Slide 12: Why so complex?

## Slide 13: Valid Subsets
A completed CC simply defines a subset of the LPM that is logically valid to instantiate
  subset need not be useful
  subset need not be (that) meaningful
LPM/5 is large and complex
  many valid subsets are possible!

## Slide 14: Hard Boundaries
The overall scope of a particular translator corresponds to a particular CC combination
  correctly translate all data within that valid subset
    every entity, and
    every (non OPTIONAL) attribute
  may translator provide user control for exporting or importing lesser valid scopes
Care when scoping a translator!

## Slide 15: Export Translator
Full information scope of the application
Full CC scope of export translator
Lesser valid subsets

## Slide 16: Export Scope: Full Data
Application fully populated with data
Export full CC scope of the translator
  CIS data will also satisfy any subset CCs
If the translator provides for it, could export a lesser valid subset
  CIS data will also satisfy any subset CCs

## Slide 17: Export Translator
Full information scope of the application
Full CC scope of export translator
Part populated information scope
Lesser valid subsets

## Slide 18: Export Scope: Partial Data
Application only partly populated with data
Export full CC scope of the translator
  will the mapping logic still work correctly?
  subset CCs may be fully populated with CIS data
If the translator provides for it, could export a lesser (but fully populated) valid subset

## Slide 19: Import Translator
Full information scope of the application
Full CC scope of import translator

## Slide 20: Import Translator
Full information scope of the application
Full CC scope of import translator
Greater valid subsets

## Slide 21: Import Scope: Full Data
Importing application not pre-populated with data
CIS data full populates CC scope of import translator
  CIS data may exceed CC scope of translator!

## Slide 22: Import Translator
Full information scope of the application
Full CC scope of import translator
Populated valid subset

## Slide 23: Import Scope: Partial Data
Importing application not pre-populated with data
Import full CC scope of translator
  will the mapping logic still work correctly?
  IDEALLY logic able to import, in isolation, each within-scope completed BASE-CC!
If the translator provides for it, could import a lesser (but fully populated) valid subset

## Slide 24: Export and Import
Export
  Full CC scope of translator
  Lesser valid subset (requested and/or partial data)
Import
  Full CC scope of translator
    Excess data CIS data ignored
  Lesser valid subset (requested and/or partial data)
    application must be able to store and manipulate any such subset!

## Slide 25: Import Translator
Full information scope of application
Full CC scope of import translator
Lesser valid subsets
Populated valid subset

## Slide 26: CIS/2 Beta Documentation

## Slide 27: Incomplete BASE-CC
Includes a reference to an entity that is external to that BASE-CC
Arise due to “dangling” multiple-choice references via
  ABSTRACT super-type
  SELECT type

## Slide 28: Via ABSTRACT supertype
ABS
OR

## Slide 29: Via ABSTRACT supertype
ABS
OR

## Slide 30: Via SELECT type
OR
SELECT

## Slide 31: Via SELECT type
OR
SELECT

## Slide 32: Incomplete BASE-CC
Must be “completed” to create a valid set
  choices for completing them!
CIS/2 defines rules for satisfy dangling relationships by adding in selected BASE-CCs
  rules derived (by hand) from the EXPRESS for each type of dangling reference

## Slide 33: CC Changes
CIS/2  to CIS/2 Publication

## Slide 34: Role of CCs
Primary role: Conformance Testing
However, also serve important practical roles in:
  specifying a translator
  describing a translator
  predicting what data exchange is possible

## Slide 35: No Easy Solution
CCs always recognised as the single most difficult area:
  wide scope of the LPM
  data exchange between dissimilar applications
  no ready-made solution (STEP or IAI)
Key to industrial deployment of the LPM

## Slide 36: Why Change from CIS/2 ?
Rigorous pre-defined “building-block” approach
  allowed any conceivable CC combination to be created
Envisaged that “industry” would determine which CC combinations would be used
  organic evolution
  but how to start?

## Slide 37: Why Change from CIS/2 ?
Some reviewers found the concept of incomplete BASE-CCs difficult
As documented, did not allow fully for the constraining effect of the WHERE rules:
  require some BASE-CCs to be used in combination
  reducing the effective number of BASE-CCs (and thus their incompleteness)

## Slide 38: Why Change from CIS/2 ?
LPM/5 has since been revised
  the number of entities has increased
  implying still more BASE-CCs
  super/sub-type trees simplified (less ORs)
  implying many less incomplete BASE-CCs
Approach involving less “permutations” required

## Slide 39: Key Changes
Fewer pre-defined CCs
  more will be added as needed
  none based-on the generic STEP entities
All CCs defined as completed
Each defined by a “short form” schema
  with an Excel spreadsheet to specify which entities are in each CC

## Slide 40: Why Complete CC Now?
Changes to the structure of LPM/5
  fewer ANDOR constructs
  more associative entities
Impact of WHERE rules
Still some cases where there is a choice over which entity to include
  engineering judgement applied to decide which

## Slide 41: Impact
More pragmatic evolutionary approach
  simpler to understand
EXPRESS centric approach
  use STEP toolkit to generate “long form” schema for each CC (and CC combination)
Specific subset schema
  focus on the relevant entities
  role in conformance testing

## Slide 42: Impact
A significant repackaging of the  approach
  offers significant benefits
The underlying industrial/commercial issues remain:
  which CC (and CC combinations) to implement
  need for compatible choices
  desirability of evolutionary convergence (plus innovation)

## Slide 43: New CCs
Typically built round a base entity
Identified by a reference number: CC123
Spreadsheet specifies which entities are included in which CC
Each also defined by a “short form” schema
  specifies which types, entities, functions and rules are included from the full schema

## Slide 44: CC Short form definition
  SCHEMA LPM5_CC123;
  USE FROM STRUCTURAL_FRAME_SCHEMA (base_entity);
  REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (list of types);
  REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (list of entities);
  REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (list of functions);
  REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (list of rules);
  END_SCHEMA;

## Slide 45: CC Short form definition
SCHEMA LPM5_CC001; -- date_and_time
USE FROM STRUCTURAL_FRAME_SCHEMA (date_and_time); -- Base Entity
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA ( -- Entites
calendar_date,
coordinated_universal_time_offset,
date, local_time);
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA ( -- Types
ahead_or_behind,
day_in_month_number,
hour_in_day,
minute_in_hour,
month_in_year_number,
second_in_minute, year_number);
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA ( -- Functions
leap_year,
valid_calendar_date, valid_time);
END_SCHEMA;

## Slide 46: Schema Interfacing
Imports entity definitions from one schema to another
Short form (incomplete) Long Form (complete)
An item explicitly imported into a schema will implicitly reference other items it needs
  good modelling practice to explicitly import all required definitions

## Slide 47: Schema Interfacing
USE FROM schema (items);
  yields first-class items (can have instances independent of being used by some other entity
REFERENCE FROM schema (items);
  yields second-class items (can have instances only if referenced by another instance)
Items may be:
  entities, types, functions, rules

## Slide 48: Definition of CCs
CC001
CC099
CC100
CC999
STRUCTURAL FRAME
SCHEMA
Generic
Classes
Specific
Classes
Data
Management
Classes

## Slide 49: Generic Classes
CC001 to CC099
Smaller CCs that are used only as building blocks in the definition of other CCs
Initially about 30 will be specified

## Slide 50: Data Management Classes
CC100 + CC101
Pre-defined CCs which, when combined with other Specific CCs, add-in data management conformance

## Slide 51: Specific Classes
CC102+
Pre-defined complete and coherent CCs which, alone or combined with other Specific CCs, provide a practically useful conformance unit.
Initially some 200 will be specified

## Slide 52: Conformance Specification
A translator is specified as being able to translate one, or more than one, Specific CC or Combination of Specific CCs:
  CC123
  CC123, CC124, CC125
  (CC111+CC222), CC333
The conformance of an application’s import and export translators may differ

## Slide 53: End