## Slide 1: AISC CIS/2 Workshop #2
Item 2.2
Proposed Design to Manufacture Conformance Class
Irvine, CA: June 1999 (rev 4)

## Slide 2: Objectives
To explain why the “D>M CC” has been assembled
To show how it has been assembled
To indicate what is included (and what is excluded)

## Slide 3: Context
Study
Implement
Map Data
Scope

## Slide 4: Why?

## Slide 5: Why D>M CC Proposed
Seen as being an “electronic framing plan”
Scope: That information which (should be) passed from the Designer to the Manufacture’s Detailer
  as-designed member sizes and grades
  member locations
  “sufficient” engineering (design) information

## Slide 6: Why D>M CC Proposed
Potentially a very useful CC
Plenty of scope for different views on:
  what information should be included
  how complex a structure to address
Workshop participants should be able to relate to this particular CC
  link to the practical workshop sessions using the Case Study

## Slide 7: Why D>M CC Proposed
Hope to elicit informative discussion on the boundaries of the CC
  workshop item 3.1 ...
  consensus on an initial CC in this area?
  potential focus for early CIS/2 implementations?

## Slide 8: Why D>M CC Proposed
Scope is non-trivial
But can be viewed in slices:
  Structural Modelling
  Loading
  Structural Response
  Decomposition

## Slide 9: How?

## Slide 10: How D>M CC Assembled
Started with a review of CIS/1 DEP1+DEP2
  similar in scope (and quite widely implemented)
  identified a number of key LPM/5 entities that must be included
However, LPM/5 has the potential to address very complex structures
  where to pitch on the entity subtype structures?

## Slide 11: How D>M CC Assembled
Instigated prior to the Generic CCs being fully defined
  some re-engineering to allow these to be demonstrated

## Slide 12: How D>M CC Assembled
Assembly staged:
  CC501 Structural Modelling
  CC502 plus Loading
  CC503 plus Structural Response
  CC504 plus Decomposition
The full set of unit related entities where included at the end

## Slide 13: Resulting Excel Spreadsheet

## Slide 14: Resulting Excel Spreadsheet

## Slide 15: How, in Greater Detail

## Slide 16: How D>M CC Assembled
Initial choice of Generic Classes
  adjusted later

## Slide 17: Build Short Form
USE FROM LPM5_CC003; -- cartesian_point

## Slide 18: How D>M CC Assembled
Initial choice of Generic Classes
  adjusted later
Started assembling CC501
  Structural Modelling
Inspected LPM/5.html to identify some key entities
  stay generic!
  built a skeletal short form ...

## Slide 19: Build CC501 Short Form
SCHEMA LPM5_CC501; -- Structural Modelling
USE FROM LPM5_CC003; -- cartesian_point
USE FROM STRUCTURAL_FRAME_SCHEMA (
analysis_model);
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (
boundary_condition,
element,
material, node, section_properties);
END_SCHEMA;

## Slide 20: CC Refinement Cycle
Short Form
Long Form
Generate
html
Generate
LPM/5 html
Compare
Refine

## Slide 21: CC Refinement Cycle
Short Form
Long Form
Generate
html
Generate
LPM/5 html
Compare
Refine
Add Entities
Refine Entities

## Slide 22: How D>M CC Assembled
Iterate round refinement cycle for CC501
Refine CC short form: add entities
  for long form completeness

## Slide 23: Refine Short Form: 1 of 2
SCHEMA LPM5_CC501; -- Structural Modelling
USE FROM LPM5_CC003; -- cartesian_point
USE FROM LPM5_CC009; -- global_unit_assigned_context
USE FROM STRUCTURAL_FRAME_SCHEMA (
analysis_model);
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (
boundary_condition,
element,
element_node_connectivity,

## Slide 24: Refine Short Form: 2 of 2
group_of_analysis_data,
material,
node,
release,
section_profile,
section_properties,
step_file);
END_SCHEMA;

## Slide 25: How D>M CC Assembled
Iterate round refinement cycle for CC501
Refine CC short form: add entities
  for long form completeness
Refine CC short form: refine the entities
  for long form functionality

## Slide 26: How D>M CC Assembled
Substitute more specialised entities:
  increases information payload
  may narrow the scope
With few subtypes
  reduces functionality
With all subtypes
  maintains functionality

## Slide 27: Refine Short Form
SCHEMA LPM5_CC501; -- Structural Modelling
USE FROM LPM5_CC003; -- cartesian_point
USE FROM LPM5_CC009; -- global_unit_assigned_context
USE FROM STRUCTURAL_FRAME_SCHEMA (
analysis_model);
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (
boundary_condition,
element,
element_node_connectivity,

## Slide 28: Refine CC Entity
Expresso: [Tools][Entity Graph]: analysis_model

## Slide 29: Refine CC Entity
ENTITY analysis_model
SUPERTYPE OF (ONEOF
(ANALYSIS_MODEL_2D,
ANALYSIS_MODEL_3D) ANDOR
ANALYSIS_MODEL_LOCATED ANDOR
ANALYSIS_MODEL_CHILD);
model_name : LABEL;
model_description : OPTIONAL TEXT;
model_type : FRAME_TYPE;
method_of_analysis : OPTIONAL ANALYSIS_METHOD;
coordinate_space_dimension : DIMENSION_COUNT;
INVERSE
component_elements : SET [1:?] OF ELEMENT
FOR parent_model;
component_nodes : SET [2:?] OF NODE
FOR parent_model;
END_ENTITY;

## Slide 30: Refine CC Entity
ENTITY analysis_model_2D
SUBTYPE OF (ANALYSIS_MODEL);
WHERE
WRA2 : SELF\ANALYSIS_MODEL.coordinate_space_dimension = 2;
WRA3 : (SELF\ANALYSIS_MODEL.model_type = PLANE_FRAME) OR
(SELF\ANALYSIS_MODEL.model_type = PLANE_TRUSS) OR
(SELF\ANALYSIS_MODEL.model_type = GRILLAGE);
END_ENTITY;
ENTITY analysis_model_3D
SUBTYPE OF (ANALYSIS_MODEL);
WHERE
WRA4 : SELF\ANALYSIS_MODEL.coordinate_space_dimension = 3;
WRA5 : (SELF\ANALYSIS_MODEL.model_type = SPACE_FRAME) OR
(SELF\ANALYSIS_MODEL.model_type = SPACE_TRUSS);
END_ENTITY;


## Slide 31: Refine CC Entity
ENTITY analysis_model_child
SUBTYPE OF (ANALYSIS_MODEL);
parent_model : ANALYSIS_MODEL;
WHERE
WRA6 : parent_model :<>: (SELF);
WRA7 : SELF\ANALYSIS_MODEL.coordinate_space_dimension <=
parent_model.coordinate_space_dimension;
END_ENTITY;
ENTITY analysis_model_located
SUBTYPE OF (ANALYSIS_MODEL);
model_coord_sys : COORD_SYSTEM;
WHERE
WRA8 : SELF\ANALYSIS_MODEL.coordinate_space_dimension <=
model_coord_sys.coord_system_dimensionality;
END_ENTITY;


## Slide 32: Refined Short Form
SCHEMA LPM5_CC501; -- Structural Modelling
USE FROM LPM5_CC003; -- cartesian_point
USE FROM LPM5_CC009; -- global_unit_assigned_context
USE FROM STRUCTURAL_FRAME_SCHEMA (
analysis_model_2D,
analysis_model_3D);
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (
boundary_condition,
element,
element_node_connectivity,

## Slide 33: Refine Short Form
SCHEMA LPM5_CC501; -- Structural Modelling
USE FROM LPM5_CC003; -- cartesian_point
USE FROM LPM5_CC009; -- global_unit_assigned_context
USE FROM STRUCTURAL_FRAME_SCHEMA (
analysis_model_2D,
analysis_model_3D);
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (
boundary_condition,
element,
element_node_connectivity,

## Slide 34: Refine CC Entity
ENTITY element
SUPERTYPE OF (ONEOF
(ELEMENT_VOLUME,
ELEMENT_SURFACE,
ELEMENT_CURVE,
ELEMENT_POINT) ANDOR
ELEMENT_WITH_MATERIAL);
element_name : LABEL;
element_description : OPTIONAL TEXT;
parent_model : ANALYSIS_MODEL;
element_dimensionality : INTEGER;
element_subdivision : OPTIONAL INTEGER;
INVERSE
connectivity : SET [1:?] OF ELEMENT_NODE_CONNECTIVITY FOR
UNIQUE connecting_element;
URE1 : element_name, parent_model;
WHERE
WRE2 : element_dimensionality <= parent_model.coordinate_space_
END_ENTITY; dimension;

## Slide 35: Refine CC Entity
ENTITY element_curve
SUPERTYPE OF (ONEOF(ELEMENT_CURVE_SIMPLE,
ELEMENT_CURVE_COMPLEX))
SUBTYPE OF (ELEMENT);
WHERE
WRE3 : SELF\ELEMENT.element_dimensionality = 1;
END_ENTITY;
ENTITY element_curve_simple
SUBTYPE OF (ELEMENT_CURVE);
cross_section : SECTION_PROFILE;
element_orientation : OPTIONAL PLANE_ANGLE_MEASURE_WITH_UNIT;
END_ENTITY;
ENTITY element_with_material
SUBTYPE OF (ELEMENT);
material_definition : MATERIAL;
END_ENTITY;

## Slide 36: Refined Short Form
SCHEMA LPM5_CC501; -- Structural Modelling
USE FROM LPM5_CC003; -- cartesian_point
USE FROM LPM5_CC009; -- global_unit_assigned_context
USE FROM STRUCTURAL_FRAME_SCHEMA (
analysis_model_2D,
analysis_model_3D);
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (
boundary_condition,
element_curve_simple,
element_with_material,

## Slide 37: Functionality Constrained

## Slide 38: The CC501 Short Form
SCHEMA SCHEMA LPM5_CC501; -- Structural Modelling
USE FROM LPM5_CC003; -- cartesian_point
USE FROM LPM5_CC009; -- global_unit_assigned_context
USE FROM STRUCTURAL_FRAME_SCHEMA (
analysis_model_2D,
analysis_model_3D);
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (
analysis_method_static,
functionality constrained

## Slide 39: The CC501 Short Form
boundary_condition_logical,
boundary_condition_skewed,
boundary_condition_spring_linear,
element_curve_simple,
element_eccentricity,
element_node_connectivity,
element_with_material,
group_of_analysis_data,
material_elasticity,
material_isotropic,
node,
functionality constrained
functionality constrained
additional entity

## Slide 40: The CC501 Short Form
release_logical,
release_spring_linear,
section_profile_angle,
section_profile_channel,
section_profile_circle_hollow,
section_profile_i_type,
section_profile_rectangle_hollow,
section_profile_t_type,
section_properties,
step_file);
END_SCHEMA;
functionality constrained
basic functionality retained

## Slide 41: Repeat for CC502
CC501 used as the starting point to built a skeletal short form

## Slide 42: Build CC502 Short Form
SCHEMA SCHEMA LPM5_CC502; -- + Loading
USE FROM LPM5_CC003; -- cartesian_point
USE FROM LPM5_CC009; -- global_unit_assigned_context
USE FROM STRUCTURAL_FRAME_SCHEMA ( -- "Structural Modelling"
analysis_model_2D,
analysis_model_3D);
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (
list-of-entities);
USE FROM STRUCTURAL_FRAME_SCHEMA ( -- "Loading"
loading_combination);
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (
applied_load,
load_element,
load_case);
END_SCHEMA;

## Slide 43: Repeat for CC502
CC501 used as the starting point to built a skeletal short form
Iterate round the CC refinement cycle
  add and refine entities

## Slide 44: The CC502 Short Form
SCHEMA SCHEMA LPM5_CC502; -- + Loading
…
USE FROM STRUCTURAL_FRAME_SCHEMA ( -- "Loading"
loading_combination);
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (
applied_load_static_displacement,
applied_load_static_force,
load_element_concentrated,
load_element_distributed_curve_line,
load_element_thermal,
load_node,
load_case,
load_combination_occurrence);
END_SCHEMA;

## Slide 45: Complete the Task
CC502 used to built CC503
  Structural Response
CC503 used to built CC504
  Decomposition
CC504 checked out
  CC029 (all units) added in
  CC501, CC502 and CC503 regenerated from CC504

## Slide 46: The CC503 Short Form
SCHEMA SCHEMA LPM5_CC503; -- + Structural Response
…
USE FROM STRUCTURAL_FRAME_SCHEMA ( -- "Structural Response"
analysis_results_set_combined);
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (
analysis_results_set_envelope,
analysis_result_element_curve,
analysis_result_node,
reaction_displacement,
reaction_equilibrium,
reaction_force);
END_SCHEMA;

## Slide 47: The CC504 Short Form
SCHEMA LPM5_CC504; -- Design to Manufacture
USE FROM LPM5_CC029; -- all units
USE FROM LPM5_CC003; -- cartesian_point
USE FROM LPM5_CC009; -- global_unit_assigned_context
USE FROM STRUCTURAL_FRAME_SCHEMA ( -- "Structural Modelling"
...
USE FROM STRUCTURAL_FRAME_SCHEMA ( -- "Loading"
...
USE FROM STRUCTURAL_FRAME_SCHEMA ( -- "Structural Response"
...

## Slide 48: The CC504 Short Form
USE FROM STRUCTURAL_FRAME_SCHEMA (
-- "Decomposition"
assembly_design_structural_frame);
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA (
assembly_design_child,
assembly_design_structural_member_linear,
assembly_design_structural_connection_internal,
assembly_design_structural_connection_external,
assembly_map,
assembly_relationship,
design_criteria,
design_part,

## Slide 49
Functionality Constrained
ASSEMBLY





## Slide 50: The CC504 Short Form
design_result_connection,
design_result_member,
effective_buckling_length,
functional_role,
group_of_design_data,
restraint_logical,
restraint_spring);
END_SCHEMA;

## Slide 51: What is Included?

## Slide 52: Proposed Scope of each CC
Please study distributed copy of spreadsheet
Will also distribute a structured list of the entities excluded from CC504
  to be reviewed in item 3.1

## Slide 53: End