## Slide 1: AISC CIS/2 Workshop #2
Item 2.3
Introduction to the NIST Expresso Tool
Irvine, CA: June 1999 (rev 2)

## Slide 2: Objectives
To outline the potential of Expresso
To enable the participants to make use of Expresso during the Workshop Sessions

## Slide 3: Context
Study
Implement
Map Data
Scope

## Slide 4: The Expresso Tool
Developed by Peter Denno of NIST
Available at no cost
  download from web site
  www.mel.nist.gov/msidstaff/denno/nist-expresso.html
Windows 95 and NT
  relatively stable and robust
  supported (?)

## Slide 5: Expresso Loading!

## Slide 6: Expresso will ...
Parse an EXPRESS model
  and detect (well) the presence of errors
Walk over the loaded model
  allowing inspection of the EXPRESS
  graph EXPRESS subtype trees
Read and write Part 21 files
  supports the validation and creation of data
Perform EXPRESS-X mapping

## Slide 7: Expresso will not ...
Replace a (commercial) STEP toolkit for
  major EXPRESS model development
  translator development
Limitations ...
  slow and hungry (implemented in lisp)
  limited model error diagnostics
  no API for programming
  EMACS style EXPRESS editor
  little documentation

## Slide 8: Relevance of Expresso
Inspection and viewing existing EXPRESS models
  LPM/5
  CC long forms
Creation, editing and validation of Part 21 files
But not the generation of CC long forms
  slow, and not sufficiently robust (??)

## Slide 9: File menu
[Load EXPRESS file]
  translated with high fidelity into internal objects
  error reporting is not very informative
  slow
[Save Translated schema]
  as .lsp file for quicker reload
[Load Part 21 file]
[Save Part 21 file]

## Slide 10: File menu

## Slide 11: Tools menu
[Data Creator]
  view and create entity instances: Good!
[Data Viewer]
  EXPRESS-X views
[EXPRESS Editor]
  dynamically update schema, add PRINTS!
  EMACS
[Entity Graph]
  view and graph entities: Good!

## Slide 12: Tools menu

## Slide 13: Data menu
[Run All Rules]
  full validate all the data
[Validation Control Panel]
  selective data validation
[Validation Statistics]
[Show Instances]
  list the data as part 21 file

## Slide 14: Data menu

## Slide 15: EXPRESS-X
Schema
One
Schema
Two
Express-X
Mapping
Data mapping

## Slide 16: Options menu
[Preferences …]
  dialog box
The only command!

## Slide 17: Options dialog

## Slide 18: Options dialog

## Slide 19: Options dialog

## Slide 20: Options dialog

## Slide 21: Help menu
[Info]
  version number
[Patches]
  that are loaded
[Report a bug]
  by email
  may send a patch
No online manual!

## Slide 22: Expresso Summary
Parsed
EXPRESS
model
Load
Model
Edit Model
View Model
Translated
Schema
Data Instances
Load
Part 21
Write
Part 21
Edit Data
Validate Data

## Slide 23: Brief Demonstration
4000 mm
3000 mm
A
B
C
D

## Slide 24: End