## Slide 1: CIS/2 Implementation Workshop III, 3-7 April 2000, Ascot
Session 1.8
Workshop
The Case Study - Introduction
Dr A.J. Crowley
CIM steel

## Slide 2: Intention of the Case Study
The Case Study is intended as practical, simple problem that will serve as the theme for the entire workshop.
  It should help you relate everything you learn during this workshop to your translator development.
By participating in the Workshop Sessions based on the Case Study exercise, you will become familiar with CIS/2

## Slide 3: Objectives of the Case Study
To enable you to identify limitations of your application
To assess the scope of data you may need to exchange to satisfy the needs of end-users.
  Note - end-users may be exchanging data at any point in the supply chain.

## Slide 4: Project Information
Engineers of Record
  Mark Holland (Lead Engineer) and
  Steven Hamburg (Assistant Engineer)
Engineering Consulting Company
  Hamburg Consulting, Inc.
Fabricator
  Paxton & Vierling Steel
Architect
  Carlos Aguera Aesthetics, LLC
Owner
  Watson, Crowley, Hamburg & Holland Enterprises, Inc.

## Slide 5: Project Information
Purpose of Structure
  To support two coffee extractors for a food & beverage facility
Location
  Miami, FL
Wind condition
  must be designed for 100-year hurricane.

## Slide 6: Geometry of the Frame
  The frame consists of a single story, one bay in width by two bays in length.
  The distance from the bottom of the base plate to the top of the beam flanges (T.O.S) is 25 feet.
  The length of the structure runs East / West.
  The single width of the structure runs North / South.
  The width of the structure is 25 feet (centre-to-centre of girders).
  The length of the structure consists of two bays, each 30 feet in length (centre-to-centre of girders).
  There are two in-fill beams in each bay running North / South. These in-fill beams are located at 10 feet on centre.

## Slide 7: Bracing
Horizontal cross bracing
  is to be used in both bays using structural tees with stem pointing downward.
    The horizontal bracing in the western-most bay will start at the Southwest corner and run to the north-eastern corner.
    The horizontal bracing in the eastern-most bay will start at the Northwest corner and run to the south-eastern corner.
Vertical
  "X" braced using double angles.
    The work points for the bracing is the gravity axis of all connected elements except the angle bracing. The work line will be the angles' gage line.

## Slide 8: Connections (1)
Each 25 foot spanning bay (girder running North / South) makes a rigid connection to the supporting column.
The beam end connection is designed to fully develop the member's capacity.
The brace end connections will be designed to develop ½ of the member's axial capacity or as required by the applied loads.

## Slide 9: Connections (2)
The horizontal bracing members are to be bolted to the in-fill beams as they run under the in-fill beams using filler plates as necessary. The horizontal bracing members are connected to the in-fill beams framing at the column locations with ½" thick gusset plates and (4) four A325 ¾" bolts.
The in-fill beams' end connections are to be designed to develop ½ of the member's allowable bending capacity. The connections shall consist of using shear tabs.
The column bases will not be designed to transfer any moment.

## Slide 10: Loading Conditions
Apply
  1.25 KLF wind load to each girder (one load case for each direction).
  100 PSF live load over entire 60 ft x 25 ft plan area of the structure.
  50 PSF dead load to each in-fill beam.
Analyse structure to include self weight of all structural members in DL loading condition for following load cases and combinations
  DL only
  DL + LL
  DL + LL + WL (North Direction)

## Slide 11: Frame Member Sizes
All columns are W27x194 members. The web is oriented running North / South.
The Girders running North / South (the 25 foot span) are W24x68 members.
The Girders running East / West (the 30 foot span) are W21x44 members.
The in-fill beams are W16x36 members.
All angle braces are double angles, L8x8x¾.
The horizontal bracing members are WT6x11 structural tees.

## Slide 12: Added Conditions
All main members are made from A572 Grade 50.
All connection material is made from A36 material.
The angle braces are made from A36 material.
All bolts are to be A325 ¾" or 1".
All steel will be painted using a Zinc-rich paint.

## Slide 13
S
E
W
N
W27 x 194
W27 x 194
W27 x 194
W27 x 194
W27 x 194
W21 x 44
W21 x 44
W21 x 44
W21 x 44
W27 x 68
W27 x 68
W27 x 68
W16 x 36
W16 x 36
W16 x 36
WT6 x 11
W16 x 36
WT6 x 11
W27 x 194
25'
30'
10'
30'
10'
10'
10'
10'
10'
Framing plan

## Slide 14
30'
30'
W27 x 194
W27 x 194
W27 x 194
2 x L8 x 8 x 3/4
2 x L8 x 8 x 3/4
2 x L8 x 8 x 3/4
2 x L8 x 8 x 3/4
Elevation