## Slide 1: CIS/2 Implementation Workshop III, 3-7 April 2000, Ascot
Session 2.4
LPM/5: Basic Principles
Dr A.J. Crowley
CIM steel

## Slide 2
CIM steel
CIS/2
CCs
STEP
Product
Modelling
LPM/5

## Slide 3
The LPM Concept
Requirements of LPM/5
Fundamental Principles
Key Aspects
LPM/5

## Slide 4: The LPM Concept
Logical
  It exists at the logical level, as opposed to the application or physical level.
Product
  the product we are concerned with is a building-type structural steel frame.
Model
  It is a limited representation of some aspect of the real world.

## Slide 5: The Logical Product Model
The LPM defines a logical structure for data in terms of:
  entities (or things),
  attributes (or characteristics),
  and relationships between entities.
part_prismatic_
simple_curved
axis_definition
curve

## Slide 6: LPM/5
A formal definition of how engineering information should be systematically structured for data exchange
  Intended to cover all types of engineering information associated with a steel frames
Graphically presented in EXPRESS-G
Formally specified in EXPRESS
  Short form (containing definitions of specialized constructs)
  Long form (implementation schema)
The key component of the CIS

## Slide 7: LPM/5: Short Form
LPM/5 EXPRESS Schema ‘short form’
  provides illustrated descriptions of LPM/5 entities
    with their attributes & formal propositions (rules & constraints),
    together with references to STEP resources.
    It does not repeat the definitions of those STEP entities that have been used from the Generic Resources.
  Contains
    Schema Declaration
    Schema Interface Declarations
    Type Declarations - for Types specific to LPM/5
    Entity Declarations - for Entities specific to LPM/5
    Rule Declarations
    Function Declarations

## Slide 8: LPM/5 Long Form
LPM/5 EXPRESS Schema ‘long form’
  one single schema
  with all the inter-schema references resolved.
  contains no definitions or explanations,
  merely an EXPRESS long form listing of the CIS/2 implementation schema.
  Contains
    Schema Declaration - STRUCTURAL_FRAME_SCHEMA
    Type Declarations - for all (Generic & Specific) Types
    Entity Declarations - for all (Generic & Specific) Entities
    Rule Declarations - for all (imported) Rules
    Function Declarations - for all (imported) Functions

## Slide 9: Fundamental Principles of LPM/5
CIS/2 presents LPM/5 as both:
  Short form EXPRESS schema and
  Long form EXPRESS schema
LPM/5 uses STEP ‘Generic Resources’ wherever possible
  ISO 10303-41: 1994 - date, person, measures and units
  ISO 10303-42: 1994 - explicit geometry and topology
  ISO 10303-43: 1994
  ISO 10303-44: 1994
LPM/5 contains 3 “Views” of the structure
  Analysis, Design, Manufacturing (Physical)

## Slide 10: LPM/5 Short Form: Details
Divided into 17 ‘subject areas’:
  1. Decomposition
  2. Project Definition
  3. Structural Modelling
  4. Loading
  5. Structural Response
  6. Parts
  7. Features
  8. Joint Systems
  9. Materials
  10. Location
  11. Grouping
  12. Geometry
  13. Units & Measures
  14. Items References
  15. Product Definition
  16. Process Definition
  17. Data Management

## Slide 11: LPM/5: The 3 ‘Views’
Analysis
Design
Manufacturing
LPM/5
Mapping

## Slide 12: Analysis - Design - Manufacturing
(ABS)
assembly
assembly_design
assembly_manufacturing
1
analysis_model
element
node
located_joint_system
located_part
design_part
design_joint_system

## Slide 13: Key Aspects of LPM/5
Data management constructs
  separating data from meta-data
Product item references
  standard, proprietary, library
Inclusion of implicit & explicit geometry
  simple & complex
Use of ANDOR SUPERTYPEs
Use of ‘associative entities’
  the ‘level discriminator’
Units and measures
  Global and individual

## Slide 14: Naming Convention
Entities listed in alphabetical order
    ENTITY action;
    ...
    ...
    ENTITY zone_of_structure
Entities given full names
  abbreviations avoided
  name reflects inheritance
    e.g. assembly_design_structural_member_linear

## Slide 15: Data Management in CIS/2
LPM/5 separates data from ‘meta-data’,
  This ‘meta-data’ includes some or all of the following:
  The unique identifier for the item.
  The person who created / modified / deleted the data.
  The date when it was created / modified / deleted.
  Whether the data was new or old data that had been modified.
  Whether the data has been approved or not.

## Slide 16: Data Management via CIS/2
In CIS/2, data management is considered to be the process of assigning meta-data to data.
  ‘Data Management Conformant’ (DMC) applications produce ‘managed data’
    Each item of data is given a unique id and placed in a data set
  ‘Non-DMC applications’ produce ‘unmanaged data’
Using a DMC application,
  ‘unmanaged data’ may be mapped onto meta data
  to become ‘managed data’
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: Product Identifiers in CIS/2
4 classes of product item are defined
  Standard Items.
  Proprietary Items
  Library Items
    information exchanged by being “passed-by-reference” rather than being “passed by attribute value”.
  Non-standard Items

## Slide 18: Assigning Item References
assigned_reference
structural_frame_item
item_reference_assigned
identifier
ref
item_reference _proprietary
item_reference _standard
(ABS)
item_ref_source
item_reference
1
1
item_ref_source _standard
item_ref_source _proprietary
source
source
assigned_to_item

## Slide 19: Standard Items
item_reference _standard
item_ref_source _standard
source
(INV) standard_items S[1:?]
label
standardization_organization
name_of_standard
REAL
year_number
STRING
year_of_standard
label
STRING
version_of_standard
label

## Slide 20: Proprietary Items
item_reference _proprietary
item_ref_source _proprietary
source
(INV) proprietary_items S[1:?]
label
manufacturers_name
organization
manufacturers_range
REAL
year_number
STRING
year_of_range
label
STRING
version_of_range
identifier
label
text
id
name
description

## Slide 21
ISO-10303-21;
HEADER;
FILE_DESCRIPTION(('STEP US FLAVOUR'), '1');
FILE_NAME('Step US Flavour', '11-05-1998', (‘’), (‘’), ‘’,’’,’’);
FILE_SCHEMA(('STRUCTURAL_FRAME_SCHEMA'));
ENDSEC;
DATA;
#3000=GROUP(‘US Flavour list’, ‘List of item references in accordance with
ASTM standards’);
#3001=FLAVOUR(#3000, (#1, #3, ….. , #2354, #2355)):
#1 = ITEM_REFERENCE_STANDARD (‘W1100X424’, #2);
#2 = ITEM_REF_SOURCE_STANDARD (‘ASTM’, ‘ASTM_A6M’, 1994, $);
#3 = ITEM_REFERENCE_STANDARD (‘W1100X369’, #2);
#4 = ITEM_REFERENCE_STANDARD (‘W1100X333’, #2);
#5 = ITEM_REFERENCE_STANDARD (‘W1100X295’, #2);
#2354 = ITEM_REFERENCE_STANDARD (‘M30_TYPE1’, #2349);
#2355 = ITEM_REFERENCE_STANDARD (‘M36_TYPE1’, #2349);
ENDSEC;
END-ISO-10303-21;
Physical File (extract)

## Slide 22
#201 = SECTION_PROFILE_I_TYPE (1, 'W14x16x500', 'Wide flange beam to ASTM', 'Plastic', $, #202, #203, #204, #205, #206);
#202 = POSITIVE_LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(498.0), #1021);
#203 = POSITIVE_ LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(432.0), #1021);
#204 = POSITIVE_ LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(55.6), #1021);
#205 = POSITIVE_ LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(88.9), #1021);
#206 = POSITIVE_ LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(280.0), #1021);
#1021 = (LENGTH_UNIT()NAMED_UNIT(*)SI_UNIT(.MILLI.,.METRE.));
Standard item - passed by attribute value (1)

## Slide 23
#201 = SECTION_PROFILE_I_TYPE (1, 'W14x16x500', 'Wide flange beam to ASTM', 'Plastic', $, #202, #203, #204, #205, #206);
#215 = SECTION_PROPERTIES (#201, $, #216, #217, #218, $, $, $, $, $, $, $, #219, #220, $, $, $, $, $);
#216 = INERTIA_MEASURE_WITH_UNIT (INERTIA_MEASURE(342200.0), #1151);
#217 = INERTIA_MEASURE_WITH_UNIT (INERTIA_MEASURE(120000.0), #1151);
#218 = AREA_MEASURE_WITH_UNIT (AREA_MEASURE(950.0), #1161);
#219 = MODULUS_MEASURE_WITH_UNIT (MODULUS_MEASURE(17180.0), #1157);
#220 = MODULUS_MEASURE_WITH_UNIT (MODULUS_MEASURE(8558.0), #1157);
#1149 = (LENGTH_UNIT()NAMED_UNIT(*)SI_UNIT(.CENTI.,.METRE.));
#1150 = DERIVED_UNIT_ELEMENT (#1149, 4.0);
#1151 = INERTIA_UNIT ((#1150));
Standard item - passed by attribute value (2)

## Slide 24
#301 = ITEM_REFERENCE_STANDARD ('W1100X424', #302);
#302 = ITEM_REF_SOURCE_STANDARD('ASTM', 'ASTM_A6M', 1994, $);
#303 = SECTION_PROFILE (2, 'W', 'Wide flange beam to ASTM’, 'Plastic', $);
#304 = ITEM_REFERENCE_ASSIGNED (#301, #303));
Standard item - passed by reference

## Slide 25: Proprietary item - passed by reference
#901 = ITEM_REFERENCE_PROPRIETARY (’1_12513', #902);
#902 = ITEM_REF_SOURCE_PROPRIETARY (#903, Zeta Sections for Purlins and Cladding Rails , 1996, $);
#903 = ORGANIZATION (‘AYRSHIRE_DAV’, ‘Ayrshire Metal Products (Daventry) Ltd’, ‘Cold formed metal products manufacturer’);
#904 = SECTION_PROFILE(2, ’Zeta',’Cold formed purlin section’, ’Slender', $);
#905 = ITEM_REFERENCE_ASSIGNED (#901, #904);

## Slide 26: Implicit and Explicit Geometry
CIS/1 contained no provision for explicit geometry
  all geometry defined implicitly using parameters
CIS/2 incorporates the whole of STEP Part 42
  all the EXPRESS constructs for geometry and topology included in LPM/5
  used as resources as required

## Slide 27: ‘Simple’ & ‘Complex’ Objects
In LPM/5 Objects are categorized (through subtyping) as either simple or complex
  depending on the definition of the shape of object
Simple Objects
  have their shape defined implicitly through parameters
Complex Objects
  have their shape defined explicitly using constructs from STEP Part 42

## Slide 28: ‘Simple’ & ‘Complex’ Objects
ENTITY object
SUPERTYPE OF (ONE OF(object_simple, object_complex));
END_ENTITY;
ENTITY object_simple
SUBTYPE OF (object);
length : length_measure_with_unit;
depth : length_measure_with_unit;
width : length_measure_with_unit;
END_ENTITY;
ENTITY object_complex
SUBTYPE OF (object);
shape : shape_representation;
END_ENTITY;

## Slide 29: ANDOR SUPERTYPEs
structural_frame_product
material_definition
part
coating
fastener
1
structural_frame_product
_with_material
ANDOR
material
(ABS)
assembly

## Slide 30: ‘Associative entities’
joined_parts S [0:?]
(INV) required_joints S [0:?]
locations S[0:?]
assembly_manufacturing
part
parent_assemblies S [0:?]
joint_system
parent_assemblies S [0:?]
coord_system
locations S[0:?]
parent_coord_system

## Slide 31: ‘The Level Discriminator’
located_part_joint
parent_assembly
located_joint_system
descriptive_joint_system
located_part
descriptive_part
(ABS)
located_item
location
1
coord_system
assembly_manufacturing
part
parent_assembly
joint_system
logically_joined_parts S[2:2]
required_joints S[1:?]
coord_system_child
parent_coord_system

## Slide 32: Representations
Two points p1 (0, 0, 0) and p2 (1, 1, 1)
  How far apart? (3?)

## Slide 33: Representation of shape
geometric_ representation_context
coordinate_space _dimension
representation
name
representation_item
context_of_items
representation_context
context_type
context_identifier
items
S[1:?]
shape_representation
name
geometric_ representation_item
Every representation item needs to be placed into its context

## Slide 34: Geometric representation items
curve
point
geometric_ representation_item
1
name
representation_item
cartesian_point
coordinates L[1:3]
line
pnt
vector
direction
orientation
length_measure
magnitude
dir
REAL
direction_ratios
L[1:3]

## Slide 35: Units & Measures
Constructs for units and measures have been taken from STEP Part 41
  Using the ‘interpreted route’
Units are specified either Globally or individually
  In general, constructs taken from STEP have their units assigned globally
  Constructs developed for LPM/5 have their units assigned individually

## Slide 36: Globally assigned units
geometric_ representation_context
coordinate_space _dimension
representation_context
context_type
context_identifier
global_unit_ assigned_context
ANDOR
unit
derived_unit
named_unit
units S[1:?]
unit
derived_unit_element
REAL
exponent
elements
S[1:?]
dimensions

## Slide 37: Named units
length_unit
mass_unit
time_unit
context_dependent_unit
name
conversion_based_unit
name
dimensions
dimensional_exponents
si_unit
name
si_unit_name
si_prefix
prefix
measure_with_unit
conversion_factor
named_unit
1
1
ANDOR

## Slide 38: Sample physical file
#1 = CARTESIAN_POINT ('node point 1', (0.0, 0.0, 0.0));
#2 = CARTESIAN_POINT ('node point 2', (0.0, 0.0, 5000.0));
...
#501 = REPRESENTATION ('nodal points', (#1, #2, #3, #4, #5, #6), #502);
#502 = (GEOMETRIC_REPRESENTATION_CONTEXT(3) GLOBAL_UNIT_ASSIGNED_CONTEXT((#1021)) REPRESENTATION_CONTEXT('context for nodal points', 'units for coordinates'));
...
/* Length Unit (mm) */
#1021 = (LENGTH_UNIT()NAMED_UNIT(*)SI_UNIT(.MILLI.,.METRE.));
/* Force Unit (KN) */
#1031 = (FORCE_UNIT()NAMED_UNIT(*)SI_UNIT(.KILO.,.NEWTON.));
/* Plane Angle Unit (radian) */
#1033 = (NAMED_UNIT(*)PLANE_ANGLE_UNIT()SI_UNIT($,.RADIAN.));

## Slide 39: Derived units
/* Inertia Unit (cm4) */
#1149 = (LENGTH_UNIT()NAMED_UNIT(*)SI_UNIT(.CENTI.,.METRE.));
#1150 = DERIVED_UNIT_ELEMENT (#1149, 4.0);
#1151 = INERTIA_UNIT ((#1150));
/* Modulus Unit (cm3) */
#1156 = DERIVED_UNIT_ELEMENT (#1149, 3.0);
#1157 = MODULUS_UNIT ((#1156));
/* Area Unit (cm2) */
#1161 = (AREA_UNIT()CONVERSION_BASED_UNIT('square centimetre', #1162)NAMED_UNIT (#1165));
#1162 = MEASURE_WITH_UNIT (1.0, #1163);
#1163 = DERIVED_UNIT ((#1164));
#1164 = DERIVED_UNIT_ELEMENT (#1149, 2.0);
#1165 = DIMENSIONAL_EXPONENTS (2.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0);

## Slide 40: Explicit units
measure_with_unit
unit
derived_unit
named_unit
unit_component
measure_value
value_component
length_measure _with_unit
mass_measure _with_unit
time_measure _with_unit
1
REAL
length_unit
mass_unit
time_unit
1
length_measure
mass_measure
time_measure
WHERE

## Slide 41: Explicit units in use
section_profile_circle
section_profile_circle_hollow
measure_with_unit
external_radius
positive_length_ measure_with_unit
wall_thickness
measure_value
value_component
length_measure
unit
named_unit
unit_component
length_unit
REAL
positive_length_measure

## Slide 42: Sample physical file
#201 = SECTION_PROFILE_CIRCLE_HOLLOW (’CHS273x10', 1, ’Circular Hollow Section beam to EN10210, 'Plastic', $, #202, #203);
#202 = POSITIVE_LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(136.5), #1021);
#203 = POSITIVE_ LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(10.0), #1021);
...
/* Length Unit (mm) */
#1021 = (LENGTH_UNIT()NAMED_UNIT(*)SI_UNIT(.MILLI.,.METRE.));

## Slide 43: LPM/5: Location
LPM/5

## Slide 44
Structure
Coord System
Located Feature
Located Part
Loc Joint System
Setting Out Point (Reference Point)
Site Coord System
Structure Coord System
Site
Assembly
Notes: Introduction
As explained in Part 4B Chapter 10 of CIS/1, the use of Coordinate Systems in the LPM is essential. Everything in the Composition and Decomposition procedures is located by coordinate system. The CIS uses a right handed Cartesian coordinate system with clockwise rotation taken as positive.
Features are located with respect to the part which they modify. Parts and Joint Systems are located with respect to the Assembly to which they belong. Each assembly has its own coordinate system. Similarly, each located part, joint system and feature has its own coordinate system.
Each Located Part and Located Joint System coordinate system, must be located within a parent coordinate system; i.e. the low level assembly (STRUC_MEMBER) coordinate system. This is done by using the origin attribute in its instance of COORD_SYSTEM (to shift the origin laterally), and the associated instance of TRANSFORMATION (to rotate the axes). (see diagrams below)

## Slide 45: Located Items
located_part_joint
parent_assembly
located_joint_system
descriptive_joint_system
located_part
descriptive_part
(ABS)
located_item
location
1
coord_system
assembly_manufacturing
part
parent_assembly
joint_system
logically_joined_parts S[2:2]
required_joints S[1:?]
coord_system_child
parent_coord_system

## Slide 47: Coordinate systems
axes_definition
(ABS)
coord_system
coord_system _child
parent_coord_system
coord_system _cartesian_3D
placement
axis_2_placement_3d
coordinates L[1:3]
direction
origin
cartesian_point
length_measure
ref_direction
REAL
direction_ratios
L[1:3]
axis
(DER)
p L[3:3]

## Slide 48: Nested coordinate systems

## Slide 49: Transforming coordinates...
… from parent
… to child
… from child
… to parent

## Slide 50: Transformation for x-axis rotation

## Slide 51: Transformation for y-axis rotation

## Slide 52: Transformation for z-axis rotation

## Slide 53: Assigning the units for coords
geometric_ representation_context
representation
representation_item
context_of_items
representation_context
items S[1:?]
point
1
cartesian_point
coordinates L[1:3]
length_measure
REAL
ANDOR
unit
named_unit
global_unit_ assigned_context
units S[1:?]
geometric_ representation_item
length_unit
si_unit
name
si_unit_name
si_prefix
prefix

## Slide 54: Sample physical file - units
#1 = CARTESIAN_POINT (‘origin point 1', (0.0, 0.0, 0.0));
...
#501 = REPRESENTATION (‘coordinate system’, (#1, …, #201, #301, #302), #502);
#502 = (GEOMETRIC_REPRESENTATION_CONTEXT(3) GLOBAL_UNIT_ASSIGNED_CONTEXT((#1021)) REPRESENTATION_CONTEXT('context for coordinate system', 'units for coordinates'));
...
/* Length Unit (mm) */
#1021 = (LENGTH_UNIT()NAMED_UNIT(*)SI_UNIT(.MILLI.,.METRE.));

## Slide 55
axes_definition
(ABS)
coord_system
coord_system _cartesian
placement
axis_2_placement_3d
coordinates L[1:3]
direction
origin
cartesian_point
length_measure
ref_direction
REAL
direction_ratios
L[1:3]
axis
(DER)
p L[3:3]
representation
representation_item
items S[1:?]
1
geometric_ representation_item
point

## Slide 56: Sample physical file - coord system
#1 = CARTESIAN_POINT (‘origin point 1', (0.0, 0.0, 0.0));
...
#501 = REPRESENTATION (‘coordinate system’, (#1, …, #201, #301, #302), #502);
#502 = (GEOMETRIC_REPRESENTATION_CONTEXT(3) GLOBAL_UNIT_ASSIGNED_CONTEXT((#1021)) REPRESENTATION_CONTEXT('context for coord system, 'units for coordinates'));
...
/* Length Unit (mm) */
#1021 = (LENGTH_UNIT()NAMED_UNIT(*)SI_UNIT(.MILLI.,.METRE.));
#101 = COORD_SYSTEM_CARTESIAN (‘my coord system’, $, ‘right handed’, #201);
#201 = AXIS2_PLACEMENT_3D (‘test placement’, #1, #301, #302);
#301 = DIRECTION (‘z vector’, (0.0, 0.0, 1.0));
#302 = DIRECTION (‘x vector’, (1.0, 0.0, 0.0));

## Slide 57: Uncertainty
geometric_ representation_context
representation_context
context_type
context_identifier
global_unit_ assigned_context
ANDOR
unit
named_unit
units S[1:?]
REAL
length_unit
global_uncertainty_assigned_context
uncertainty_measure_with_unit
uncertainty S[1:?]
measure_with_unit
measure_value
value_component
length_measure
unit_component