## Slide 1: CIS/2 Implementation Workshop
Item 2.5
(1) The Translator Development Process
SCI: April 2000

## Slide 2: Objectives
To introduce the concept of a Data Exchange Translator
To provide a general introduction to the (CIS/2) Translator Development Process

## Slide 3: Some Basics

## Slide 4: Neutral Data Exchange
Engineering
Application
Software 1
IMPORT
EXPORT
Data
Exchange
File
Engineering
Application
Software 2
Data
Exchange
File

## Slide 5: CIS/2 Translators
Engineering
Application
Software
EXPORT
IMPORT
Standardised
CIS/2 Data
Structures
Native
Data
Neutral
Data
TRANSLATE
CIS/2 Specifies

## Slide 6: CIS/2 Translators
Native
Data
Neutral
Data
Governed by
application’s own
Data Structures
in Memory
in Database
in File

## Slide 7: CIS/2 Translators
Native
Data
Neutral
Data
Governed by
the CIS/2
Product Model
in CIS Exchange File
in Data Repository

## Slide 8: CIS/2 Product Model
“LPM/5”
  Logical Product Model version 5
Large and Complex information model!
  engineering and production of Steelwork
  formally defined in EXPRESS


## Slide 9: Express DDL
ENTITY boundary_condition_spring_linear
SUPERTYPE OF (boundary_condition_warping)
SUBTYPE OF (boundary_condition);
bc_x_displacement : OPTIONAL linear_stiffness_measure_with_unit;
bc_y_displacement : OPTIONAL linear_stiffness_measure_with_unit;
bc_z_displacement : OPTIONAL linear_stiffness_measure_with_unit;
bc_x_rotation : OPTIONAL rotational_stiffness_measure_with_unit;
bc_y_rotation : OPTIONAL rotational_stiffness_measure_with_unit;
bc_z_rotation : OPTIONAL rotational_stiffness_measure_with_unit;
WHERE
WRB10 : EXISTS (bc_x_displacement)
OR EXISTS (bc_y_displacement)
OR EXISTS (bc_z_displacement);
WRB11 : EXISTS (bc_x_rotation)
OR EXISTS (bc_y_rotation)
OR EXISTS (bc_z_rotation);
END_ENTITY;

## Slide 10: Scope of Translation
Potential data scope of
exporting application
Scope of existing data
Native
Data
Within Exporting
Application

## Slide 11: Scope of Translation

## Slide 12: Scope of Translation

## Slide 13: Scope of Translation

## Slide 14: Scope of Translation
Neutral
Data
Within CIS
EXPORT
Scope of
exported data

## Slide 15: Scope #1
An export translator (typically) has the potential to export only a subset of the data that can be held by the application’s native data structures.

## Slide 16: Scope #2
The exporting application’s native data structures may not be fully populated with data.

## Slide 17: Data Exchange File
#215 = SECTION_PROPERTIES (#201, $, #216, #217, #218, $, $, $, $, $, $, $, #219,
#220, $, $, $, $, $);
#216 = INERTIA_MEASURE_WITH_UNIT (INERTIA_MEASURE(342200.0), #1151);
#217 = INERTIA_MEASURE_WITH_UNIT (INERTIA_MEASURE(120000.0), #1151);
#218 = AREA_MEASURE_WITH_UNIT (AREA_MEASURE(950.0), #1161);
#219 = MODULUS_MEASURE_WITH_UNIT (MODULUS_MEASURE(17180.0), #1157);
#220 = MODULUS_MEASURE_WITH_UNIT (MODULUS_MEASURE(8558.0), #1157);
#301 = ITEM_REFERENCE_STANDARD ('W1100X424', #302);
#302 = ITEM_REF_SOURCE_STANDARD ('ASTM', 'ASTM_A6M', 1994, $);
#303 = SECTION_PROFILE (2, 'W', 'Wide flange beam to ASTM', 'Plastic', $);
#304 = ITEM_REFERENCE_ASSIGNED (#301, #303);

## Slide 18: Scope of Translation
Potential data scope of
importing application
Native
Data
Within Importing
Application

## Slide 19: Scope #3
An import translator (typically) has the potential to import only a subset of the data that can be held by the application’s native data structures.

## Slide 20: Scope of Translation
Neutral
Data
Within CIS

## Slide 21: Scope of Translation
Neutral
Data
Within CIS

## Slide 22: Scope of Translation
Neutral
Data
Within CIS

## Slide 23: Scope of Translation
Neutral
Data
Within CIS

## Slide 24: Scope of Translation
Neutral
Data
Within CIS

## Slide 25: Scope of Translation
Neutral
Data
Within CIS

## Slide 26: Scope of Translation
Scope of
Exported Data
Scope of
LPM

## Slide 27: Scope #4
A translator will (typically) employ only a subset of the neutral data structure defined by the LPM.

## Slide 28: Conformance Classes
Logical “subsets” of the LPM
  pre-defined by CIS/2
  many and overlapping

## Slide 29: Conformance Classes

## Slide 30: Conformance Classes
Logical subsets of the LPM
  pre-defined by CIS/2
  many and overlapping
Used singly or in combination
  to scope and specify translators
  test conformance against
  export may be less critical than import

## Slide 31: Export Translator
Source data held in native data structures of the application
Map relevant data into neutral data structures of the LPM
  scope by CC Combinations
Write data exchange file
  generate log file
Exported data held in neutral data structures

## Slide 32: Import Translator
Source data held in neutral data structures of the LPM
Read data exchange file
Map relevant data into native data structures
  scope by CC Combinations
  generate log file
Imported data held in native date structures of the application

## Slide 33: Implementation Toolkits
STEP implementation toolkit
LPM defined in EXPRESS
Software components (configured to LPM) to facilitate translator implementation

## Slide 34: Implementation Toolkits
STEP implementation toolkit
SDAI
File Writer
File Reader
Repository

## Slide 35: ISO 10303 (STEP)
Part 11 : EXPRESS
      language reference manual
Part 21 : Data exchange file format
      Clear text encoding exchange structure
      Technical Corrigendum 1
Part 22 : Standard Data Access Interface
      Plus language bindings (Part 23 = C++, Part 24 = C)
Part 41-49 : Integrated Generic Resources

## Slide 36: The Development Process
(An Export Translator)

## Slide 37: Export Translator
Engineering
Application
Software
EXPORT
Data
Exchange
File
Native
Data
Neutral
Data
TRANSLATE

## Slide 38: Export Translator
SDAI
File
Writer
Mapping
Logic
Hand Coded
Generated
Automatically
Reliable and
maintainable
translators
log
file

## Slide 39: Process Walkthrough 1
Familiarisation with CIS/2
Study the LPM
Study Application
  scope
  data structures
Study

## Slide 40: Process Walkthrough 2
Outline specification
  industrial function
Select CC Combination(s)
  market requirements
  commercial considerations
  technical practicality
Scope

## Slide 41: Process Walkthrough 3
Specify Data mappings
  where does each data item come from?
  tabular presentation
  define algorithms where needed
Map Data

## Slide 42: Process Walkthrough 4
Parse the LPM
Write mapping code
  log file output
Test and debug
  write documentation
Conformance test
Implement

## Slide 43: Process Summary
Study
Implement
Map Data
Scope

## Slide 44: End