## Slide 1: CIS/2 Implementation Workshop III, 3-7 April 2000, Ascot
Session 3.2
LPM/5 - Project Definition
Dr A.J. Crowley
CIM steel

## Slide 2
structure
building
site
grid
project
project _plan
zone

## Slide 3
site
zone
1
zone_of_site
zone_of_building
zone_for_site
zone_of_structure
zone_of_project
zone_bounded
building
zone_for_building
structure
zone_for_structure
project
zone_for_project
grid
1
grid_of_site
grid_of_building
grid_of_structure
grid_level
gridline
bounding_ gridlines S[2:4]
bounding_ levels S[1:2]

## Slide 4
grid
grid_level
gridline
parent_grid
parent_grid
plane
grid_intersection
grid_intersection _resolved
grid_offset
level
gridlines S[2:2]
intersection
length_measure _with_unit
offset
L[2:3]
geographical _location
resolution_point

## Slide 5: Grid Level (Horizontal Plane)
Z
X
Y
\axis2_placement_3d.ref_direction
\direction.direction_ratios
p[1] = (1.0, 0.0, 0.0)
x vector for horizontal plane
\axis2_placement_3d.axis
\direction.direction_ratios
p[3] = (0.0, 0.0, 1.0)
z vector (normal to horizontal plane)
placement.location\
cartesian_point.coordinates
point on horizontal plane
(0.0, 0.0, 0.0)

## Slide 6: Gridline (Vertical Plane)
Z
X
Y
\axis2_placement_3d.ref_direction
\direction.direction_ratios
p[1] = (0.0, 0.0, -1.0)
x vector for vertical plane
\axis2_placement_3d.axis
\direction.direction_ratios
p[3] = (1.0, 0.0, 0.0)
z vector (normal to vertical plane)
placement.location\
cartesian_point.coordinates
point on vertical plane
(0.0, 0.0, 0.0)

## Slide 7: Sample Part 21 instances: Planes
#5 = (LENGTH_UNIT() NAMED_UNIT(*) SI_UNIT(.MILLI., .METRE.));
#11 = GRID_LEVEL ('my grid level', #12, #26);
#12 = AXIS2_PLACEMENT_3D ('axes for plane', #13, #14, #15);
#13 = CARTESIAN_POINT ('point for plane axes', (0.0, 0.0, 0.0));
#14 = DIRECTION ('z-vector for horizontal plane', (0.0, 0.0, 1.0));
#15 = DIRECTION ('x-vector for horizontal plane', (1.0, 0.0, 0.0));
#22 = AXIS2_PLACEMENT_3D ('2nd axes', #13, #20, #21);
#20 = DIRECTION ('z-vector for plane', (1.0, 0.0, 0.0));
#21 = DIRECTION ('x-vector for plane', (0.0, 0.0, -1.0));
#23 = GRIDLINE ('my gridline', #22, #26, $);
#24 = (GEOMETRIC_REPRESENTATION_CONTEXT(3) GLOBAL_UNIT_ASSIGNED_CONTEXT((#5)) REPRESENTATION_CONTEXT('context id', 'context for planes'));
#25 = REPRESENTATION ('rep for two planes', (#11, #23), #24);
#26 = GRID (‘my grid’, $, $);

## Slide 8: Located Items - Parts & Joints
located_part_joint
parent_assembly
located_joint_system
descriptive_joint_system
located_part
descriptive_part
(ABS)
located_item
location
1
coord_system
assembly_manufacturing
part
parent_assembly
joint_system
logically_joined_parts S[2:2]
required_joints S[1:?]
coord_system_child
parent_coord_system

## Slide 9: Located Items - Assemblies
grid_offset
located_assembly
descriptive_assembly
(ABS)
located_item
location
1
coord_system
structure
assembly
parent_structure
location_on_grid S[1:?]
coord_system_child
parent_coord_system
structure_select
zone_of_structure
zone_of_building
located_structure

## Slide 10: Located_assembly
#3121 = LOCATED_ASSEMBLY (111, 'my assbly', 'my description', #3101, (#1431), #1121, #1291);
#3101 = COORD_SYSTEM_CARTESIAN_3D ('My coord sys', 'Assembly Coordinate System', $, 3, #246);
#1121 = ASSEMBLY_MANUFACTURING (1, 'M1', 'floor plate', 'preliminary', 1, .LOW., 'my treatment', '4, 3, 2, 5', 'my use', .SHOP_PROCESS.);
#1291 = STRUCTURE (4556, 'my structure', 'my description');

## Slide 11: location_on_grid
#3121 = LOCATED_ASSEMBLY (111, 'my assbly', 'my description', #3101, (#1431), #1121, #1291);
#1431 = GRID_OFFSET (#1383, (#13, #13));
#1383 = GRID_INTERSECTION ('1A', (#1372, #1374), #1371);
#1371 = GRID_LEVEL ('my level', #1376, #1375);
#1372 = GRIDLINE ('gridline 1', #1377, #1375, $);
#1373 = GRIDLINE ('gridline 2', #1378, #1375, #1372);
#1374 = GRIDLINE ('gridline A', #1379, #1375, #1373);
#1375 = GRID ('my grid', 'my description', 'my use');

## Slide 12: Building Complex (CC133)
#8901 = BUILDING_COMPLEX (654789, 'Coffee Man', 'Food & Beverage Facility', #55501, (#8801));
#8801 = BUILDING (31556, 'Coffee Extractor', $, 'Class 1', #45007, (#57701));
#57701 = STRUCTURE (987654, 'Example Structure', 'Support structure for two coffee extractors');

## Slide 13: Setting Out Point (CC152)
#54901 = SETTING_OUT_POINT (#55501, #1001);
#55501 = SITE (2143, 'Site X', $, #403);
#403 = ADDRESS ($, '15', 'High Street', $, 'Miami', 'Florida', '123466', 'USA', $, $, $, $);
#1001 = GLOBAL_LOCATION (#1002, 'mean sea level', 25, 33, $, -80, 21, $);
#1002 = LENGTH_MEASURE_WITH_UNIT (LENGTH_MEASURE(1200.0), #11);

## Slide 14: Project Organization (CC149)
#47701 = PROJECT (12345, 'Worked Example 2', 'AISC Workshop 2 Case Study');
#47801 = PROJECT_ORGANIZATION (#45011, #47701, #45101);
#45101 = PERSON_AND_ORGANIZATION_ROLE ('Lead Engineer of Record');
#45011 = PERSON_AND_ORGANIZATION (#44904, #41707);
#44904 = PERSON ('32', 'Holland', 'Mark', ('V'), ('Mr'), ('P.E.'));
#41707 = ORGANIZATION ('HCI', 'Hamburg Consulting, Inc', 'Consulting Engineers');