## Slide 1: CIS/2 Implementation Workshop III, 3-7 April 2000, Ascot
Session 4.4
Mapping Tables:
Explanation & Development
CIM steel
Dr A.J. Crowley

## Slide 2: CIS/2 Translators
Engineering
Application
Software
EXPORT
IMPORT
Standardized
CIS/2 Data
Structures
Neutral
Data
Native
Data
Governed by
vendor’s own
Data Structures
Governed by
CIM steel
TRANSLATE
TRANSLATE

## Slide 3: Translator Development Process
Study
Implement
Map Data
Scope

## Slide 4: Translator Development Process
Study
Analyse and understand native data structures
  If necessary - documents them in detail
  If possible - create an EXPRESS model
Analyse and understand neutral data structures
  LPM/5 EXPRESS Schema
  Long form & Short Form
  EXPRESS-G Diagrams

## Slide 5: Translator Development Process
Scope
Consider scope of data that will be supported
  on export and import
  unit systems (SI or US or both)
  Item references (‘flavours’)
Consider likely usage scenarios
  for import translators - which other applications will be sending data
  for export translators - which other applications will be receiving data

## Slide 6: Scope of Translation
Potential data scope of
importing application
Potential data scope of
exporting application
Scope of
exchanged data
Neutral
Data
Native
Data
Native
Data

## Slide 7: Scope of Data Exchange
Scope of
Translator A
Scope of
Translator C
Scope of
Translator D
Scope of
Translator B
LPM/5

## Slide 8: Mapping
Map Data
Map the data structures
  export - native to neutral
  import - neutral to native
Probably the most difficult and demanding task of the whole translator development process!
  Unlikely to be simple one-to-one mapping
Can be subjective
Dependent upon knowledge of
  CIS/2 neutral data structures ... AND ...
  vendor’s own native data structures

## Slide 9: Mapping
Map Data
2 aspects of mapping:
  data structures (the template model)
  data values (the populated model)
    required when using a native database
‘W36X359’
-- neutral (flavour)
‘36x16½W359’
-- native (database)

## Slide 10
CIS Translator Program
Import | Export
SDAI Library
Application Software
STEP Data Repository
Native Data Repository
EXPORT
Data mapping
(native to neutral)
IMPORT
Data mapping
(neutral to native)
STEP File Formatter / Writer
STEP File Reader / Parser
Import File
Export File

## Slide 11: Export Mapping Table
Neutral Function Native
entity_a
.attribute_1 << table_x.field_3
.attribute_2 x1000 table_z.field_9
entity_b
.attribute_1 << table_y.field_1
.attribute_2 << table_p.field_9
.attribute_3 << table_z.field_2
.attribute_4 << table_z.field_3
CIM steel

## Slide 12: Import Mapping Table
Native Algorithm Neutral
table_x entity_a.attribute_1
.field_1 entity_a.attribute_2
.field_2 /1000 entity_c.attribute_5
table_y entity_b.attribute_1
.field_1 entity_b.attribute_2
.field_2 entity_c.attribute_2
.field_3 entity_f.attribute_2
CIM steel

## Slide 13: Native Data Structures
NodePoint
id
STRING
REAL
y_coord
REAL
REAL
x_coord
z_coord
LOGICAL
LOGICAL
LOGICAL
LOGICAL
LOGICAL
LOGICAL
bc_dx
bc_dy
bc_dz
bc_rx
bc_ry
bc_rz

## Slide 14: Neutral Data Structures
point
geometric_ representation_item
1
name
representation_item
cartesian_point
coordinates L[1:3]
length_measure
REAL
node
boundary_condition
restraints
analysis_model
parent_model
(INV) component_nodes S[2:?]
node_coords
boundary_condition_logical

## Slide 15: Example Export Mapping Table (1)
Neutral Function Native
node
.node_name << NodePoint.id
.node_coords (point)
.restraints (boundary_condition)
.parent_model (analysis_model)
cartesian_point
.name NodePoint.id
.coordinates[1] NodePoint.x_coord
.coordinates[2] NodePoint.y_coord
.coordinates[3] NodePoint.z_coord

## Slide 16: Example Export Mapping Table (2)
Neutral Function Native
boundary_condition_logical
.bc_x_displacement_free << NodePoint.bc_dx
.bc_y_displacement_free NodePoint.bc_dy
.bc_z_displacement_free NodePoint.bc_dy
.bc_x_rotation_free NodePoint.bc_rx
.bc_y_rotation_free NodePoint.bc_ry
.bc_z_rotation_free NodePoint.bc_rz

## Slide 17: Example Import Mapping Table
Native Data Neutral Data
Node Point
.id node.node_coords.point
\representation_item.name
.x_coord node.node_coords.point
\cartesian_point.coordinates[1]\length_measure
.y_coord node.node_coords.point
\cartesian_point.coordinates[2]\length_measure
.z_coord node.node_coords.point
\cartesian_point.coordinates[3]\length_measure
.bc_xd node.restraints\boundary_condition
\boundary_condition_logical.bc_x_displacement_free

## Slide 18: Example Scheduling Database

## Slide 19: Table: Detail (Native Data)

## Slide 20: Finding equivalent neutral data
!
structural_frame_item
group
structural_frame_product
_with_material
material
structural_frame_product
part
(ABS)
assembly
part_prismatic
part_prismatic_simple
assembly_manufacturing
group_assignment

## Slide 21: Example Import Mapping (Entities)

## Slide 22: Example Import Mapping (Attributes)
Native Data Neutral Data
Detail
.Grade
.Length prismatic_part_simple.cut_length.value_component
Or In full...
prismatic_part_simple.cut_length.
\positive_length_measure_with_unit.
\SELF\measure_with_unitvalue_component.
\measure_value\positive_length_measure
\length_measure = REAL

## Slide 23: Example Import Mapping (Entities)

## Slide 24
Native Data Neutral Data
Detail
.Type of material prismatic_part_simple.profile\section_profile
.Size of material SELF\structural_frame_item.item_name
alternatively
item_reference_assigned.assigned_reference
\item_reference.ref
IF
item_reference_assigned.assigned_to_item
\structural_frame_item :=: section_profile
.Grade
.Length
Example Import Mapping (Attributes)

## Slide 25: Likely Problems
Units
  Order of magnitude
    millimetres to metres
Sign Convention
  Clockwise positive, z-up
Implied information
  Project name, description, client
Code of practice
Unmapped items

## Slide 26: Unmapped data
An export translators may require information not available in native data structures
A value may be derived from
  the operating system supporting the application
    e.g. date and time
  the user during installation of the translator
    e.g. user name
  the user during operation of the translator
    e.g. project name
  default values hard coded into translator
    e.g. units
Mapping table must record which!

## Slide 27: IAI IFC Mapping to CIS/2
ST
-
1 scope
ST
-
1 scope
IFC
-
IFC
-
model
model
CIS
-
CIS
-
model
model
C1
C1
C3
C2
C4
C5
Finnish SteelBase Project - IAI ST1 Project

## Slide 28: CIS/2 & IFC model decompositions