## Slide 1: CIS/2 Implementation Workshop III, 3-7 April 2000, Ascot
Session 5.5
LPM/5 - Manufacturing Constructs
CIM steel
Dr A.J. Crowley

## Slide 2: LPM/5: The 3 ‘Views’
Analysis
Design
Manufacturing
LPM/5

## Slide 3: Analysis - Design - Manufacturing
(ABS)
assembly
assembly_design
assembly_manufacturing
1
analysis_model
element
node
located_joint_system
located_part
design_part
design_joint_system

## Slide 4: LPM/5 Short Form (Manufacturing)
The physical model information is contained primarily in 4 of the 17 ‘subject areas’:
  1. Decomposition
  2. Project Definition
  3. Structural Modelling
  4. Loading
  5. Structural Response
  6. Parts
  7. Features
  8. Joint Systems
  9. Materials
  10. Location
  11. Grouping
  12. Geometry
  13. Units & Measures
  14. Items References
  15. Product Definition
  16. Process Definition
  17. Data Management

## Slide 5: LPM/5 Short Form (Manufacturing)
Product Definition & Items References
Decomposition & Composition
Parts
Joint Systems
LPM/5
Features
Location
Coordinate Systems
Transformations

## Slide 6: LPM/5: Features
LPM/5

## Slide 7: Defining Features
plane
feature
1
feature_cutting_plane
feature_edge_chamfer
plane_definition
item_reference_assigned
assigned_reference
item_reference
assigned_to_item
structural_frame_item
label
text
item_name
item_description
INTEGER
item_number
feature_surface
feature_volume
feature_thread

## Slide 8: Cutting plane

## Slide 9: Defining a Plane
#5 = (LENGTH_UNIT() NAMED_UNIT(*) SI_UNIT(.MILLI.,.METRE.));
#11 = PLANE ('my horizontal plane', #12);
#12 = AXIS2_PLACEMENT_3D ('axes for plane', #13, #14, #15);
#13 = CARTESIAN_POINT ('point for plane axes', (0.0, 0.0, 0.0));
#14 = DIRECTION ('z-vector for plane', (0.0, 0.0, 1.0));
#15 = DIRECTION ('x-vector for plane', (1.0, 0.0, 0.0));
#24 = (GEOMETRIC_REPRESENTATION_CONTEXT(3) GLOBAL_UNIT_ASSIGNED_CONTEXT((#5)) REPRESENTATION_CONTEXT ('context id', 'context for planes'));
#25 = REPRESENTATION ('rep for two planes', (#11), #24);

## Slide 10: Edge Chamfers

## Slide 11: An edge 'rounding' and a 'fillet'

## Slide 12: Volume Features
shape_representation
feature_volume
1
feature_volume_complex
feature_volume_hole
label
feature_shape
feature_volume_prismatic
feature_volume_curved
feature_volume_with_layout
feature_volume_with_process
ANDOR
plane
feature_trace
point
layout S[2:?]
cut
process_definition
ANDOR
ANDOR

## Slide 13: Holes (Volume Features)
feature_volume_hole
1
feature_volume_hole_circular
feature_volume_hole_rectangular
feature_volume_hole_slotted
feature_volume_hole_slotted_curved
feature_volume_ hole_circular_threaded
thread_ definition
feature_thread

## Slide 14: Circular Holes
positive_length_
measure_with_unit
feature_volume_hole
1
feature_volume_hole_circular
hole_radius

## Slide 15: Sample Part 21 Instance
#1 = DIMENSIONAL_EXPONENTS (1.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0);
#2 = LENGTH_UNIT (#1);
#3 = POSITIVE_LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(150.0), #2);
#6 = FEATURE_VOLUME_HOLE_CIRCULAR (1, 'my feature’, $, #3);

## Slide 16: Rectangular Holes
feature_volume_
hole_rectangular
hole_length
hole_height
fillet_radius
positive_length_
measure_with_unit

## Slide 17: Sample Part 21 Instance
#1 = DIMENSIONAL_EXPONENTS (1.0, 0.0, 0.0, 0.0, 0.0, 0.0, 0.0);
#2 = LENGTH_UNIT (#1);
#3 = POSITIVE_LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(150.0), #2);
#4 = POSITIVE_LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(250.0), #2);
#5 = LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(12.0), #2);
#6 = FEATURE_VOLUME_HOLE_RECTANGULAR (2, 'my feature’, $, #3, #4, #5);

## Slide 18: Slotted Hole
feature_volume
_hole_slotted
slot_length
slot_height
positive_length_
measure_with_unit

## Slide 19: Curved slotted Holes

## Slide 20: Volume Features
feature_volume_prismatic
1
feature_volume_prismatic_chamfer
feature_volume_prismatic_flange_chamfer
feature_volume_prismatic_flange_notch
feature_volume_prismatic_notch
feature_volume_prismatic_skewed_end
BOOLEAN
top_or_bottom
start_or_end_face
start_or_end_face
top_or_bottom_edge
original_face

## Slide 23: Horizontal Plane
Z
X
Y
\axis2_placement_3d.ref_direction
\direction.direction_ratios
p[1] = (1.0, 0.0, 0.0)
x vector for horizontal plane
\axis2_placement_3d.axis
\direction.direction_ratios
p[3] = (0.0, 0.0, 1.0)
z vector (normal to horizontal plane)
placement.location\
cartesian_point.coordinates
point on horizontal plane
(0.0, 0.0, 0.0)

## Slide 24: Vertical Plane
Z
X
Y
\axis2_placement_3d.ref_direction
\direction.direction_ratios
p[1] = (0.0, 0.0, -1.0)
x vector for vertical plane
\axis2_placement_3d.axis
\direction.direction_ratios
p[3] = (1.0, 0.0, 0.0)
z vector (normal to vertical plane)
placement.location\
cartesian_point.coordinates
point on vertical plane
(0.0, 0.0, 0.0)

## Slide 25: Sample Part 21 instances: Planes
#5 = (LENGTH_UNIT() NAMED_UNIT(*) SI_UNIT(.MILLI.,.METRE.));
#11 = PLANE ('my horizontal plane', #12);
#12 = AXIS2_PLACEMENT_3D ('axes for plane', #13, #14, #15);
#13 = CARTESIAN_POINT ('point for plane axes', (0.0, 0.0, 0.0));
#14 = DIRECTION ('z-vector for horizontal plane', (0.0, 0.0, 1.0));
#15 = DIRECTION ('x-vector for horizontal plane', (1.0, 0.0, 0.0));
#22 = AXIS2_PLACEMENT_3D ('2nd axes', #13, #20, #21);
#20 = DIRECTION ('z-vector for plane', (1.0, 0.0, 0.0));
#21 = DIRECTION ('x-vector for plane', (0.0, 0.0, -1.0));
#23 = PLANE ('my vertical plane', #22);
#24 = (GEOMETRIC_REPRESENTATION_CONTEXT(3) GLOBAL_UNIT_ASSIGNED_CONTEXT((#5)) REPRESENTATION_CONTEXT('context id','context for planes'));
#25 = REPRESENTATION ('rep for two planes', (#11, #23), #24);

## Slide 26: Cylindrical Surface
Z
X
Y
cylindrical_surface.radius
p[1] = (1.0, 0.0, 0.0)
x vector for horizontal plane
\axis2_placement_3d.axis
\direction.direction_ratios
p[3] = (0.0, 0.0, 1.0)
z vector (axis of cylinder)
placement.location\
cartesian_point.coordinates
point on axis of cylinder
(0.0, 0.0, 0.0)

## Slide 27: Sample Part 21 instances: Cylindrical surfaces
#5 = (LENGTH_UNIT() NAMED_UNIT(*) SI_UNIT(.MILLI.,.METRE.));
#11 = CYLINDRICAL_SURFACE ('my cylindrical surface', #12, 2300.0);
#12 = AXIS2_PLACEMENT_3D ('axes for cylindrical surface', #13, #14, #15);
#13 = CARTESIAN_POINT ('point for cylinder axes', (0.0, 0.0, 0.0));
#14 = DIRECTION ('z-vector for cylindrical surface', (0.0, 0.0, 1.0));
#15 = DIRECTION ('x-vector for cylindrical surface', (1.0, 0.0, 0.0));
#24 = (GEOMETRIC_REPRESENTATION_CONTEXT(3) GLOBAL_UNIT_ASSIGNED_CONTEXT((#5)) REPRESENTATION_CONTEXT('context id','context for cylinder'));
#25 = REPRESENTATION ('rep for cylindrical surface', (#11), #24);

## Slide 28: LPM/5: Location
LPM/5

## Slide 29
Structure
Coord System
Located Feature
Located Part
Loc Joint System
Setting Out Point (Reference Point)
Site Coord System
Structure Coord System
Site
Assembly
Notes: Introduction
As explained in Part 4B Chapter 10 of CIS/1, the use of Coordinate Systems in the LPM is essential. Everything in the Composition and Decomposition procedures is located by coordinate system. The CIS uses a right handed Cartesian coordinate system with clockwise rotation taken as positive.
Features are located with respect to the part which they modify. Parts and Joint Systems are located with respect to the Assembly to which they belong. Each assembly has its own coordinate system. Similarly, each located part, joint system and feature has its own coordinate system.
Each Located Part and Located Joint System coordinate system, must be located within a parent coordinate system; i.e. the low level assembly (STRUC_MEMBER) coordinate system. This is done by using the origin attribute in its instance of COORD_SYSTEM (to shift the origin laterally), and the associated instance of TRANSFORMATION (to rotate the axes). (see diagrams below)

## Slide 30: Locating Parts & Joint Systems
joined_parts S [0:?]
(INV) required_joints S [0:?]
locations S[0:?]
assembly_manufacturing
part
parent_assemblies S [0:?]
joint_system
parent_assemblies S [0:?]
coord_system
locations S[0:?]
parent_coord_system

## Slide 31: Located Items
located_part_joint
parent_assembly
located_joint_system
descriptive_joint_system
located_part
descriptive_part
(ABS)
located_item
location
1
coord_system
assembly_manufacturing
part
parent_assembly
joint_system
logically_joined_parts S[2:2]
required_joints S[1:?]
coord_system_child
parent_coord_system