## Slide 1: CIS/2 Workshop 5, Houston, TX 13th Nov 2000
Conformance Classes

## Slide 2: Conformance Class
Term borrowed from ISO10303 (STEP)
Each CC a logical subset of LPM/5
  used for specifying translator scope
  used for testing translator compliance
CCs have hard boundaries
  all entities within must be supported in full!

## Slide 3: Conformance Class
The CIS/2 documentation pre-defines 275 modular CCs
Each is focused on a different base entity
  Starting point for defining a CC
  Other entities where pulled-in thus:
    entities it references directly
    entities that must point at it
Defines those CCs that are most likely to be needed
  only selected bases entities

## Slide 4: CC Combinations
Each CC is designed to be minimal
  a small coherent building block within a much larger LPM/5 (atoms)
  a legitimate set of data
  not necessarily a meaningful set of data
CCs can be used individually or in combination (molecules)
  but which CC Combinations to use?

## Slide 5: Scope of Translation
Potential data scope of
importing application
Potential data scope of
exporting application
Scope of
exchanged data
Neutral
Data
Native
Data
Native
Data

## Slide 6: Scope of Data Exchange
Scope of
Translator A
Scope of
Translator C
Scope of
Translator D
Scope of
Translator B
LPM/5

## Slide 7: Entities in a CC
CC1 = entities A1+A11+A111+B1+B11+C1

## Slide 8: Entities in a CC
CC2 = entities B1+B12+D1+E1

## Slide 9: Hard Boundaries
The overall scope of a particular translator corresponds to a particular CCC
  correctly translate all data within that valid subset
    every entity, and
    every (non OPTIONAL) attribute
  translator may provide user control for exporting or importing lesser CCCs

## Slide 10: Short Form Schema
A shorthand definition
References pre-defined elements from existing EXPRESS schema
  No declarations of TYPES, ENTITIES, FUNCTIONS
  USE FROM
  REFERENCE FROM
A STEP toolkit will automatically generate the corresponding “long form” schema

## Slide 11: STEP Short to Long Form
Short Form
Schema
(specification)
Long Form
Schema
(implementation)
Resource
Schema

## Slide 12: CC Short to Long Form
LPM/5
(implementation)
CC Short Form
(specification)
CC Long Form
(testing)
CC Short Form

## Slide 13: Short Form for CC001
SCHEMA LPM5_CC001; -- date_and_time
USE FROM STRUCTURAL_FRAME_SCHEMA (date_and_time);
-- Base Entity - frequently used in other CCs
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA
calendar_date,
coordinated_universal_time_offset,
date,
local_time);

## Slide 14: Short Form for CC001
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA ahead_or_behind,
day_in_month_number,
hour_in_day,
minute_in_hour,
month_in_year_number,
second_in_minute,
year_number);
REFERENCE FROM STRUCTURAL_FRAME_SCHEMA leap_year,
valid_calendar_date,
valid_time);
END_SCHEMA;

## Slide 15: Long Form
Generated from the short form
  using a STEP toolkit
Expanded schema results
  specific to that CC
Other types or entities may be pulled in
SELECTS may also be pulled in

## Slide 16: Numbering of CCs
CC001 - CC035 … Common Resources
CC100 … DMC
CC101 … Advanced DMC
CC102 - CC339 … Specific CCs
Thus, a given translator might support:
  “CC104, CC123, CC223”
A particular CCC is denoted
  “(CC201+CC203)”
Thus, a given translator might support:
  “CC105, (CC201+CC203)”

## Slide 17: Translator Scope - Export
Full information scope of the application
Full CCC scope
of translator
Part populated information scope
Populated lesser (supported) CCCs

## Slide 18: Translator Scope - Import
Full information scope of the application
Full CCC scope of import translator
Populated greater CCCs