## Slide 1: CIS/2 Workshop 5, Houston, TX 13th Nov 2000
Flavour Files

## Slide 2: Product Identifiers in CIS/2
4 classes of product item are defined
  Standard Items.
  Proprietary Items
  Library Items
    information exchanged by being “passed-by-reference” rather than being “passed by attribute value”.
  Non-standard Items

## Slide 3: Assigning Item References
assigned_reference
structural_frame_item
item_reference_assigned
identifier
ref
item_reference _proprietary
item_reference _standard
(ABS)
item_ref_source
item_reference
1
1
item_ref_source _standard
item_ref_source _proprietary
source
source
assigned_to_item

## Slide 4: Standard Items
item_reference _standard
item_ref_source _standard
source
(INV) standard_items S[1:?]
label
standardization_organization
name_of_standard
REAL
year_number
STRING
year_of_standard
label
STRING
version_of_standard
label

## Slide 5: Proprietary Items
item_reference _proprietary
item_ref_source _proprietary
source
(INV) proprietary_items S[1:?]
label
manufacturers_name
organization
manufacturers_range
REAL
year_number
STRING
year_of_range
label
STRING
version_of_range
identifier
label
text
id
name
description

## Slide 6
ISO-10303-21;
HEADER;
FILE_DESCRIPTION (('STEP US FLAVOUR'), '1');
FILE_NAME ('Step US Flavour', '11-05-1998', (‘’), (‘’), ‘’,’’,’’);
FILE_SCHEMA (('STRUCTURAL_FRAME_SCHEMA'));
ENDSEC;
DATA;
#3000 = GROUP (‘US Flavour list’, ‘List of item references in accordance with ASTM standards’);
#3001 = FLAVOUR (#3000, (#1, #3, ….. , #2354, #2355)):
#1 = ITEM_REFERENCE_STANDARD (‘W1100X424’, #2);
#2 = ITEM_REF_SOURCE_STANDARD (‘ASTM’, ‘ASTM_A6M’, 1994, $);
#3 = ITEM_REFERENCE_STANDARD (‘W1100X369’, #2);
#4 = ITEM_REFERENCE_STANDARD (‘W1100X333’, #2);
#5 = ITEM_REFERENCE_STANDARD (‘W1100X295’, #2);
#2354 = ITEM_REFERENCE_STANDARD (‘M30_TYPE1’, #2349);
#2355 = ITEM_REFERENCE_STANDARD (‘M36_TYPE1’, #2349);
ENDSEC;
END-ISO-10303-21;
Physical File (extract)

## Slide 7
#201 = SECTION_PROFILE_I_TYPE (1, 'W14x16x500', 'Wide flange beam to ASTM', 'Plastic', 10, .F., #202, #203, #204, #205, #206);
#202 = POSITIVE_LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(498.0), #1021);
#203 = POSITIVE_ LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(432.0), #1021);
#204 = POSITIVE_ LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(55.6), #1021);
#205 = POSITIVE_ LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(88.9), #1021);
#206 = POSITIVE_ LENGTH_MEASURE_WITH_UNIT (POSITIVE_LENGTH_MEASURE(280.0), #1021);
#1021 = (LENGTH_UNIT()NAMED_UNIT(*)SI_UNIT(.MILLI., .METRE.));
Standard item - passed by attribute value (1)

## Slide 8
#201 = SECTION_PROFILE_I_TYPE (1, 'W14x16x500', 'Wide flange beam to ASTM', 'Plastic', $, #202, #203, #204, #205, #206);
#215 = SECTION_PROPERTIES (#201, $, #216, #217, #218, $, $, $, $, $, $, $, #219, #220, $, $, $, $, $);
#216 = INERTIA_MEASURE_WITH_UNIT (INERTIA_MEASURE(342200.0), #1151);
#217 = INERTIA_MEASURE_WITH_UNIT (INERTIA_MEASURE(120000.0), #1151);
#218 = AREA_MEASURE_WITH_UNIT (AREA_MEASURE(950.0), #1161);
#219 = MODULUS_MEASURE_WITH_UNIT (MODULUS_MEASURE(17180.0), #1157);
#220 = MODULUS_MEASURE_WITH_UNIT (MODULUS_MEASURE(8558.0), #1157);
#1149 = (LENGTH_UNIT()NAMED_UNIT(*)SI_UNIT(.CENTI.,.METRE.));
#1150 = DERIVED_UNIT_ELEMENT (#1149, 4.0);
#1151 = INERTIA_UNIT ((#1150));
Standard item - passed by attribute value (2)

## Slide 9
#301 = ITEM_REFERENCE_STANDARD ('W1100X424', #302);
#302 = ITEM_REF_SOURCE_STANDARD('ASTM', 'ASTM_A6M', 1994, $);
#303 = SECTION_PROFILE (2, 'W', 'Wide flange beam to ASTM’, 'Plastic', $);
#304 = ITEM_REFERENCE_ASSIGNED (#301, #303));
Standard item - passed by reference

## Slide 10: Proprietary item - passed by reference
#901 = ITEM_REFERENCE_PROPRIETARY (’1_12513', #902);
#902 = ITEM_REF_SOURCE_PROPRIETARY (#903, Zeta Sections for Purlins and Cladding Rails , 1996, $);
#903 = ORGANIZATION (‘AYRSHIRE_DAV’, ‘Ayrshire Metal Products (Daventry) Ltd’, ‘Cold formed metal products manufacturer’);
#904 = SECTION_PROFILE(2, ’Zeta',’Cold formed purlin section’, ’Slender', 10, .F.);
#905 = ITEM_REFERENCE_ASSIGNED (#901, #904);

## Slide 11: Mapping
Map the data structures
  export - native to neutral
  import - neutral to native
Probably the most difficult and demanding task of the whole translator development process!
  Unlikely to be simple one-to-one mapping
Can be subjective
Dependent upon knowledge of
  CIS/2 neutral data structures ... AND ...
  vendor’s own native data structures

## Slide 12: Mapping
2 aspects of mapping:
  data structures (the template model)
  data values (the populated model)
    required when using a native database
‘W36X359’
-- neutral (flavour)
‘36x16½W359’
-- native (database)