## Slide 1
Connection Libraries

## Slide 2: Background
Structural Connections Sources
Bechtel Design
    GBU Standard Detail Drawings
    Project Details
Subcontract Detailer or Engineer
Client Requirements
Variations
  Fabricator Site Capabilities
Notes: Structural Connection Designs at Bechtel can come from many sources. Currently using connection details depicted in Global Business Unit (GBU) Engineering standards drawings is the first preference for a connection. If a suitable connection does not exist, the Structural Engineer may design a special connection or may pass the responsibility to a sub-contractor. In some cases, Client connection requirements can govern.
Additionally, Fabricators shop capabilities can cause last minute variations to otherwise completed connection designs. These variation are usually subtle but in some cases they can warrant Structural Engineering evaluation.

## Slide 3: Next Generation
Structural Connections Sources
Bechtel Design
    GBU Standard Detail Drawings or Flavor Files
    Project Details
Subcontract Detailer or Engineer
Client Requirements
Variations
  Fabricator Site Capabilities
Notes: In a CIS2 environment Structural Connection Designs will come from many sources. Using connection details depicted in Global Business Unit (GBU) Engineering flavor files will be the first preference for a connection. If a suitable connection does not exist, the Structural Engineer may design a special connection or may pass the responsibility to a sub-contractor. In some cases, Client connection requirements will govern.
Additionally, Fabricators shop capabilities will cause last minute variations to otherwise completed connection designs. These variation will usually be subtle but in some cases they will warrant Structural Engineering evaluation.

## Slide 4: What’s Different
Everthing & Nothing!
Model Assigned Connections
  Not drafted onto Engineering Drawings
  Referenced from Usual Sources
Published Catalogs
  Enables Equivalency Mapping
  Known Fabricator Variations
Notes: Some have asked what’s different? In my view everything and nothing. Yes we still have pictures that relate what is being asked for but we will communicate through models not drawings. Engineers and Fabricators should seek out Software or individuals to publish their connections into Catalogs with p21 attachments. This will enable mapping between the equivalent connections allowing review to be waived for those cases.

## Slide 5: Work Process Suggestions
Catalog Derived from Placement Application
  P21 Listing of Catalog Connections
Utility for Referencing Application
  Populate Tools w/Connection Names
Provide a Depicting Document
  Publishers Choice
Provide a Code for non-Catalog Design
  Triggers Review Cycle
Toolkits for Precise Placement
  User Friendly
Notes: The highest level of success will be achieved when the Connection Catalog is based upon established capabilities in the software that applies the connection material. A part 21 file listing the catalog content should be provided to populate tools in the referencing application.
A depicting document should be provided. This document can be presented however the owner desires. Ultimately, PDF or VRML will prove to be the best choices.

## Slide 6: Examples and Demo