## Slide 1: Quantum Networks
Leonardo Bacciottini
UMass Amherst
Presented @ QCE2026
Collaborators: Subhransu Maji, Gayane Vardoyan, Don Towsley
arXiv:2609.16198

## Slide 2: Path Selection and Configuration in Quantum Networks
Leonardo Bacciottini
UMass Amherst
Presented @ QCE2026
Collaborators: Subhransu Maji, Gayane Vardoyan, Don Towsley
arXiv:2609.16198

## Slide 3: Utility-based Path Selection and Configuration in Quantum Networks
Leonardo Bacciottini
UMass Amherst
Presented @ QCE2026
Collaborators: Subhransu Maji, Gayane Vardoyan, Don Towsley
arXiv:2609.16198

## Slide 4: Utility-based Path Selection and Configuration in Quantum Networks via Layered Shortest Paths
Leonardo Bacciottini
UMass Amherst
Presented @ QCE2026
Collaborators: Subhransu Maji, Gayane Vardoyan, Don Towsley
arXiv:2609.16198

## Slide 5: 2-Way Quantum Network

## Slide 6: 2-Way Quantum Network
links attempt entanglement generation
Note: Generation rate and entanglement quality trade each other off
(distillation, brightness,…)

## Slide 7: 2-Way Quantum Network
repeaters perform swaps

## Slide 8: 2-Way Quantum Network
end-to-end entanglement generated

## Slide 9: Entanglement distillation

## Slide 10: Path Selection – Classical Internet
Winning strategy: Asynchronous, based on shortest path
Bob
Alice

## Slide 11: Path Selection – Classical Internet
Winning strategy: Asynchronous, based on shortest path
Bob
Alice
Example: Cost of a link = 1/Rate
12
20
14
30
11
15
10
10
Dijkstra

## Slide 12: Path Selection – Quantum Network
Now we have two competing objectives:
  Entanglement rate (how many pairs path can deliver)
  Entanglement quality (fidelity of e2e entanglement)
Utility function: Alice and Bob run QKD: what they care about is secret key rate, function of both rate and quality
Problem:
  Bicriteria shortest path is NP hard
  Constrained shortest path is NP hard

## Slide 13: Path Configuration
How many distillation rounds?
What pump power to use for my SPDC?
…
One physical link …
…
… Many operating points
Path + Operating point selection is a joint problem
Choosing a physical path is not enough. For every link…

## Slide 14: The Domain Space
Notes: Let’s now take a look at what the domain space of path selection + configuration looks like

## Slide 15: The Domain Space

## Slide 16: The Domain Space

## Slide 17: The Domain Space

## Slide 18: The Domain Space

## Slide 19: The Domain Space

## Slide 20: The Domain Space
Optimal for BB84 secret key rate (SKR)
Optimal for negativity-based utility
(Note: Werner state model)
Takeaway: Different applications select different optima
Notes: The only general way that enables us to pre-compute paths is to sweep the pareto frontier so that we can best serve users based on their utility functions.

## Slide 21: The Domain Space

## Slide 22: Quantum Layered Shortest Path (QLSP)
Idea: Discretize fidelity into “bins”
Why? Tracking fidelity becomes a graph exploration problem
How? Extend the graph so that vertices track fidelity
Solution: Solve Dijkstra once on the extended graph
F=1.0
F=0.5
F = 1.0
F = .99
F = .98
F = .97
F = .5
…

## Slide 23: QLSP
Physical Graph
QLSP Graph
Graph grows linearly with number of bins
Theorem: QLSP is FPTAS
for monotone utilities satisfying a sensitivity condition on fidelity loss

## Slide 24: Results
We found non-convex frontiers on all considered topologies
Model:
Werner states, ideal swaps, no decoherence
Midpoint interference scheme, 10Mhz, 0.2dB/km
Raw fidelity F=0.97, rate depends on link length
5 operating points per link: 0 to 4 BBPSSW distillation rounds
Baselines based on scalarized
objectives can’t find these!

## Slide 25: Summary
Joint path selection and configuration: one computation produces a discretized rate–fidelity Pareto frontier from one source to every destination, reusable across utilities.
Guarantees: complexity and approximation analysis establishes an FPTAS under the stated utility-regularity assumptions.
Scalarization: We establish when weighted-sum routing is optimal, and show why unsupported configurations require a richer frontier representation.
arXiv:2609.16198