## Slide 1: How Neutrons Are Produced: The NIST Research Reactor and Cold Neutron Sources
Robert Williams
NIST Center for Neutron Research
February 3, 2021
robert.williams@nist.gov

## Slide 2: Outline:
    Basics
    NBSR History, Description
    Cold Source Development
    Conclusion
Informal History on the NCNR Web Site under About NCNR:
https://www.ncnr.nist.gov/NCNRHistory_Rush_Cappelletti.pdf

## Slide 3: NIST Research Reactor History
Designed in the 1960’s and included a beam port for a cold neutron source.
NBSR First Critical, December 7, 1967.
10 MW until 1985, 20 MW since.
Cold Neutron Facility Development:
  D2O Cold Neutron Source installed, 1987.
  First neutrons in the guide hall in 1990.
  LH2 Source installed September 1995.
  Advanced LH2 CNS, Unit 2, installed 2002.
  NCNR Expansion Project – 5 more guides.
  “Peewee” CNS installed 2012 in BT-9.

## Slide 4
Fissile fuel material, such as 235U, only 0.7% abundant, or 239Pu.
Moderator to slow neutrons (D2O, H2O, Graphite)
Control Elements (Cd, B)
Other Stuff:
  Shielding
  Coolant
  Neutron Source
  Neutron Detectors
Thermal Reactor Components
Moderator
Biological Shield

## Slide 5: NBSR Core Characteristics
HEU** Fuel: 93% 235U3O8 + Al
  350 g 235U per Fuel Element
  34 plates: 11 in x 2.5 in x .02 in
  Heavy water coolant (D2O)
30 Fuel Elements
  Fuel cycle ~38 days @ 20 MW
  Load 4 fresh elements, reposition the others
  About 960 g 235U consumed per cycle
Split Core – No Fuel at Mid-plane
  The BTs and CNS are at this elevation.
  Thermal neutron “flux trap”.
  BT fluxes ~ 1.5 x 1014 n/cm2-s
** Need to convert to LEU (U-10Mo) when fuel is qualified.

## Slide 7
Cut-away View of the NBSR Core
Top Grid Plate
Fuel Elements (30)
Fuel Plates
Liquid Hydrogen Cold Neutron Source
Bottom Grid Plate
D2O Primary Inlet Plenums
Cd Shim Safety Arms (4)
Reactor Vessel
Radial Beam Tubes (9)
Split Core:
18-cm Unfueled Gap – Flux Trap
Primary Outlet (2)
Thermal Shield

## Slide 8
The NBSR was designed with a 55-cm diameter cryogenic beam port for a D2O-ice CNS.
History:
D2O Tank (1967)
D2O Ice (1987) with gain 3-5
Unit 1 LH2 (1995), gain ~ 6
Unit 2 LH2 (2002), gain ~ 2
Reference: Kopetka et. al., NISTIR 7352

## Slide 9: Production of Cold Neutrons
The neutrons born in fission have an average kinetic energy of about 2 Mega-electron volts, 2 MeV.
They are slowed to thermal energies (20 – 400 milli-eV) by scattering from the molecules of the heavy water (D2O) moderator in the reactor. The D2O is about 115 °F, or 320 Kelvin.
In thermal equilibrium, the neutron energy spectrum is determined solely by the temperature of the moderator (a Maxwell-Boltzmann distribution), analogous to the motion of atoms in an ideal gas.
To reach lower energies, therefore, we introduce a cold moderator, such as liquid hydrogen at 20 K.

## Slide 10: The LH2 CNS, Unit 1, installed in 1995, had a gain of 6 times the D2O source
To fully illuminate the beam ports, the source had to have a very large area.
A 320-mm spherical annulus, 20 mm thick, with a 200-mm diameter exit hole was chosen:
  Low heat load (850 W)
  Ease of fabrication. Material: Al 6061-T6
  Composed of concentric Al spheres (5 liters of LH2)
  Hydrogen vapor filled the inner sphere, which was open at the bottom.
Thermal-hydraulic tests with LH2 conducted at NIST Boulder.

## Slide 11
Unit 1 had too much empty space next to the reactor core.
Vapor in the inner sphere scattered cold neutrons from the beam.
Much more D2O in Unit 2 results in a higher neutron flux in the CNS region and the adjacent fuel elements.
32 x 24 cm ellipsoid allowed more D2O and a thicker LH2 annulus.
Gain ~ 2 (2002)

## Slide 12: The liquid hydrogen cold source is passively safe, simple to operate, and very reliable
A thermosiphon is the simplest way to supply the source with LH2.
  Cold helium gas cools the condenser below 20 K.
  Hydrogen liquefies and flows by gravity to the moderator chamber.
  Vapor rises to the condenser and a naturally circulating system is established.
The system is closed to minimize hydrogen gas handling.
All system components are surrounded by He containments.

## Slide 13
Insertion of Unit 2 Cold source – November 2001

## Slide 14
Existing LH2 CNS, In-pile Guides as of April 2011
MACS
NG-1
NG-2
NG-3
NG-4
NG-5
NG-6
NG-7
CTW Beam Port (now has inpile piece for new guides)
CTE

## Slide 15: A second LH2 source was installed in BT-9 (2012) as part of the NCNR Expansion Initiative
5 new guides have been installed for the guide hall expansion.
MACS has moved to BT-9 and has its own small LH2 source.
“Peewee” : 11-cm ID, and a 0.5-l volume.
It has a gain of about 1.7 over Unit 2.
MCNP code used to estimate performance and heat load.

## Slide 16
Side View of BT-9 Cold Source
Peewee:
14.6-cm OD water jacket
It has its own H2 tank, but the condenser is cooled in parallel with Unit 2.
Piccolo “phase separator”
Operating successfully since April 2012.
Reference: IGORR 2009
Thermal-hydraulic tests of thermosiphon used R-134.

## Slide 17
The plug provides shielding and supports the cryostat assembly.
A diverging beam of cold neutrons is provided for MACS.

## Slide 18
CNS Team installed Peewee in BT-9 in September 2011.

## Slide 19: Conclusion
The LH2 cold sources at NIST have made NCNR a world class cold neutron facility.
About 70% of experiments use cold neutrons.
LD2 source planned for 2023(?), to replace Unit 2 (reference: IGORR 2016, Berlin).
Relicensed in 2009 for 20 more years!!
Plan to relicense again in 2029.
Studies have been initiated for a new reactor optimized for cold neutron production.

## Slide 20
Technical Support Building
Guide Hall Addition
Original Building 1963-1967
NCNR Expansion – Fall 2010

## Slide 22: Xenon Poisoning

## Slide 23
The buildup of 135Xe can overwhelm the available excess reactivity and keep the NBSR shutdown 30 – 40 hours.
After an unplanned shutdown the operators are very busy:
  - Find the cause, fix it
  - Reduce cooling flow
  - Commence restart
The Xe clock is ticking, so please refrain from calling the control room!

## Slide 24
New Guide Hall
Existing Instrument Layout – Nov 2014