## Slide 1: RRBC Method National Institute of Standards and Technology Marek Franaszek and Geraldine Cheok

## Slide 2: What is Registration?
Sensor Frame
Robot Frame
World Frame
Table Frame
Registration is a process to transform one coordinate frame to another coordinate frame.
For example, the sensor system, robot, and work table each have their own coordinate frames.

## Slide 3: Why is registration needed?
It is required when locations of objects measured in one coordinate frame are needed in another frame. Examples:
Robots using sensors to determine location of work objects or obstacles need to register the sensor to the robot coordinate frame
Multiple robots carrying the same object need to register their respective coordinate frames
Applications:
  Automated assembly and pick-and-place tasks
  Humans/objects for collision avoidance and spatial awareness

## Slide 4: Point-Based, Rigid-Body Registration
Point-based, rigid-body registration is used in this presentation.
This type of registration requires a set of 3 or more registration points to determine the transformation matrix (R, t).
The set of registration points is measured in the frames (e.g., sensor and robot frames) to be transformed.
robot can measure the points by touching the points with its end effector.
A
B
C
Registration points
Sensor Frame
Robot Frame

## Slide 5
Point-based, rigid-body registration in a nutshell …
Transform Frame 2 to Frame 1.
Measure registration points in Frames 1 & 2.
Pts. A, B, C measured
in Frame 1
A
B
C
0
10
20
10
20
30
C’
A’
B’
Pts. A, B, C measured
in Frame 2
-40
-30
-20
60
70
80
50
Frame 1
A
B
C
B’
A’
C’
0
10
20
10
20
30
Determine transformation matrix (R, t).
  Many open source algorithms and commercial software available to perform this task, e.g.,
    Arun, K. S. et al., Least-squares Fitting of Two 3_D Point sets, IEEE Pattern Analysis and Machine Intelligence, Sept. 1987
    Software: e.g., Spatial Analyzer, Polyworks, Cyclone, CloudCompare, Matlab

## Slide 6: Registration Error
After transforming to Frame 1, corresponding points are not mapped exactly onto each other.
For example, A and A’ should be in the same location after transformation of A’.
The distances between any two points (e.g., AB & A’B’ or BC & B’C’) should be the same but are not.
A
B
C
B’
A’
C’
= Points measured in Frame 1
= Points transformed to Frame 1

## Slide 7: What does the RRBC (restoration of rigid-body condition) method do?
d, positional error:
Due to measurement error (e.g., robot, sensor, environment) of point location
Consists of measurement error and registration error
  If there is no measurement error, then registration error is zero.
  If there is measurement error, then (R, t) will have errors which are propagated to ALL transformed points.
RRBC reduces d
Point Q as measured in Frame 1
Point Q after transformation from Frame 2 to Frame 1
d
Point Q is a target point (see Slide 15) not a registration point.

## Slide 8
Criteria for using RRBC Method
Need more positional accuracy
> 2.5
where
= sensor-robot differences*
= sensor noise from sensor spec
* See Franaszek, M. and Cheok, G. S., Improving Rigid-Body Registration Based on Points Affected by Bias and Noise," presented at the 8th Int. Precision Assembly Seminar, Chamonix, France, 2018 on how to determine this variable.

## Slide 9
Next two slides list steps in RRBC method
(Illustration of the method follows)

## Slide 10: RRBC Method
Measure minimum of 3 registration points with robot and sensor.
  Registration points should be well distributed and encompass the work volume
Using any appropriate registration method, determine transformation matrix (R, t) that transforms registration points measured by sensor from sensor frame to robot frame.
Identify points of interest (target points*) within robot work volume.
Identify points (fiducial points*) around target points and measure them with
sensor and with robot.
  Ensure that region bounded by fiducial points encompass the uncertainty of the target point location.
  *Target and fiducial points are explained later in the presentation

## Slide 11: RRBC Method (continued)
Apply inverse of transformation matrix (R, t)-1 to fiducial points measured by the robot
(from Step 4) transforming them from robot frame to sensor frame.
Calculate differences between transformed, robot-measured, fiducial points (from
Step 5) and sensor-measured, fiducial points (from Step 4) to obtain corrections to sensor-
measured fiducial points.
Measure location of target points with the sensor.
Calculate and apply corrections (from Step 6, using the fiducials closest to the
target points) to the measured target points (from Step 7).
Transform corrected target points (from Step 8) from sensor frame to robot frame using (R, t).

## Slide 12
Steps in RRBC illustrated using a 2D example

## Slide 13
Measure a minimum of 3 registration points with robot and sensor.
A
B
C
A
B
C
Robot Frame
A’
B’
C’
Sensor Frame

## Slide 14
2. Using ANY appropriate registration method, determine the transformation matrix (R, t) that transforms the sensor registration points from sensor frame to robot frame.
Determine (R, t) to map sensor pts. to robot pts.
A’
B’
C’
Sensor Frame
Sensor registration pt.
Sensor registration points transformed to robot frame
Robot Frame

## Slide 15
3. Identify points of interest (target points) within robot work volume.
A
B
C
Target pt.
Target pt.
Robot Frame
In this example, target points are hole locations where the robot needs to insert a peg.
Generally, target “points” are centers of regions where a robot needs to perform a task such as drilling, insertion, or assembly or regions where accurate location is required.
Robot Frame
A
B
C

## Slide 16
4. Select points (fiducial points) around target points. Measure their locations with sensor and with robot.
A
B
C
F1
F2
F3
F4
F7
F6
F8
F5
Robot Frame
A
B
C
F7’
F8’
F6’
F5’
F3’
F4’
F2’
F1’
Fiducials in Sensor Frame

## Slide 17
Selecting Fiducial Locations
Select location of fiducial points so that the region bounded by the fiducials contains the region of variability of the target point location. It is expected that there will be some variability in the target placement within the robot work volume.
Region bounded by the fiducials.
Region of variability in the location of target point. That is, actual target location may be anywhere within this region.
Nominal/expected location of target.
F1
F2
F3
F4
B

## Slide 18
5. Apply the inverse of the transformation matrix (R, t)-1 to robot-measured, fiducial points transforming them from robot frame to sensor frame.
Apply (R, t)-1 to fiducials
Sensor Frame
Fiducials in Robot Frame
F1
F2
F3
F4
F5
F6
F7
F8
F5
F6
F7
F8
F1
F2
F3
F4

## Slide 19
Calculate differences between transformed, robot-measured fiducial points and sensor-measured fiducial points to obtain corrections, ei , for fiducial points in sensor frame. ei are vectors.
Fiducials in sensor frame
See (a)
See (b)
(a)
(b)
e8
e7
e5
e6
e4
e2
e3
e1

## Slide 20
Measure locations of target points with sensor.
Sensor Frame
Fiducial pt.
Target pt.

## Slide 21
Calculate correction (using fiducials closest to target point) for the measured target point. Target corrections are linearly interpolated using fiducial corrections which are weighted based on their distance from the target point.
Apply correction to target point.
Target pt.
Fiducial pt.
Target correction
Fiducial correction
Sensor Frame
* Correction vectors exaggerated for illustration
e8
e7
e5
e6
e4
e2
e3
e1

## Slide 22
9. Transform corrected target points from sensor frame to robot frame using (R, t).
Apply (R, t) to target points
Target measured in robot frame
Transformed corrected target
Transformed uncorrected target
Robot Frame
Sensor Frame
Corrected target pt.
Fiducial
Uncorrected target pt.
* Uncorrected target points also transformed using (R, t) and shown only to illustrate the benefit of using RRBC method. Transformation of uncorrected target points would not be performed in actual practice.

## Slide 23: Other methods to compensate for or reduce the positional error
Active compliance control based on feedback from force/torque sensors
  Involves a robot with this capability or the addition of hardware to obtain this capability
Visual servo control
  Involves image processing, computer vision, and robot control
Volumetric Error Compensation methods
  Discussed in next slide

## Slide 24: RRBC vs. Volumetric Error Compensation (VEC) methods
RRBC | VEC
RRBC compensates for position error but does not require in-depth knowledge of the robot or sensor. Steps are easy to perform. | VEC models compensate for position error by using an analytical model that combines robot and sensor error. This requires in-depth knowledge of robot and sensor to compensate for potential sources of error. This is a challenging task.
If a different sensor is used with robot, the interpolation scheme in RRBC method does not have to be modified. | If a different sensor (from the original sensor) is used with robot, VEC model needs to be updated.
Both methods require comparable amounts of data to be collected – to determine model parameters in VEC method and for the interpolation scheme in RRBC method. |