## Slide 1: Peg-in-Hole Experiments
Three experiments (Exp. 1 – 3)
  Robot in position control (no active compliance control)
  Seven runs (repeats) in each experiment
  Each run = inserting a 12.7 mm peg into 80 holes
  Two peg types
Metric
  Pass = Peg fully inserted
  Fail
    Peg not fully inserted or
    Insertion force > 17 N
Exp. 1
Exp. 2 & 3

## Slide 2
World frame
Optical Table
Optical table w/ threaded holes
Target points
Fiducial points.
Only 8 shown for clarity
Hole into which peg is inserted
Notes: Hide slide if not needed.

## Slide 3
UNCORRECTED = Conventional registration
CORRECTED = Conventional registration
  w/ RRBC method applied
  BASELINE = No registration applied
Experiment 1, 0.002” hole tolerance
Experiment 2, 0.002” hole tolerance
Experiment 3, 0.001” hole tolerance

## Slide 4
 | Peg type | Peg-Hole tolerance (in.) | Failed Insertions1, 2 (%) |  |  | 
 |  |  | Baseline3 | Uncorrected | Corrected | Uncorrected Corrected
Experiment 1 (7 runs) |  | 0.002 | 3.4 | 23.8 | 10.0 | 2.4
Experiment 2 (7 runs) |  | 0.002 | 3.4 | 26.3 | 2.7 | 11.0
Experiment 3 (7 runs) |  | 0.001 | 4.5 | 42.1 | 10.0 | 4.5
Values are averages for 7 runs in a given experiment.
Failed insertion = # failed insertions in a run/total # of holes.
Baseline = failures in this category are due solely to measurement noise.

## Slide 5
Target Registration Error
Target registration error (TRE)
  metric for registration quality
  calculated for all 80 target hole locations in an experiment
Target hole location as measured by robot
Target hole location transformed
from world frame to robot frame
Robot Frame
TRE
Experiment 1
Experiment 2
Experiment 3
RMST = root mean square of TRE