## Slide 1: Implementation of the RRBC Method
Notes: Slides 1-5 meant for presentation.
Slides 6-9 are same as Slides 2-5 but different color and style and are meant for generating handouts.

## Slide 2
System Integrator consults with User
Determines:
User applications
Accuracy requirements
Sensors used
  RRBC applicable if
    (sensor bias/sensor noise) > 2.5
Number of fiducial points
System Integrator develops software
User executes software

## Slide 3
User
Measures registration points with robot and with sensor
Determines and measures nominal/expected locations of objects (target points) with sensor
Determines variability of object placement in work volume
Software
(System Integrator)
Robot path planner
Corrected target point locations
System Integrator and User Responsibilities
Location of target points
Sensor

## Slide 4
Registration Module: determine transformation matrix,
Measures registration points in robot and sensor frames
Nominal location of target points in sensor frame
Determine locations of fiducial points, in robot frame, around each target,
Determine distance from fiducial pt. to target pt. based on variability of object placement and level of accuracy needed.
Send command to robot to move to fiducial pts.
A
Trigger sensor to measure fiducial points,
Software Developed by System Integrator

## Slide 5
  Determine weights () based on proximity to target location for each fiducial correction.
  Determine weighted corrections for
  each target
  Calculate corrected target locations
  Robot path planner
Apply inverse of transformation matrix, to to transform points to sensor frame.
Calculate corrections, , for each fiducial
= (transformed, robot-measured, fiducial pt.) –
(sensor-measured, fiducial pt.)
=
A
  Apply transformation matrix, , to .
Target points from sensor,