## Slide 1: Solid-Phase Extraction (SPE)
Lane C. Sander, Ph.D.
Chemical Sciences Division
Material Measurement Laboratory
National Institute of Standards and Technology1
1Contribution of the National Institute of Standards and Technology. Not subject to copyright. Certain commercial equipment, instruments, or materials are identified to specify adequately the experimental procedure. Such identification does not imply recommendation or endorsement by the National Institute of Standards and Technology, nor does it imply that the materials or equipment identified are the best available for the purpose.
Notes: Solid-Phase extraction is a form of liquid chromatography used in processing samples to selectively isolate constituents of interest from other compounds that may interfere with the analysis. Strictly speaking, Solid-Phase extraction is only applicable to solutions. Before a solid sample can be processed by SPE, it must first be extracted by soxhlet extraction, pressurized fluid extraction, or other methods, to produce a solution that contains the analytes of interest.
This presentation will provide an overview of the theory and practice of Solid-Phase extraction, and will include a demonstration of the use of different types of SPE devices.

## Slide 2: Why Use Solid-Phase Extraction?
Sample processing prior to analysis
  Better metrology
  Purification (selective extraction of analytes or interferences)
  Trace enrichment
  Fractionation
  Solvent exchange
  Derivatization
  Parallel processing of multiple samples
Practical considerations
  Extension of column lifetime
  Reduced maintenance
Notes: Solid-Phase extraction is useful in processing a sample to achieve improved analytical results. For natural matrix samples, the complexity of unprocessed extracts may result in measurement bias as a consequence of co-eluting interferences. Other sample components such as salts may change the ionization efficiency with mass spectrometry.
SPE methods usually target the analytes of interest through choice of selective retention mechanisms. The resulting processed samples are simpler than the original extracts.
SPE methods can also be developed to retain interferences as a class of compounds, for example, nonpolar compounds can be selectively retained by reversed phase adsorbents. SPE methods often use a combination of loading, washing, and elution steps to isolate the constituents of interest.
When sample size is not a limitation, it may be possible to extend the quantification of trace level constituents by concentrating larger sample quantities.
Samples can be divided into fractions, for example, on the basis of polarity, by changing the composition of the solvent used in elution.
As an alternative to evaporation, the solvent matrix can be changed by SPE. For example, an aqueous sample can be retained by reversed-phase SPE, and eluted with an organic solvent, for better compatibility with an instrumental technique that requires organic solvent mixtures, such as gas chromatography.
SPE can also be used in derivatization methods. Analytes are isolated on the SPE adsorbent, and derivatized. This approach can remove matrix constituents that might interfere with the derivatizations, particularly reactive solvents such as water.
When used with manifolds, multiple samples can be processed in parallel to increase sample throughput
Solid-Phase extraction may also be useful in reducing costs associated with instrument maintenance and solvent consumption.
Cleaner samples can reduce the need to perform maintenance on MS sources, and can extend the useful lifetime of LC and GC columns
Solvent consumption is also reduced compared with liquid-liquid extraction.

## Slide 3: SPE Cartridge Design
Stationary Phase
  Chemically modified surfaces
  Reversed-phase, normal-phase, ion-exchange, mixed-mode
Substrate
  Silica, fluorosil, alumina, polymer
  Particle configuration (diameter, pore size, shape)
Physical Configuration
  Cartridge design
    Packed syringe body with reservoir
    Molded cartridge w/o reservoir
  Sorbent mass
SPE without
reservoir
SPE with
reservoir
Notes: SPE cartridges differ in several aspects to permit development of methods for a wide variety of applications.
Most stationary phase chemistries in common use with analytical LC columns are available for SPE applications. Because SPE is a low resolution technique, subtle differences among stationary phases of the same type, but produced by different manufacturers, are less important than with HPLC columns. Some of the more common stationary phase chemistries for SPE are C18, amino, phenyl, ligands with ion exchange properties, and phases with mixed mode chemistries. The latter stationary phases usually employ ion exchange and reversed-phase ligands, and can be highly selective for their target species. For example, mixed mode SPE cartridges have been developed specifically for elicit drug screening of urine samples.
As with analytical and preparative LC, the most common substrate for SPE is chemically modified silica. Unbonded substrates are sometimes used in normal phase methods, with silica, fluorosil, and alumina being the most common. Polymer substrates are less commonly employed, but a few materials exist making applications at high pH feasible.
The analyst has little control over particle configuration, and manufacturers typically do not specify these parameters. Both irregular and spherical shaped particles are used for SPE, and particles are typically about 50 um in diameter. Smaller particle substrates provide higher efficiency, but this aspect may less important for sample cleanup than for HPLC. Methods are usually designed to fully retain the targeted species while eluting other components in the sample. However, wide pore sorbents should be used with proteins and peptides. In practice, the most important variable is the retention mechanism afforded by the SPE adsorbent.
3) The most common configuration for SPE is the packed syringe-style cartridge. The unpacked portion of the cartridge serves as a reservoir for the sample. Less common are molded cartridges that can be fitted to a syringe or reservoir by means of a tapered joint. The mass of sorbent contained in the SPE cartridge differs for different intended applications, but range from about 30 mg to 3 g per cartridge.

## Slide 4: Anatomy of a SPE Cartridge
SPE cartridges are LC columns
Cartridges are available with/without reservoirs
Tube/reservoir size: 1 mL, 3 mL, 6 mL, 12 mL, 20 mL, 60 mL
Mass adsorbent: scales with tube size; 50 mg to 3000 mg
Particles are typically ≈ 50 μm diameter
SPE Cartridges with and without integral reservoirs
SPE reservoirs for use with vacuum manifold
Notes: SPE cartridges are a type of LC column. The design of these cartridges is optimized to permit use without high pressure pumps, and at low cost for single usage.
Cartridges are available with and without reservoirs. Cartridges without a reservoir are typically intended for use with a disposable syringe, for loading and elution of individual samples. Cartridges with a reservoir are used with a vacuum manifold. This approach permits the simultaneous processing of multiple samples.
Reservoir sizes range from 1 to 60 mL.
The mass of the adsorbent within these tubes is scaled with tube size from about 50 mg to 3 g of adsorbent. The quantity of adsorbent must be matched with the size of the sample to be processed to prevent sample overloading and breakthrough.
The diameter of the sorbent particles is significantly larger than sorbents used in analytical columns. This results in greatly reduced backpressure for the SPE cartridge, with low cost. The reduced efficiency is typically not an issue, since SPE methods are similar to flash chromatography, with either complete retention or complete elution of sample components.

## Slide 5: Survey of SPE Stationary Phase Chemistries
Silica-Based Sorbents
  Reversed-Phase
    C18, C8, phenyl, cyanopropyl, aminopropyl
  Normal-Phase
    Cyanopropyl, aminopropyl, diol
  Ion-exchange
    SAX, SCX, WCX, aminopropyl
Unmodified Substrates
  Silica
  Alumina
  Florisil
  Graphitized Carbon
  Resins
Notes: SPE cartridges are most commonly prepared with covalently modified silica substrates. The usual stationary phases used in liquid chromatography are also available for SPE. These include:
Reversed phase materials with alkyl and aromatic stationary phases, cyanopropyl phases and aminopropyl phases. The propyl linkage used with cyano and amino phases provides limited hydrophobicity when the materials are used in aqueous environments. These interactions can be exploited in addition to interactions with the polar head groups.
The cyanopropyl and aminopropyl phases can also be used as normal phase adsorbents, when used with nonpolar solvents. As an example, environmental samples are commonly processed using aminopropyl SPE cartridges with a hexane / methylene chloride mobile phase to retain pesticides, polychlorinated biphenyl congeners, and polycyclic aromatic hydrocarbons.
Ion exchange SPE are available with strong and weak ion exchange chemistries. The choice of the ion exchange chemistry employed requires consideration of the pH of the mobile phase, and the ionic state of both the ion exchanger and the constituents at that pH. More detail on the use of ion exchange SPE will be provided in a later section.
A variety of substrates are useful adsorbents without surface modification.
Silica, alumina, and florisil are used in normal phase methods to retain polar constituents, whereas
Graphitized carbon and various resins can be used to retain nonpolar constituents with polar solvents. Styrene divinylbenzene is a commonly used resin adsorbent.

## Slide 6: Elution of solvent
Positive-pressure and negative-pressure driven elution
  Syringe
  Vacuum manifold
  Gravity
  Centrifugation
Flow rate:
  Generic methods < 5 mL/min
  Ion exchange < 2 mL/min
Match elution and washing volumes to the reservoir volume
Vacuum Manifold
SPE with
syringe
Notes: Solvent flow through the SPE cartridge can be achieved by pressurizing the reservoir, or by applying reduced pressure to the SPE outlet. For organic solvents, gravity may be sufficient for washing and elution steps. Aqueous samples require a pressure differential between inlet and outlet of the cartridge.
For individual samples, it is sometimes most convenient to use a syringe to pressurize the reservoir to effect the flow. However, vacuum manifolds have been developed that permit parallel processing of multiple samples. Vacuum manifolds also provides better control of elution flowrate, which equates to improved reproducibility for quantitation. Specially designed SPE cartridges are available for use with centrifugation for loading, washing, and elution steps.
In general, SPE methods benefit from the use of slow solvent flowrates. A couple of rules of thumb can guide the development of new SPE methods. For generic reversed-phase or normal phase SPE methods, a flowrate of 5 mL/min or less can be recommended. Because the kinetics of ion exchange is slower than with other retention mechanisms, a flow rate of 2 mL/min or less is recommended. Higher recoveries have been reported for dropwise flowrates.
With proper solvent selection, quantitative washing and elution steps are usually achieved with a volume of solvent equal to the volume of the reservoir.

## Slide 7: Steps in the use of SPE
Condition the SPE cartridge
  Reversed-phase: methanol
  Normal phase: sample solvent
Load the sample
Wash the sample
Elute the sample
Notes: Most applications of SPE use the same basic steps for sample cleanup. Differences will exist among methods for applications that retain the analytes compared with applications that retain the interferences.
The first step is to condition the SPE cartridge with an appropriate solvent. For reversed phase applications, methanol or acetonitrile are commonly used. For all other applications, use the same solvent as is in the sample. Fill the reservoir with this solvent, and then allow the solvent to drain from the SPE, but do not let the sorbent bed dry. Stop the flow with a couple of mm’s solvent remaining above the tube frit.
Apply the sample to the SPE reservoir, and then elute the sample solution with either positive pressure from a syringe or reduced pressure from a vacuum manifold.
Fill the reservoir one or more times with an appropriate wash solvent, and elute the solvent. The wash solvent should remove unwanted components, but should not elute the target analytes.
Finally, elute the target analytes with a stronger solvent and collect this fraction for analysis.

## Slide 8: Method Development
Identify the desired result
  Sample cleanup (isolation of analytes from matrix)
  Sample concentration
Identify the sample matrix
  Organic
  Aqueous
Identify analyte properties
  Polarity
  Ionizability
Identify potential separation scheme; select SPE chemistry
  Retention of analyte
  Retention of interfering compounds
Notes: The development of a new SPE method can require considerable effort. Knowledge of the properties of the analytes, interferences, matrix components, and desired goals are essential to successful method development. Fortunately, most manufacturers of SPE cartridges and equipment provide in-depth guides to assist in method development, usually in the form of a flow chart. A few steps in this processed can be summarized.
The first step in the process is to identify the desired goals. Usually SPE is used for sample cleanup and concentration, but other goals are possible, including solvent exchange, derivatization, and fractionation, which is a type of cleanup step.
Selection of the most appropriate SPE cartridge requires in-depth knowledge of the sample. Different methods are usually required for aqueous samples and samples in an organic solvent.
The retention mechanism is key to method development, and depends on both the properties of the analytes and the interferences. If either analytes or interfering compounds are ionizable, highly selective methods can be developed based on ion exchange. In such cases, the pH of the eluent is adjusted such that the species to be retained is fully ionized, typically at least 2 pH units above or below the pKa of the target species, for acids or bases, respectively. For aqueous samples, nonpolar species are separated from polar species by reversed-phase SPE. If the sample is dissolved in a nonpolar solvent such as hexane, polar and nonpolar species can be separated with normal phase SPE, using silica, alumina, Florisil, or aminopropyl adsorbents.

## Slide 9: Method Development: mode of separation
biological fluids
mixed mode SPE
retain interferences
elute analyte for analysis
retain interferences
elute analyte for analysis
retain analyte
elute interferences to waste
retain analyte
elute interferences to waste
neutral
interferences
ionizable
interferences
normal phase
reversed-phase
organic solvent
water soluble
immiscible
water miscible
nonizable
analytes
ionizable
analytes
Sample (extract)
ION EXCHANGE
REVERSED-PHASE
NORMAL PHASE
MIXED MODE
Notes: The following flow chart illustrates steps that can be used in developing a SPE method. The different pathways indicated will be discussed in the following slides. A variety of approaches can be employed, and different approaches may work well with the same sample. For solid samples such as particulates, Solid-Phase extraction can be considered a fractionation or cleanup step, rather than an extraction method. Samples to be processed must be in solution form, and need to be extracted from the solid matrix with a solvent, using an extraction method such as soxhlet extraction, pressurized fluid extraction, or sonication extraction.
In developing a SPE method for processing the extract, the possible approaches can be narrowed by considering the properties of both the analytes and potential interferences
The first step is to identify the solvent to be used to extract the sample. If the sample can be dissolved in a water soluble matrix, ion exchange and reversed-phase SPE are potential approaches for sample cleanup. If the sample extract is soluble in an organic solvent that is not water miscible, then normal phase SPE is indicated. In the next few slides, more detail is presented for each of these paths.

## Slide 10: Method Development: Ion Exchange
water soluble
Sample (extract)
ION EXCHANGE
biological fluids
mixed mode SPE
retain interferences
elute analyte for analysis
retain analyte
elute interferences to waste
neutral
interferences
ionizable
interferences
ionizable
analytes
MIXED MODE
Notes: If the analytes are ionizable, then ion exchange is often the method of choice. Ion exchange provides a high degree of selectivity, and retention can be controlled by adjusting the pH of the eluent. Basic species are retained with cation exchange sorbent, at pH environments at least 2 pH units below their pKa. Acidic species are retained with anion exchange sorbents, at pH environments at least 2 pH units above their pKa.
If the matrix interferences are primarily neutral, then conditions can be adjusted to retain the analyte and elute the interferences to waste in wash steps.
However, if the matrix interferences are also ionizable, then the analyst has a choice in the method development to retain the interfering compounds and elute the analyte, or retain the analyte and elute the interferences. This decision depends on the pKa’s of the various species. Typically, at least 2 pH units difference in pKa’s is needed to provide full separation. Elution of group of compounds is effected by adjusting the pH of the eluent at least 2 pH units above or below the pKa for that group, such that the compounds are forced into the neutral species. The compounds to be retained must maintain their ionic state for the separation to work.
Samples with a high ionic strength matrix, such as biological fluids, are sometime best processed using a mixed mode SPE adsorbent that utilizes ion exchange and reversed-phase interaction mechanisms. Analytes are strongly retained by the dual retention mechanisms, whereas conditions are adjusted to elute the high salt matrix components to waste.

## Slide 11: Method Development: Reversed-Phase
retain analyte
elute interferences to waste
reversed-phase
organic solvent
water soluble
water miscible
nonizable
analytes
Sample (extract)
REVERSED-PHASE
Notes: Reversed-phase SPE cleanup methods are often indicated for aqueous sample extracts, or extracts in organic solvents that are miscible with water. For the typical application, the sample is loaded onto a hydrophobic SPE cartridge with a C18 or phenyl stationary phase. The cartridge is washed with a polar solvent to elute the polar interferences. The nonpolar analytes are subsequently collected for analysis by elution from the SPE with a stronger, less-polar solvent.

## Slide 12: Method Development: Normal Phase
retain interferences
elute analyte for analysis
normal phase
organic solvent
immiscible
Sample (extract)
NORMAL PHASE
Notes: If the sample is extracted with a nonpolar solvent that is not miscible with water (such as hexane or toluene), normal phase SPE can be used to separate polar compounds from nonpolar compounds. Under these conditions, ionic species are not present. Common normal phase adsorbents include aminopropyl, silica, alumina, and Florisil. The sample is loaded onto the SPE cartridge in the hexane environment, and eluted with more polar solvents such as methylene chloride. The elution order is opposite from reversed-phase separations. The most nonpolar compounds elute first, and are followed by compounds that are increasingly polar.

## Slide 13
Notes: The use of a Solid Phase Extraction cartridge with a syringe is very similar to its use with a vacuum manifold, except that the syringe provides positive pressure at the inlet of the cartridge, rather than negative pressure at the outlet.
Begin by attaching the SPE cartridge onto the end of the syringe. It is good practice to remove the SPE cartridge from the syringe when the syringe barrel is withdrawn, to prevent aspiration of air through the cartridge, and potential sample loss.
To use the SPE cartridge, it first must be conditioned in a 2-step process. Begin by washing the cartridge with an appropriate solvent to wet the adsorbent. For reversed phase adsorbents, methanol or acetonitrile is typically used. After eluting the solvent, apply several mL’s of water to the cartridge. Don’t allow the cartridge to dry between steps. After eluting the water, the sample can be loaded. For normal phase adsorbents, hexane or other alkanes are often used to condition the SPE cartridge in a single step.
Fill the reservoir with an appropriate quantity of the sample, and apply the sample to the SPE bed with a dropwise flow rate, taking at least 15 to 30 seconds or longer. With the sample loaded onto the cartridge, rinse and elution steps can be carried out, as required by the SPE method.
The following video segment illustrates the use of an SPE vacuum manifold. The manifold consists of a transparent base with a pressure gauge and release valve, a tube holder for placement of tubes to accept waste or sample eluent, and a cover with valves to accept the SPE cartridges. These SPE ports have guide tubes to direct the eluent into adjacent tubes. These parts can be disassembled between uses for cleaning to prevent cross contamination of samples.
Two types of SPE cartridges are shown. At the left is a cartridge without integral reservoir, and at the right is a one piece SPE cartridge with reservoir.
The first step is to condition the SPE cartridge prior to loading the sample. With the manifold assembled and with the sample valves closed, reduced the pressure to the manifold. For most types of SPE adsorbents, about 3 to 5 mL of methanol or acetonitrile is added to the reservoir and the sample valve is opened to allow dropwise flow through the cartridge. This step is repeated with solvent composition the same as for the sample. After conditioning, the SPE cartridge should not be allowed to dry. Either close the sample valve or disconnect the vacuum source.
Replace the sample receptacle tubes with empty tubes. Apply the sample to the SPE reservoir, and adjust the sample valve to result in dropwise loading of the sample onto the cartridge.
Depending on the cleanup method, the SPE cartridge can be washed with solvents of different composition to elute unwanted sample constituents. Typically, the wash solvent should elute interferences but not sample constituents of interest. After the wash steps, the target analytes are eluted using appropriate solvent compositions.
For the development of a new SPE method, the eluent from the wash and elution steps must be analyzed to verify that the solvent composition is appropriate for the intended result. For example, the wash step must not elute any of the targeted analytes, and the elution step should provide complete recovery of these analytes.
To learn more about the National Institute of Standards and Technology, visit www.nist.gov