## Slide 1: Industrial Research Applications of Neutron Scattering
NCNR/CHRNS Summer School
July 22-26, 2024
Hubert King
Stony Brook  IBM Research  ExxonMobil (retired)  NCNR
A STORY IN THREE PARTS
A look at industries impacted
A path for industry to utilize NCNR
A few examples

## Slide 2: Industrial Impact from 2024 RTI Report
Commercial Products/Services: Isotope Production & Transmutation (P in Si)
Walsh, A. C., Nienow, S., Merker, J. M. S., Decker, E. C., Strack, C. N., Salem, M. E., Martin, G., & Shaw, B. (2024). Assessment of the retrospective and prospective economic impacts of investments in U.S. neutron research sources and facilities from 1960 to 2030: Final report. RTI International
Notes: Additionally, neutrons can characterize magnetic fields at depth or at low temperatures, which has helped with the development of small and powerful semiconductors and other electrical components for hard drives and cell phones
(CINS, 2016). Companies using neutron scattering for these purposes include Dow Chemical and PPG Industries in the chemicals and gases industry, Coherent Corp. and Raychem in the electrical equipment industry, and Intel and Texas Instruments in the semiconductor industry.
Research on giant magnetoresistance (GMR) serves to illustrate how neutron scattering techniques promoted the development of hard drive technology. GMR occurs when a system of extremely small (nanometer or subnanometer in width) alternating magnetic and nonmagnetic conductive layers undergoes a major change in electrical resistance after being exposed to an external magnetic field (Pessoa Barradas, 2017). GMR enabled hard drives to detect the presence of even extremely small magnetic fields, allowing them to store and access significantly more information (Pessoa Barradas, 2017). The high-density magnetic recording of modern hard drives would not have been possible without the discovery of the GMR effect (Pessoa Barradas, 2017). Crucially, using GMR for this purpose depends on a thorough understanding of the characteristics of each nanolayer in a hard drive (Pessoa Barradas, 2017). Polarized neutron reflectometry, a specific type of neutron scattering, is uniquely suited for acquiring this understanding and is described as the “technique of choice” for this matter (Pessoa Barradas, 2017).

## Slide 3: Patent Activity Shows Growth and Impact

## Slide 4: How Can Industry Access and Develop Experimental Neutron Facilities?
nSoft
Solutions to challenges
Measurement Needs
Materials Science
Neutron-based Measurements
nSoft: Provides a non-proprietary environment where soft materials manufacturers gain expertise and drive innovation in neutron measurements.
Over 20 industry affiliates and now growing with expansion beyond soft-materials
Jonathan Seppala, director

## Slide 5: Example Research Activities
AFL
Rheo-SANS
R. P. Murphy, et al. Soft Matter, 2020.
Neutron Imaging
Auto Formulation Lab:
AI meets Experiment Design
Fuel Cells and Rocks
Structure & Rheology Impacts Processing

## Slide 10
Designing Stable Drug Delivery Suspensions (liquids)
Eli Lilly:
Ken K. Qian
David P. Allen
University of Delaware/NIST
Peter Gilbert (NCNR/University of Delaware)
Rachel Ford (NCNR/University of Delaware)
Norman J. Wagner (Uni. of Delaware)
Yun Liu (NCNR/University of Delaware)

## Slide 11
The Problem: Drug Storage and Delivery Affected
Polysorbate 80: solubility in water is about 100 mg/ml
m-cresol: solubility in water is larger than 20 mg/ml
However,
0 mg/mL
1.3 mg/mL
1.9 mg/mL
2.5 mg/mL
3.15 mg/mL
Preservative
Conc.
(m-Cresol)
1mg/ml PS80
Non-ionic surfactant
Preservative

## Slide 12
PS80 micelles
~ 66 Å
~34 Å
~70 Å
~28 Å
Gilbert, et al. J. Pharm. Sci. 110, 2395-2404 (2021).
Polysorbate 80 Micelles Too Small to Account for Cloudy Solution

## Slide 13
PS80 micelles+ m-Cresol
0.5 mg/mL PS80 + 3.15 mg/mL m-cresol
in Unbuffered D2O
Change with Time
Gilbert, et al. J. Pharm. Sci. 110, 2395-2404 (2021).
Cloudy

## Slide 14
PS80 micelles+ m-Cresol
Aggregation kinetics
1 mg/mL PS80 + 3.15 mg/mL m-cresol
Unbuffered D2O (22 ºC)
Aggregate Volume
Gyration Radius
Time
Gilbert, et al. J. Pharm. Sci. 110, 2395-2404 (2021).

## Slide 15
PS80 micelles+ m-Cresol:
Growth of the aggregate size
1 mg/mL PS80 + 3.15 mg/mL m-cresol
Unbuffered D2O
Gilbert, et al. J. Pharm. Sci. 110, 2395-2404 (2021).
Aggregates Continue to Grow at Low T, Exhibit Universal Power-Law Growth. Diffusion Limited Aggregation

## Slide 16
Conclusions
Adding m-Cresol introduces aggregation in some PS80 solutions.
There are two steps for the aggregation formation. The size of the aggregates grows as t1/3 at the second step.
The kinetics of the aggregation are very sensitive to the buffer conditions.
SAXS/SANS is a powerful tool to study the morphology and their changes of macromolecules in solution.
Gilbert, et al. J. Pharm. Sci. 110, 2395-2404 (2021).
Gilbert, et al. Mol. Pharm. 19(3), 862-875 (2022).

## Slide 21: Neutron Research Yields Substantial Impacts Past, Present and Future
Walsh, A. C., Nienow, S., Merker, J. M. S., Decker, E. C., Strack, C. N., Salem, M. E., Martin, G., & Shaw, B. (2024). Assessment of the retrospective and prospective economic impacts of investments in U.S. neutron research sources and facilities from 1960 to 2030: Final report. RTI International.
Four Case Studies
Computer Performance
Aerospace Safety
BioPharma
Electric Vehicles
Neutron scattering research facilities have generated a Net Present Value of $29.4 billion
Driven by research using polarized neutron reflectometry on giant magnetoresistance (GMR) materials