## Slide 1: The NIST Research Reactor (NBSR), Cold Neutrons, and Reactor Engineering Work at the NIST Center for Neutron Research
NIST Center for Neutron Research
100 Bureau Dr., 20899 Gaithersburg, MD, USA
Abdullah G. Weiss, PhD Nuclear Engineer Reactor Design & Safety Team Leader
July 23rd, 2024

## Slide 2: Outline
Nuclear fission basics (What is a nuclear reactor?)
NBSR Description & History
Cold Sources
Current Developments
New Reactor Stuff
Q/A

## Slide 3: Nuclear Fission & Fuel
Breaking an atom apart
  Releases a lot of thermal energy
  Also releases fission products (other isotopes)
  Usually done with a fuel
    Fissile material (235U)
    Fissionable material (238U)
235U
n
n
n
n
141Ba
92Kr
~200 MeV
We can boil water with this!
Pellets
Plates
Pebbles
Molten Salt

## Slide 4: Nuclear Reactors
Contain fuel, coolant, and (if thermal spectrum) moderator
Also must contain a form of control on the neutron population
  Control/shim rods/arms
  Made of strong neutron absorbers (Cd, B, Hf)
Radiation shielding, detectors, and a neutron source (to initialize the chain rxn) are also needed
Moderator
Biological Shield

## Slide 5: Types of Nuclear Reactors Water systems
https://www.britannica.com/technology/nuclear-reactor/Types-of-reactors

## Slide 6: Types of Nuclear Reactors Pebble bed systems
https://upload.wikimedia.org/wikipedia/commons/thumb/0/0f/Pebble_bed_reactor_scheme_%28English%29.svg/1200px-Pebble_bed_reactor_scheme_%28English%29.svg.png

## Slide 7: The NBSR Overview
Top Grid Plate
Fuel Elements (30)
Fuel Plates
Liquid Hydrogen Cold Neutron Source
Bottom Grid Plate
D2O Primary Inlet Plenums
Cd Shim Safety Arms (4)
Reactor Vessel
Radial Beam Tubes (9)
Split Core:
18-cm Unfueled Gap – Flux Trap
Primary Outlet (2)
Thermal Shield

## Slide 8: The NBSR Core Characteristics
HEU fuel (93% 235U) – U3O8+Al
  350 g 235U/fuel element
  34 plates: 11”2.5”0.02”
  Heavy water coolant (D2O)
30 Fuel Elements
  ~38-day fuel cycle at 20 MW
  4 fresh elements per cycle (usually) with a management scheme to shuffle other elements in the core
  ~960 g of 235U consumed per cycle
  7 or 8 cycles per element depending on where it is loaded initially
Axially split-core
  BTs and CNS(s) are at the thermal neutron flux trap elevation
  BT fluxes ~ 1.51014 n/cm2-s

## Slide 9: The NBSR Core Characteristics
CNS
BT-9

## Slide 10: The NBSR History
Designed in 1960s (included a beam port for a single cold source)
It first reached criticality on December 7th, 1967
Originally it was a 10 MW reactor
Converted to 20 MW in 1985
Cold Neutron Facility
  D2O cold neutron source (CNS) installed in 1987
  LH2 CNS installed in 1995
  An advanced LH2 CNS installed in 2002
  Peewee (smaller CNS) installed in 2012 in BT-9
  An upcoming cold source upgrade is planned

## Slide 11: The NBSR Instruments Layout
Main CNS
Peewee

## Slide 12: Neutron Thermalization
Fission neutrons are ~2 MeV (fast)
Thermalized (20 – 400 meV) via scattering off of the D2O moderator in the core
  D2O is ~320 K (115 ), which is what dictates the thermal energy of the neutrons
  Can be calculated with particle kinematics (classical mechanics formulae)
To reach lower energies, you introduce a cryogenic facility, the cold neutron source (CNS)
  Currently liquid hydrogen (LH2) at 20 K.
https://ars.els-cdn.com/content/image/1-s2.0-S0306454919300180-gr7.jpg
https://www.nrc.gov/docs/ML1214/ML12142A083.pdf

## Slide 13: Neutron Flux in the NBSR Flux Trap (10 MW)
Obtained from NBSR-9 SAR
Flux Trap

## Slide 14: How do we produce cold neutrons?
Fission neutrons are ~2 MeV (fast)
Thermalized (20 – 400 meV) via scattering off of the D2O moderator in the core
  D2O is ~320 K (115 ), which is what dictates the thermal energy of the neutrons
To reach lower energies, you introduce a cryogenic facility, the cold neutron source (CNS)
  Currently liquid hydrogen (LH2) at 20 K.
Installation of LH2 CNS (Nov. 2001)

## Slide 15: The Cold Source Through the years
D2O tank (1967)
D2O Ice (1987)
  Gain of 3-5x in brightness
Unit 1 LH2 (1995)
  Gain of ~6x
Unit 2 LH2 (2002)
  Gain of ~2x
LD2 (Planned)
55 cm Diameter

## Slide 16: The Current Cold Source Unit 2
Passively safe and simple to operate (and reliable)
Utilizes a thermosiphon system to supply the CNS with LH2
Closed system
He containments

## Slide 17: The OTHER Cold Source Peewee
“Peewee” installed on BT-9 (MACS-II)
  11 cm ID, ½ L volume
  Gain of ~1.7 over being directly installed on Unit 2
  14.6 cm D2O jacket and its own H2 tank
  Condenser is cooled in parallel with Unit 2
Operating successfully since April 2012
Notes: MACS=Multi-axis Cyrstal Spectrometer

## Slide 18: The OTHER Cold Source Peewee
Installation of peewee (Sep. 2011)

## Slide 19: We Also Have Rabbit Tubes
RT-2
RT-1
Pneumatically-driven sample insertion and removal systems
Used for in-core irradiation

## Slide 20: Developments NBSR Recovery
February 3rd refueling accident
  Highest internal dose received by any personnel was 5.2 mrem (520 bananas, or ~75% of dose from living in a stone, brick, or concrete building for a year)
Cleaning of primary system was conducted
Fuel loading analysis completed
  Currently updated to meet operations developments
New training program developed
New Reactor aging management program developed
Obtained restart authorization from NRC!
Restarted safely
Currently doing low-power testing

## Slide 21: Developments NBSR Recovery
Can operate with loose fuel in the water
Can operate with alternative fuel management schemes

## Slide 22: Developments NBSR Recovery 2.0
Aug. 8th, 2023: un-anticipated loss of power
Reactor was operating at 1 MW
NIST general electrical maintenance outside NCNR caused loss of power at multiple NIST buildings, including NCNR
Loss of power initiated a temporary shutdown of ventilation, allowing fission gases to be released through confinement
Several personnel got minor contamination
  100 counts per minute (~1.7 Bq)
  Dose was minimal, roughly <0.5 mrem
    Equivalent to roughly 50 bananas
    Less than half the dose of a flight from DC to Boulder, CO
Consequences yielded additional oversight and administrative controls to prevent such accidents in the future.
Additional recovery efforts initiated to further clean the NBSR & its systems.
Predicted Total Mass of Loose U3O8 if concentrated in any given location in the core
(0-5 grams scale)

## Slide 23: Developments NBSR Recovery 2.0
Additional recovery work includes QA programs development, Ageing reactor management processes development, power noise monitoring system, fuel detection technique, control room upgrades, Thermal column work, Work towards relicensing, SSC classifications and setpoint developments, Integration of reliability and risk assessment techniques, Secondary loop work, cold source upgrade work, LEU conversion, New reactor development. (I probably missed some)

## Slide 24: Developments LEU Conversion
US High Performance Research Reactors Conversion Program
  Collaboration with several DOE laboratories (ANL, INL, BNL, ORNL)
  To meet US and international non-proliferation goals
Converting to U-10Mo HALEU (19.75% enrichment)
Finished Rev. 1 of the drawings and fuel specification document for the NBSR U-10Mo.
  Working on a unified version for all US high-performance research reactors converting to U-10Mo LEU fuel.
Working on irradiation and qualification plan and schedule for the test NBSR LEU fuel element at BR-2 (SCK-CEN).

## Slide 25: Developments Cold Source Upgrade
Planned NBSR LEU conversion results in 10% reduction in thermal and cold neutron beams, which can be mitigated by replacing LH2 to LD2.
Support for some of these modifications comes from US NNSA
Increase in cryogenic heat load to ~4 kW
Already purchased and installed a new 7 kW fridge to accommodate the heat load increase.

## Slide 26: Developments Cold Source Upgrade
Planned NBSR LEU conversion results in 10% reduction in thermal and cold neutron beams, which can be mitigated by replacing LH2 to LD2.
Support for some of these modifications comes from US NNSA
Increase in cryogenic heat load to ~4 kW
Already purchased and installed a new 7 kW fridge to accommodate the heat load increase (will still use the thermosiphon system).
D2O Jacket
Vacuum Jacket (thin wall)
LD2 Supply Line
D2 Return Line
Moderator Chamber

## Slide 27: Developments Cold Source Upgrade
Cryostat Assembly
Shield Plug
Condenser Enclosure
LD2 Transfer Lines

## Slide 28: Developments Cold Source Upgrade

## Slide 29: Developments Cold Source Upgrade
LD2 Source (2025?)
BT-9 LH2 Source (installed 2012)

## Slide 30: Developments Cold Source Upgrade
Radiation source | Unit 2 |  | PeeWee |  | LD2 | 
 | H2 | Al | H2 | Al | D2 | Al
Neutrons | 104 | 3 | 33 | 1 | 440 | 6
Beta Particles |  | 308 |  | 29 |  | 567
Gamma rays | 185 | 815 | 25 | 74 | 1053 | 1538
Subtotal | 281 | 1080 | 58 | 104 | 1493 | 2111
Total cryogenic heat load [w] | 1361 |  | 162 |  | 3604 | 
 | LH2 (PeeWee) | LH2 (Unit 2) | LD2 (Proposed)
Operating Pressure (kPa) | 200 | 100 | 100 - 200
B.P. (K) | 23.0 | 20.4 | 23.2 – 25.9
M.P (K) | 14 | 13.8 | 18.8 - 19.0
Density (kg/m3) | 67.5 | 70 | 164 - 157
Geometry | Disk | Elliptical Annulus | Cylindrical
Dimensions (cm) | 11 | 32 x 24 | 40 x 40
Wall Thickness (mm) | 4.5 | 2.3 | 3.2
Liquid Volume (L) | 0.45 | 5 | 35
Mass (kg) | 0.03 | 0.32 | 5.2
Al Mass (kg) | 0.14 | 0.28 | 7.2
Heat Load (kW) | 0.16 | 1.2 | 3.6

## Slide 31: The Future
The New Reactor: NIST Neutron Source (NNS)

## Slide 32: Why a new reactor?
A study on future options for the NCNR -> replacement reactor is the best option
  Refurbish and Replace NBSR Internals
    No advancement as a neutron source, and similar cost to building a new reactor.
  Keep NBSR Operational
    long-term uncertainty in the condition of the reactor
  Spallation Source
    Steady-state reactor sources are complementary to pulsed accelerator-based neutron sources
  New Core inside NBSR
    Retains the ageing issues of NBSR, and it is likely as expensive as a new reactor.
  New Reactor
    A clean slate: ultimately the best path forward. Allows “Ideal’ neutron source design

## Slide 33: Why a new reactor?
The Law: H.R.4346 – Chips and Science Act, Sec. 10231. Neutron Scattering
STRATEGIC PLAN FOR THE INSTITUTE NEUTRON REACTOR.—The Director shall develop a strategic plan for the future of the NIST Center for Neutron Research after the current neutron reactor is decommissioned, including—
  a succession plan for the reactor, including a roadmap with timeline and milestones;
  conceptual design of a new reactor and accompanying facilities, as appropriate; and
  a plan to minimize disruption to the user community during the transition.
COORDINATION WITH THE DEPARTMENT OF ENERGY.—The Secretary, acting through the Director, shall coordinate with the Secretary of Energy on issues related to Federal support for neutron science, including estimation of long-term needs for research using neutron sources, and planning efforts for future facilities to meet such needs.

## Slide 34: Design of NNS Overview
Influenced by several reactors designed for neutron science
Nominal power of 20 MW
U-10Mo LEU (or U3Si2)
Light-water-cooled compact reactor core
Surrounded by heavy-water in the reflector tank
2 Cold Neutron Sources
8 Thermal Neutron Beams
40 days operating cycle
Reactor Pool and Primary Coolant System
Reflector tank with surrounding features

## Slide 35: Design of NNS Core, Cold Sources, and Reflector Tank
Reflector Tank with the core, cold sources, and beam tubes
Thermal Beams
Cold Neutron Guides
Cold Sources
Core
35
Chimney

## Slide 36: Design of NNS Core
Nine fuel assemblies (FA) in a 3x3 array
Each FA contains 21 U-10Mo fuel plates
19.75% enriched Y-12 fuel wrapped with ~8 µm thick zirconium foil
Four control blades and two safety blades placed in the center within two guide boxes
Core horizontally divided into three rows
64 coolant channels at each row
Optimize fuel cycle length & maintain a negative reactivity feedback
Reactor Core
Fuel Assembly
x9
x4
x2
x2
24 cm
29 cm

## Slide 37: Design of NNS
Fuel Assembly Top View
Cd Poison Rods x42
Coolant Channels
Fuel Plates x21
Side Plate
8.05 cm

## Slide 38: Core Power Analyses
Normalized Power Heatmap of Assemblies in Each Cycle State
NNS Current Fuel Management Scheme

## Slide 39: Core Power Analyses
Detailed relative power distributions of the 1st and last fuel plate in each assembly
Axial-averaged relative powers of each fuel plate

## Slide 40: Core Neutron Flux Distributions
“Cold”
(<0.025 eV)
“Thermal”
(0.025 – 0.4 eV)
“Fast”
(100 keV – 20 MeV)

## Slide 41: Thermal (<0.3eV) neutron flux
NBSR
NNS

## Slide 42: Fission Density Discharge
Elevated power densities for 2nd cycle FAs are observed with values greater than 18 kW/cm3 and are accompanied with fission densities in the range of 1.5 – 2 × 1021 cm-3. The 3rd cycle fuel assemblies have suppressed power densities with elevated fission densities in excess of 3 × 1021 cm -3. The maximum fission density is found to be 4.47 × 1021 cm -3.
NNS
Power and Fission Density Profiles in other USHPRR (modified and reproduced)

## Slide 43: Core Thermal Hydraulics
CFD Model of Normalized Streamwise Velocity Profile of NNS Inlet
Analyses show no departure from nucleate boiling (DNBR) at any cycle state.
Maximum bulk temperature was nearly uniform in all channels and remains below 335 K.
Maximum cladding temperature remains below 365K.
CFD work is ongoing to assess the flow behavior at the inlet of the core (do we have undercooled channels?).
Work is starting to assess the design of the chimney and the outlet of the NNS (how tall should it be? how should the outlet connection look?).
DNBR is @ mCHFR=1

## Slide 44: Core Thermal Hydraulics More CFD
CFD Modeling of the NNS Inlet
(Streamwise and Spanwise velocities shown)
CFD Modeling of the NNS Outlet
(Streamwise velocity and vectors are shown)
10 kPa pressure at the chimney outlet is assumed

## Slide 45: Thermal Hydraulics Hot Channel in Normal Operation
Safety Criterion | Correlation | NNS | NNS | NBSR | NBSR
 |  | System | Core (SU) | HEU | LEU
CHFR | Mirshak | 3.03 | 3.09 | 3.04 | -
 | Sudo-Kaminaga | 3.22 | 3.28 | 3.99 | 3.96
OFIR | Saha-Zuber | 7.17 | 7.22 | 5.50 | 5.61
 | Costa | 5.62 | 5.48 | - | -
ONBR | Bergles-Rosenhow | 1.96 | 2.15 | - | -

## Slide 46: Proposed Cold Neutron Instruments
Plan view through the fuel center of the reactor core
Instrument type | Total Number | End position
Small-Angle Neutron Scattering (SANS) | 2-3 | YES
Reflectometer (CANDOR type) | 2 | YES
Cold Neutron Imaging (CNI) | 2 | YES
Cold 3-Axis (CN3X) | 2 | YES
Backscattering (BS) | 2 | YES/NO?
Neutron Spin-Echo (NSE) (Mezei-type) | 1 | YES
Neutron Spin-Echo (NSE) (WASP type) | 1 | YES
High current physics experimental position (Physics) | 1 | YES
Prompt Gamma Activation Analysis (PGAA) | 1 | YES
Neutron Depth Profiling (NDP) | 1 | YES
Materials Diffractometer (λ > 0.3 nm)? | 1? | YES
Interferometer | 1? | NO
Monochromatic Physical Measurements Laboratory (PML) positions | 2-3? | NO
Miscellaneous monochromatic/ test positions | 2-3? | NO
Very Small-Angle Neutron Scattering (vSANS) | 1 | YES
TOTAL | 22-25 | 16-18
Proposed Cold Neutron Instruments

## Slide 47: Proposed Thermal Neutron Instruments
View of Potential Thermal Instruments
Proposed Thermal Neutron Instruments
Instrument Type | Abbreviation
Prompt Gamma Neutron Activation Analysis | PGNAA
Neutron Microscope | Imaging
High-Resolution powder diffractometer | D
Triple Axis Spectrometer | 3X
Ultra-Small Angle Neutron Scattering | USANS
High Throughput Fast Powder Diffractometer | D
White Beam Engineering Diffractometer (with CANDOR-type detector) | ENG
High Current Physics Experimental Position | PHYS

## Slide 48: Performance Comparison
OPAL-like CNS
Courtesy of Jeremy C. Cook
Notes: NNS CNS model cold neutron brightness ratios with respect to the anticipated NBSR LD2 Unit 3 CNS brightness for the LD2 vessel diameters indicated in the legend. These curves are obtained from ratios of the brightness curves shown in Figure 2. The reference OPAL-like (Æ 30 cm) CNS model is represented by the black circles.

## Slide 49: NNS Publications (since Oct. 2022)
D. Şahin, et al., “NIST Neutron Source Preconceptual Design”, Proceedings of RERTR, Oct. 2022.
O. Çelikten, et al., “Highlights of Neutronics Analyses for the Pre-conceptual NIST Neutron Source Design”, Proceedings of American Nuclear Society, Nov. 2022.
I.R. Baroukh, et al., “A Preliminary Thermal-hydraulics Analysis for the NIST Neutron Source”, Proceedings of American Nuclear Society, Nov. 2022.
I.R. Baroukh, et al., “Preliminary CFD Investigations for the NIST Neutron Source”, Proceedings of American Nuclear Society, Nov. 2022.
J.C. Cook, et al., “Proposed NIST Neutron Source User Facility”, Proceedings of American Nuclear Society, Nov. 2022.
J.C. Cook, et al., “Neutron Delivery Systems Design of the Proposed NIST Neutron Source”, Proceedings of American Nuclear Society, Nov. 2022.
D. Şahin, et al., “Pre-Conceptual Design of the NIST Neutron Source”, Proceedings of RRFM, April 2023.
A.G. Weiss, et al., “Modeling Approach for the Design of the NIST Neutron Source”, Proceedings of RRFM, April 2023.
O. Çelikten, et al., “Comparison of U3Si2 and U-10Mo LEU-fueled Reactor Cores for the Preconceptual NIST Neutron Source Design”, Proceedings of ICONE30, May 2023.
J. Shen, et al., “Turbulence Model Sensitivity Analysis of Thermal-Hydraulic Properties on the Pre-Conceptual NIST Neutron Source Design”, Proceedings of ICONE30, May 2023.
A.G. Weiss, et al., “Sensitivity Analyses of the Thermal-hydraulics Safety Margins in the Proposed NIST Neutron Source Design”, Proceedings of ICONE30, May 2023.
Y. Shaposhnik, et al., “Alternative Reflectors for the NIST Neutron Source”, In Transactions of TRTR/IGORR, June 2023.
J. Jurns, et al., “Liquid deuterium cold source concept for the NIST neutron source”, In Proceedings of CEC/IMS 2023, July 2023.
A.G. Weiss, et al., “A Turbulence Model Sensitivity Analysis on the Hydraulic Behavior in the Inlet Plenum of the Proposed NIST Neutron Source Design”, In Proceedings of NURETH-20, Aug. 2023.
A. Gurgen, et al., “Thermal-hydraulic Assessment of the Proposed NIST Neutron Source Design”, In Proceedings of NURETH-20, Aug. 2023.
E. Bures, et al., “Validation and Comparison of 2D and 3D RANS Models for Flow Through Curved Channels in MTR-type Nuclear Fuel Assemblies”, Proceedings of RERTR, Nov. 2023.

## Slide 50: NIST Technical Notes
CNS & Thermal Beams Assessments
Facility Design Planning
Neutronics Safety Assessments
Thermal-hydraulics Safety Assessments
Published
https://doi.org/10.6028/NIST.TN.2280
Published
https://doi.org/10.6028/NIST.TN.2284
In Review
In Review

## Slide 51: Thank you for listening!
Abdullah G. Weiss
NIST Center for Neutron Research
100 Bureau Drive, Gaithersburg, 20899, USA
abdullah.weiss@nist.gov
Questions??
Acknowledgements:
Dağıstan Şahin, Osman Ş. Çelikten, Anil Gurgen, John M. Jurns, Jeremy C. Cook, Timothy F. Mengers

## Slide 52: The NBSR Backup
BACKUP