## Slide 1: Metrology and Entanglement Distribution in Metropolitan Quantum Networks
Thomas Gerrits
Boris Korzh
Oliver Slattery
Josh Bienfang
Alan Migdall
Ivan Burenkov
Sergey Polyakov
Pranish Shrestha
Mheni Merzouki
Abderrahim Amlou
*Any mention of commercial products is for information only; it does not imply recommendation or endorsement by NIST.
Jaden He
Paulina Kuo
Ya-Shian Li-Baboud
Jabir MV
Anouar Rahmouni
Yicheng Shi
Abdella Battou
Riley Dawkins
Jing Su

## Slide 2: NIST Mission
a
©Nicholas McIntosh Photography
©Robert Rathe
Credit: J.Burrus/NIST
To promote U.S. innovation and industrial competitiveness by advancing measurement science, standards, and technology in ways that enhance economic security and improve our quality of life

## Slide 3: Quantum Networking
©Nicholas McIntosh Photography
©Robert Rathe
To promote U.S. innovation and industrial competitiveness by advancing measurement science, standards, and technology in ways that enhance economic security and improve our quality of life
Testbeds
When do things break?
Metrology
How do things break?
Standards
Inform future standards

## Slide 4: It’s All About Transporting Photons
Node
It’s a challenge! Deployed Fibers
Retain information imprinted on photons
Heterogenous operation
quantum link, e.g. fiber
classical link
components
components
C
C
Sources
Detectors
Switches
Fibers
Converters
Memories
Repeaters
Qubits
etc.
components

## Slide 5: Quantum Networking Challenges
Must operate in practical, deployed environment
Compared to Classical Networking, Quantum Networking needs:
  Noise to be 9 orders of magnitude lower
  Timing to be 5 orders of magnitude better
Understand and reduce sources of noise/errors due to more stringent requirements
Measurements will destroy the qubits – a need for non-invasive telemetry

## Slide 6: Quantum Network Metrology Tasks
Fiber polarization stability
Quantum/Classical Coexistence
Fiber loss characterization
Node synchronization
Fiber connector loss characterization
Detector characterization
Notes: Metrology for Quantum
Quantum for Metrology

## Slide 7: Testbeds
to UMD
100 m

## Slide 8: NIST – UMD(JQI) Quantum Network Nodes
Quantum network nodes
Entangled Source
Detectors
Time taggers
Synchronization
Polarization stabilization
14 km
60 km aerial fiber

## Slide 9: Benchmarking Synchronization Systems Polarization Entanglement Distribution Over Aerial Fibers Optical Fiber Connector Loss

## Slide 10: Node synchronization: Entanglement Swapping
*10 ps ≡ 2 mm in fiber
Jin et al, Sci Rep 5, 9333 (2015)
Excellent synchronization is required
Polarization must be stabilized
Photon noise must be mitigated
10’s km
*
Notes: Why do we need stabilization systems? On the right you see a representative graph for a foundational operation on a QN. Entanglement swapping. Entanglement swapping is needed to cover long distances for QNs to mitigate loss that occurs within the optical fiber. Entanglement swapping entails the simultaneous arrival of two photons from distant nodes at the location where the swapping occurs. These photons travel at the speed of light and were very short, about 10 ps to be more precise, and their temporal shape is indicated by this Gaussian envelope. 10 ps at the speed of light corresponds to 2 mm path length in optical fibers. So, we are now trying to solve the challenge of having two photons, at the speed of light, arrive within less than 2 mm from one another after having travelled through ten’s of km of fibers. Also, some very efficient swapping protocols require optical phase stabilization – here we are talking about attosecond stabilization – another 3 orders of magnitude. I guess you can see how difficult this is in a deployed environment. Furthermore, swapping requires both photons to have the same polarization, and therefore polarization must also to stabilized. All of this stabilization has to happen without imposing noise on the delicate quantum photons.

## Slide 11: High-Accuracy PTP Performance
Short term stability
Long term stability
Short term stability: ~ 1 ps
Long term stability: < 5 ps p-p @3 km
< 30 ps p-p @88 km (in lab)
T. Gerrits, et al., CLEO 2022, paper FM1C.2.

## Slide 12: Metropolitan Scale Node Synchronization
GM – BC delay (ps)
Dtp-p = 184 ps
DtFWHM = 60 ps
W. McKenzie, et al., CLEO 2023, paper FF3A.3.
60 km aerial fiber link

## Slide 13: Benchmarking Synchronization Systems
pulsed laser
(pilot)
SNSPD
1538.98
1539.77
1541.35
1550.12
Single-photon
spectrum
Dongxing He, et al., J. Opt. Commun. Netw. 17, 1128-1135 (2025)

## Slide 14: Roundtrip time comparison
Precision of 610 ms roundtrip time-of-flight is less than 2 ps @ 0.5 sec integration time.
Dongxing He, et al., J. Opt. Commun. Netw. 17, 1128-1135 (2025)

## Slide 15: Roundtrip time comparison
Dongxing He, et al., J. Opt. Commun. Netw. 17, 1128-1135 (2025)
Phase error (10’s of ps) matches in amplitude the difference between WR-RTT estimate and time-of-flight.
WR roundtrip time measurement
& WR phase error

## Slide 16: Aerial Polarization State Fidelity Drift
Fidelity vs. time
Fidelity vs. time
Active stabilization is required

## Slide 17: Incorporating Polarization Stabilization in Entanglement Distribution
APC performs compensation if fidelity check result < 98%;
Time-tagging sessions scheduled right after compensation
Y. Shi, et.al. J. Opt. Commun. Netw. 18, 813-819 (2026)

## Slide 18: Entanglement Distribution over Polarization-stabilized fiber: Result
Smean = 2.41 0.09
Quantum channel uptime: 93%
Y. Shi, et.al. J. Opt. Commun. Netw. 18, 813-819 (2026)

## Slide 19: Low-loss, high repeatability fiber connectors
Loss: 0.39 ± 0.21 %
95-percentile: 0.76 %
Evaluate 40x40 random fiber connector matings on a batch of 20 patchcords following IEC 61300-3-34 standard
J. Su et al., CLEO 2026, paper JTU.176.

## Slide 20: Conclusions & Outlook
Metrology will play an important role for the success of Quantum Networks
We are studying the behavior of deployed fibers to mitigate sources of noise
Metrology will be integrated into the quantum network control plane
Synchronization benchmarking can identify errors in node synchronization
Successful distribution of entanglement over a 60 km aerial noisy fiber link
Thank you!
gerrits@nist.gov
We are hiring!!! Now accepting applications for Postdoc and Graduate Student positions in experimental quantum optics for quantum networking.

## Slide 21: Device Metrics - Dictionary
A common language to promote clarity in communication
Provides clarity on datasheets
Serves as basis for standard development