## Slide 1: Chapter 8 Robust Designs

## Slide 2: Robust Designs
C
S
R
O
R
Focus: A Few Primary Factors
Output: Best/Robust Settings

## Slide 3: Robust Designs
C
S
R
O
R
I/O Arrays
Assembled Designs

## Slide 4: Robust Experimentation
Try to reduce the variation in the product.process, not just set it on target.
Try to find conditions of design factors which make the product/process insensitive or robust to its environment.
The idea was championed by Genichi Taguchi.
  Taguchi really opened a whole area that previously had been talked about only by a few very applied people.
  His methodology is heavily dependent on design of experiments, but he wanted to look at not just the mean but also the variance.

## Slide 5: Classification of Factors
Control Factors–Design factors that are to be set at optimal levels to improve quality and reduce sensitivity to noise
  Dimensions of parts, type of material, etc
Noise Factors–Factors that represent the noise that is expected in production or in use
  Dimensional variation
  Operating Temperature
Adjustment Factor – Affects the mean but not the variance of a response
  Deposition time in silicon wafer fabrication
Signal Factors – Set by the user to communicate desires of the user
  Position of the gas pedal

## Slide 6: Example: Ignition Coil
Most automotive sub-assemblies like the alternator, the ignition coil, and the electronic control module must undergo testing to determine if they are resistant to salt water that may be splashed on them from the read. An automotive supplier is testing an ignition coil to determine if it will withstand salt water. The following factors are tested:

## Slide 7: Control or Noise Factor?
Factor | Low Level | High Level | Factor Type
Housing Material | Polyethylene ($9/lb) | Polypropylen ($20/lb) | C
Concentration Of Salt | 10% | 20% | N
Water Temperature | 5ºC | 15ºC | N
Water Pressure | 10 PSI | 20 PSI | N
Seal Material | Silicone | Vinyl | C
Seal Thickness | 0.02” | 0.03” | C
Exposure Time | 1 hr. | 5 hrs. | N
Type of Salt | Detroit Blue | Chicago Pink | N

## Slide 8: Taguchi’s Design of Experiments Ideas
Use Orthogonal Arrays (e.g., Resolution III Fractional Factorials) that only estimate main effects and specified interactions.
Intentionally vary the noise factors so that you choose a set of conditions that will work well in the face of the noise expected in the actual application.
Inner/Outer Arrays
  Two statistical designs per experiment:
    A design in the control factors called an inner array
    A design in the noise factors called an outer array
  Good for estimating CxN Factor Interactions.

## Slide 9: Taguchi’s Analysis Ideas Signal to Noise Ratio
A single response which makes a tradeoff between setting the mean to a desirable level while keeping the variance low.
Always try to MAXIMIZE a SN Ratio
There are three types:
  Smaller is Better
  Target is Best
  Larger is Better

## Slide 10: Smaller is Better
Maximize the signal to noise ratio
Run a confirmatory experiment
The signal to noise ratio confounds the mean and the variance together and assumes that the variance is proportional to the mean.

## Slide 11: Examples with the same SNS Ratio

## Slide 12: Target is Best
Maximize the signal to noise ratio
Adjust the mean to target using an adjustment factor that has no effect on the signal to noise ratio
The signal to noise ratio does tend to prefer combinations of levels that decrease noise and are on target, but assumes that the variance is proportional to the mean.
If it isn’t, then the method gives an unknown compromise.

## Slide 13: Larger is Better
Maximize the signal to noise ratio
Run a confirmation
The signal to noise ratio again confounds the mean and the variance together and assumes that the variance is proportional to the mean.

## Slide 14: Sources of Variance
Measurement
Setup
Blocks
Noise Factors
  Manufacturing Variation
  Field Conditions

## Slide 15: Repeats
2 represents measurement error

## Slide 16: Replicates
2 represents measurement and setup error

## Slide 17: Blocks
2 represents variance between blocks
and measurement and setup error.

## Slide 18: Noise Factors
2 represents variance expected in the field due to field conditions and measurement and setup error. The idea of robustness is to set the x’s to minimize the variance, while keeping the average response at a desired level.

## Slide 19: I/O (crossed) Array An Inner Array of Control Factors and an Outer Array of Noise Factors
2 represents variance expected in the field and measurement and setup error.

## Slide 20: Analysis
Taguchi suggests SN Ratios.
We could analyze the average and the standard deviation separately.
We could define some other summary response
  Minimize the range or the curvature
We could include effects for each y and explain each one individually like we do with blocks.

## Slide 21: Analyzing the Mean and Standard Deviation Separately
For each row of y’s, we can take the mean of the row as one response and the log of the standard deviation as another response.
The log is used because the variance of the standard deviation is not constant as the standard deviation increases.
We then try to compromise between setting the mean to a desirable level and reducing the standard deviation.
Effects on the mean are called Location Effects.
Effects on the standard deviation are called Dispersion Effects

## Slide 22: Analysis of I/O (Crossed) Arrays
When we have I/O array there will be three types of effects
  Control Main Effects and Interactions
  Noise Main Effects and Interactions
  Control by Noise Interactions
Depending on HOW WE RUN THE EXPERIMENT, the different effects may have different variances.
Suppose that there are n runs in the control array and m runs in the noise array. There will be a total of nm data points.

## Slide 23: Example: Cake Mix Example
Amounts of ingredients like egg, shortening and flour are the control factors (n levels in the control array)
Time and Temperature in baking are the noise factors (m levels in the noise array)

## Slide 24: How do we run the experiment?
Fully Randomized
Split Plot
Strip Block

## Slide 25: 1. Fully Randomized
Make nm products and test them each separately.

## Slide 26: 2. Split Plot
Experiments where you can’t or don’t think it is worth it to fully randomize the experiment
Used when there are certain effects that you want to estimate with high precision. (like blocking)
Often needed when some factors are “hard to change” and others are “easy to change”
I/O arrays are often but not always run as split plot experiments

## Slide 27: Split Plot Variance
Whole-plot effects have high variance.
Sub-plot effects have lower variance.
Only effects that have the same variance should be put on the same normal plot.

## Slide 28: 2a. Split Plot Arrangement Control Factors as Whole-Plot Effects
Mix up n big batches of batter
Split each batch into m parts
Bake m x n cakes in m x n oven runs
All Control Effects have error due to batch error and due to random error
All Noise Effects and CxN interactions have only random error
2 Normal Plots

## Slide 29: 2b. Split Plot Arrangement Control Factors as Sub-Plot Effects
Mix up m x n batches of batter
Bake all n batter types together under each set of noise conditions
Bake m x n cakes in m oven runs
All Noise Effects have error due to oven error and due to random error
All Control Effects and CxN interactions have only random error
2 Normal Plots

## Slide 30: 3. Strip Block Arrangement
Mix up n batches of batter
Split each batch into m parts
Bake all n batter types together under each set of noise conditions
Bake m x n cakes in m oven runs
All Noise Effects have error due to oven error and due to random error
All Control Effects have error due to batch error and due to random error
CxN interactions have only random error
3 Normal Plots

## Slide 31: The purpose of each of these configurations is to reduce the experimental cost and target certain effects to have higher precision of measurement.

## Slide 32: HOW WE RUN THE EXPERIMENT
Fully Randomize
  Make nm different products and test them each separately
  One normal plot with all effects
Split Plot
  Make n different products and test each product in nm separate tests.
    Two normal plots (1) Control (2) Noise and CxN
  Make nm different products and test them in groups of n in m tests.
    Two normal plots (1) Control and CxN (2) Noise
Strip Block
  Make n different products and test them each in m tests.
    Three normal plots (1) Control (2) CxN (3) Noise

## Slide 33: Control by Noise Factor Interactions
-
1
1
1
1
-
1
-
1
6
0
5
0
4
0
3
0
2
0
T
e
m
p
Moistness
Set Control Factor
(e.g. Shortening) to
Low Level
Noise Factor (e.g. Temp.)
Shortening
Interaction between Shortening and Temperature

## Slide 34: Control by Noise Factor Interactions
Moistness
Set Control Factor
(e.g. Flour) to
Middle Level
Noise Factor (e.g. Temp.)
Flour
Interaction between Flour and Temperature
-
1
1
1
1
-
1
-
1
6
0
5
0
4
0
3
0
2
0
T
e
m
p
M
e
a
n

## Slide 35: Control by Noise Factor Interactions
Moistness
Set the Adjustment
Factor (e.g. Egg) to
Set Mean on Target
Noise Factor (e.g. Temp.)
Egg
Interaction between Egg and Temperature
-
1
1
1
1
-
1
-
1
6
0
5
0
4
0
3
0
2
0
T
e
m
p
M
e
a
n

## Slide 36: I/O Arrays and Control by Noise Interactions
I/O arrays always estimate the CxN Interactions with the highest precision (lowest variance).
Sometimes the I/O array design is larger than it needs to be to get the same resolution
However, if we are interested in estimating CxN interactions, then an I/O array design can be a very good design.

## Slide 37: Confounding in I/O Arrays
Same as in standard arrays
  Write down identity relationships from generators
  Multiply out all possible combinations to get defining relation
  Multiply defining relation by any effect to get alias structure
  Equivalently we could get the individual defining relations and multiply every possible pair of terms
Resolution of a crossed array experiment is the minimum of the resolutions of the individual arrays
  RC = Resolution of Control Array
  RN = Resolution of Noise Array

## Slide 38: Defining Relation I=ABC=PQR=ABCPQR
Notice that as long as each individual array is Resolution III the shortest word containing both control and noise factors will have length 6.

## Slide 39: Confounding Pattern
A=BC=APQR=BCPQR
B=AC=BPQR=ACPQR
C=AB=CPQR=ABPQR
P=ABCP=QR=ABCQR
Q=ABCQ=PR=ABCPR
R=ABCR=PQ=ABCPQ
AP=BCP=AQR=BCQR
AQ=BCQ=APR=BCPR
AR=BCR=APQ=BCPQ
BP=ACP=BQR=ACQR
BQ=ACQ=BPR=ACPR
BR=ACR=BPQ=ACPQ
CP=ABP=CQR=BCQR
CQ=ABQ=CPR=ABPR
CR=ABR=CPQ=ABPQ

## Slide 40: Control by Noise Factor Interactions will be confounded with interactions of order Min(RC, RN). So, if both arrays have Resolution III then CxN interactions will be confounded with three factor interactions.

## Slide 41: Summary
I/O arrays are always good for studying CxN interactions
I/O arrays are often but not always run as split plot experiments
Split plot is determined by how you run the experiment not how you design it.
You must know how the experiment was run in order to analyze it with the correct error structure

## Slide 42: My Recommendations
Think about the idea of robustness in the planning stage of your experiment and choose the response accordingly.
If you choose to reduce variance, then make sure that the variance that you are reducing is the variance that you want to reduce and that it is worth the experimental effort.
Analyze the mean and variance separately and make decisions concerning the tradeoffs between reducing variance and achieving the desired mean value.
Use Inner and Outer Arrays to estimate Control by Noise Interactions for designing Robust Products and Processes.

## Slide 43: Assembled Designs
Parameters:
r = # of Design Points
n = # of observations per Treatment Combination (assume constant)
s = # of different structures used in the design
BT = total number of Batches
x1
x3
x2
1
2
3
4
5
6
7
8
A class of experimental design for estimating location effects,
dispersion effects, and variance components.
“Works for anything that involves making batches and taking observations”
r = 8
n = 4
s = 2
BT = 20

## Slide 44: Notation for Assembled Designs
Example: 23 design, Splitting Generator = ABC, r=8, s=2, B1=4, B2=3, n=6
Must have design points ordered in some way.