## Slide 1: …We have a large reservoir of engineers (and scientists) with a vast background of engineering know-how. They need to learn statistical methods that can tap into the knowledge. Statistics used as a catalyst to engineering creation will, I believe, always result in the fastest and most economical progress…
George Box, 1992

## Slide 2: Chapter 7 Taguchi Designs

## Slide 3: Genichi Taguchi
An engineer who has developed an approach (Taguchi Methods) involving statistical planned experiments to reduce variation
1950’s: applied his approach in Japan
1980’s: introduced his ideas to US
Many (in Japan and US) consider DEX and Taguchi Methods synonyms…

## Slide 4: What are Taguchi’s Contributions?
Quality Engineering Philosophy
Methodology
Experiment Design
Analysis

## Slide 5: Taguchi focuses mostly on Off-Line Quality Control
Off-Line Quality Control =
Improving Quality and Reducing Total Cost in the Design Stage
Total Cost means cost to society so it includes the cost of
problems in manufacturing and the cost of problems in the
field.

## Slide 6: The Quadratic Loss Function and the Typically Assumed Loss Function
Target
Lo Spec
Hi Spec
Loss

## Slide 7: The Design Process is Divided
System Design
  Choose the sub-systems, mechanisms, form of the prototype.
Parameter Design
  Optimize the design, set up the design so that it improves quality and reduces cost
Tolerance Design
  Study the tradeoffs that must be made and determine what tolerances and grades of materials are necessary

## Slide 8: Taguchi’s Contributions
Quality Engineering Philosophy
Methodology
Experiment Design
Analysis

## Slide 9: Parameter Design (Robust Design)
Optimize the settings of the design to minimize its sensitivity to noise – ROBUSTNESS.
Taguchi really opened a whole area that previously had been talked about only by a few very applied people.
His methodology is heavily dependent on design of experiments, but he wanted to look at not just the mean but also the variance.

## Slide 10: Classification of Factors
Control Factors–Design factors that are to be set at optimal levels to improve quality and reduce sensitivity to noise
  Dimensions of parts, type of material, etc
Noise Factors–Factors that represent the noise that is expected in production or in use
  Dimensional variation
  Operating Temperature
Adjustment Factor – Affects the mean but not the variance of a response
  Deposition time in silicon wafer fabrication
Signal Factors – Set by the user to communicate desires of the user
  Position of the gas pedal

## Slide 11: Taguchi’s Contributions
Quality Engineering Philosophy
Methodology
Experiment Design
Analysis

## Slide 12: Screening Designs Taguchi Designs
C
S
R
O
R
Focus: Many Factors
Output: List of Important Factors, Best Settings, Good Model

## Slide 13: Alternative Notation
X1 X2 X3
X1 X2 X3

## Slide 14: L8 array

## Slide 15: Linear Graphs for L8 Array
1
2
3
4
5
6
7
1
2
3
4
5
6
7
Main effects are assigned to columns at nodes in the plot.
Interactions are assigned to the columns on the lines.

## Slide 16: Orthogonal Designs
“Classical”
(2-level Factorials)
“Taguchi”
23
24
25
26-3
27-1
…
23-1=L4
27-4=L8
215-11=L16
…
L12
L18
L27
…

## Slide 17: Montgomery (1997), Design and Analysis of Experiments, P. 631

## Slide 18: Taguchi Designs Notation
Total Number of Runs
Number of Levels per Factor
Number of Factors

## Slide 19: Taguchi Orthogonal Array Tables
2-level (fractional factorial) arrays
  L4(23). L8(27), L16(215). L32(231), L64(263)
2-level array
  L12(211) (Plackett-Burman Design)
3-level arrays
  L9(34). L27(313), L81(340)
4-level arrays
  L16(45). L64(421)
5-level array
  L25(56)
Mixed-level arrays
  L18(21x37), L32(21x49), L50(21x511)
  L36(211x312), L36(23x313), L54(21x325)

## Slide 20: Where is a list of Taguchi Designs?
DATAPLOT
  L4.DAT
  L8.DAT
  L9.DAT
  L12.DAT
  L16.DAT
  ETC.
  TAGINDEX.DAT

## Slide 21: Comments on Taguchi Design Selection Method
Assumes most interactions are small and those that aren’t are known ahead of time.
  He claims that it is possible to eliminate these interactions either by correctly specifying the response and design factors or by using a sliding setting approach to those factor levels.
Doesn’t guarantee that we get highest resolution design.
Instead of designing the experiment to investigate potential interactions, Taguchi prefers to use three-level factors to estimate curvature.

## Slide 22: Taguchi’s Contributions
Quality Engineering Philosophy
Methodology
Experiment Design
Analysis

## Slide 23: Analysis
Taguchi uses signal to noise ratios as response variables.
  e.g.,
It is often more informative to analyze mean and standard deviation separately (sd), rather than combine into a signal to noise ratio
  analyze sd in the same manner that we have previously analyzed the mean.
Taguchi analysis techniques are often inefficient…

## Slide 24: We should support Taguchi’s philosophy of quality engineering. However, we must rely on simpler, more efficient methods that are easier to learn and apply to carry this philosophy into practice… You can use the techniques presented thus far in class to analyze Taguchi Designs.

## Slide 25: More Screening Designs...
(See Pink Hand-Out)
Wu and Hamada (2000), Experiments,
Appendices 6C, 6D, 7A, and 7C